## Slide 1: CAS 2017 Vacuum simulations
Individual work – Tutorial Group #1
15 June 2017 – Glumslov - Sweden

## Slide 2: Outline
Problem description
Molflow in a nutshell
Geometrical model
Results
  Sticking factor & outgassing rate
  Saturation time - analytical versus Monte Carlo approaches
  Transmission probability and pressure ratio as a function of sticking probability
Reference paper
Conclusions

## Slide 3: Problem description
We have a NEG coated vacuum pipe connected to a vacuum system and two pressure gauges reading. A gas injection is performed and at steady state, the pressures measured in gauges 1 and 2 are:
What is the sticking factor of the NEG?
What is the flow rate of the inlet gas?
P2
P1

## Slide 4: Problem description
What do we know:
Pipe geometry
Pumping speed of the pump
Pressure on gauges
S = 300 l/s
Gauge 1
Gauge 2

## Slide 5: Problem description
Principle:
Mass flow flowing through
a coated chamber
Some molecules sticking
to the coating
Some molecules pumped

## Slide 6: Molflow in a nutshell
MolFlow+ is a software developed at CERN in 1990 based on Monte Carlo method
The software allows to:
Draw a vacuum system
Calculate pressure profiles for complex geometries in molecular flow regime
In our case, evaluate the sticking probability α of NEG coating
All the results can be visualized in a user friendly way and shown in a real time

## Slide 7: Building the geometry
Gauge
2
Gauge
1
Coated sample
1000 mm
63 mm
~150 mm
~150 mm
Q
S = 300 l/s

## Slide 8: Building the geometry

## Slide 9: Question 1: sticking probability and injection rate
Work out pressure ratio of two gauges
Apply sticking probability to obtain the same pressure ratio in Molflow
– 0.052
Set the gas injection rate in the simulation to get the same pressures as given above
– 0.0001 mbar*l/s

## Slide 10: The complete system
P1 = 1e-6 mbar
P2 = 2.5e-9 mbar
S = 300 l/s
Q = 1e-4 mbar*l/s
NEG coating
Sticking factor 0.052

## Slide 11: Question 2
NEG coating is an effective pump, but it can’t pump gas forever: eventually it saturates. Its pumping ability drops quickly when the pumped gas forms one monolayer on the surface – corresponding to about 1E15 pumped molecules/cm2
In our setup, how much gas is that?
How much time does it take until our setup saturates?

## Slide 12: Question 2: time for complete saturation - analytical way
How much time does it take until our setup saturates?
p1=1*10-6 mbar
p2=2.5*10-7 mbar
S=300l/s
Aneg=1971.1cm2
Qs=10-4 mbar*l/s
Nsat=1015 molecules/cm2

## Slide 13: Question 2: time for complete saturation - analytical way
As first we calculate the gas load Q2 after the NEG chamber:
To get the gas load absorbed by NEG coating we just subtract it from the total inlet gas:
By dividing with the total surface area of NEG chamber we get the absorption rate of coating:

## Slide 14: Question 2: time for complete saturation - analytical way
With the ideal gas equation we get number of molecules absorbed by NEG surface area in a second:
With division of number of absorbed molecules with total number of molecules needed to saturate the film we gate the time before pumping speed of NEG drops to zero:
In our setup, how much gas is that?
13.77 min

## Slide 15: Question 2- time for complete saturation in Molflow
Engineering way: Using Molflow+ to solve the problem
1) Select a facet of the NEG area and read impingement rate : 2.4 x1017 molecules*m-2*s-1 = 2.4 x1013 molecules*cm-2*s-1
2) The impingement rate times the sticking factor of the NEG of 0.05 gives us the number of absorbed particles per area Nabs = 1.2x1012 molecules*cm-2*s-1
3) We know that NEG coating is saturated at Nsat =1015 molecules*cm-2
4) The full saturation is reached at t=Nsat/NAbs
t=1015 molecules*cm-2/2.4 x1013 molecules*cm-2*s-1= 833 s
13.88 min

## Slide 16: Question 3
What was the transmission ratio of the gas for the pressure ratio given in the task?
By changing the simulation parameters, make a “transmission ratio as a function of the sample’s sticking factor” plot given that:
  X axis: different sticking factor values (around 5-7 different values)
  Y axis: gas transmission ratio

## Slide 17: Question 3: trans. probability and pressure ratio as a function of α
5.E-2

## Slide 18: Real life applications
Ref.: CERN, building 101

## Slide 19: Reference paper

## Slide 20: Conclusions
Tutorial based on a real world application
The same problem was addressed analytically and numerically
With the basic knowledge of vacuum technology, Molflow becomes a very powerful tool

## Slide 21: Final conclusion Hard work & Ice cream