## Slide 1: Technology of superfluid helium
Philippe Lebrun & Laurent Tavian
CERN, Geneva, Switzerland
CERN Accelerator School «Superconductivity for Accelerators»
Ettore Majorana Foundation and Centre for Scientific Culture
Erice, Italy, 24 April – 4 May 2013

## Slide 2: Contents
Introduction to superfluid helium
Superfluid helium as a technical coolant
Practical cooling schemes
Refrigeration below 2 K
Specific technology for He II systems
Applications

## Slide 3: Contents
Introduction to superfluid helium
Superfluid helium as a technical coolant
Practical cooling schemes
Refrigeration below 2 K
Specific technology for He II systems
Applications

## Slide 4: First liquefaction of helium (1908)
Leiden « cascade » to produce liquid hydrogen
Helium liquefaction stage precooled by liquid hydrogen

## Slide 6: Unsuccessful attempt to solidify helium

## Slide 7: Hint of a quantum effect…?

## Slide 8: Zero-point (quantum) energy prevents helium from solidifying
F. London

## Slide 9: Discovery of He II phase transition (1928) Helium phase diagram (1933)
W.H. Keesom

## Slide 10: Phase diagram of helium
l line

## Slide 11: Discovery of superfluidity in He II (1938)
J.F. Allen & A.D. Misener (Cambridge)
P.L. Kapitsa (Moscow)
Vaporization of liquid helium under applied heat load
He I (T=2.4 K)
He II (T=2.1 K)

## Slide 12: Theoretical approaches to superfluid helium
Fritz London
Laszlo Tisza
Lev Davidovich Landau
Bose-Einstein condensation
Two-fluid model
Quasi-particle description

## Slide 13: Bose-Einstein condensation in gas of particles

## Slide 14: Two-fluid model of He II
Phenomenological model
Two interpenetrating fluids
= rs + rn
Normal & superfluid fractions varying with T
v = rs vs + rn vn
s = rn sn since ss = 0
All entropy carried by normal component
Physical basis of the two-fluid model
  Collective excitations constitute the normal component (Landau)
  B-E condensate in liquid (Penrose & Onsager)

## Slide 15: He II behaviour explained by two-fluid model
Frictionless flow through small channels
  Film flow
  Andronikashvilii experiment
Thermal transport by counterflow
  Laminar
  Turbulent
Thermomechanical effect
Second sound

## Slide 16: Contents
Introduction to superfluid helium
Superfluid helium as a technical coolant
Practical cooling schemes
Refrigeration below 2 K
Specific technology for He II systems
Applications

## Slide 17: Benefits of He II cooling
Lower the operating temperature
  Achieve higher magnetic field through increase of critical current density of superconductor
  Minimize overall energy dissipation in RF cavities
Enhance heat transfer
  At solid-liquid interface  conductor cooling
  In the bulk liquid
   device/system cooling scheme
   calorimetry in isothermal bath

## Slide 18: Critical current density of superconductors for high-field magnets

## Slide 19: Optimization of operating temperature for superconducting RF cavities
BCS theory RBCS = (A w2 /T) exp (-B Tc/T)
For practical materials RS = RBCS + R0
Refrigeration (Carnot) Pa = P (Ta/T - 1)
 depending upon w and R0, optimum operating temperature for superconducting cavities
Niobium

## Slide 20: Enhancement of heat transfer
Low viscosity  permeation
Very high specific heat  stabilization
  105 times that of the conductor per unit mass
  2 x 103 times that of the conductor per unit volume
Very high thermal conductivity  heat transport
  103 times that of cryogenic-grade OFHC copper
  peaking at 1.9 K
Full benefit of these transport properties can only be reaped by appropriate design providing good wetting of the superconductors and percolation paths in the insulation, often in conflict with other technical requirements

## Slide 21: Specific heat of liquid helium and copper

## Slide 22: Equivalent thermal conductivity of He II p
Copper OFHC
Helium II

## Slide 23: Solid-liquid interface: Kapitza conductance
Experimental data for Copper (S. Van Sciver, "Helium Cryogenics")
hK ~ T 3
Valid for small heat flux (when DT<<T)

## Slide 24: Application of high thermal conductivity Calorimetry in isothermal He II bath
For slow thermal transients, the He II bath is quasi-isothermal: a single temperature measurement allows to estimate heat deposition/generation Q'
- at constant P Q' = Mbath dH/dt|1
- at constant V Q' = Mbath dE/dt|1
Mbath can be estimated by in situ calibration, using applied heating power W'
- at constant P W' = Mbath dH/dt|2
- at constant V W' = Mbath dE/dt|2
T
Q'
W'

## Slide 25: Calorimetry of magnet quench in He II bath
Time evolution of bath temperature
Correlation with electrical measurements

## Slide 26: Precision thermometry allows calorimetric detection of faulty joints in LHC at safe powering level
Current | Total (measured) |  | Nominal Splices* | Add. local dissipation | Uncertainty
[A] | [mW/m] | [W] | [W] | [W] | [W]
3000 | 4.4 | 1.0 | 0.4 | 0.6 | 0.6
5000 | 14.9 | 3.2 | 1.1 | 2.1 | 0.6
7000 | 32.2 | 6.9 | 2.1 | 4.8 | 0.6
Local resistance: ~90 nW, confirmed by electrical measurement

## Slide 27: Pressurized vs saturated He II

## Slide 28: Advantages & drawbacks of He II p
Advantages
  limits the risk of air inleaks and contamination in large and complex cryogenic systems
  for electrical devices, limits the risk of electrical breakdown at fairly low voltage due to the bad dielectric characteristics of helium vapour (Paschen curve)
  better stabilizer for heat buffering
Drawbacks
  one more level of heat transfer
  additional process equipment (pressurized-to-saturated helium II heat exchanger)

## Slide 29: Paschen curve for gaseous He at 20 °C
e.g., 1.6 kPa pressure and 6 mm gap

## Slide 30: Thermal stabilisation in He II s
The corresponding DH is 9 mJ/cm3

## Slide 31: Thermal stabilisation in He II p
The corresponding DH is 280 mJ/cm3
(30 times higher than in He II s)

## Slide 32: Contents
Introduction to superfluid helium
Superfluid helium as a technical coolant
Practical cooling schemes
Refrigeration below 2 K
Specific technology for He II systems
Applications

## Slide 33: Working with superfluid helium at atmospheric pressure
He I
He II
Tl
Tl-e
Refri
« Roubeau bath »: He II conduction prevents from lowering the bath temperature well below Tl
P atm
4.2 K
He I
He II
Tl
Tl-e
T<<Tl
Refri
« Claudet bath »: restriction in cryostat allows subooling He II bath to temperatures well below Tl
P atm
4.2 K

## Slide 34: A practical Claudet bath

## Slide 35: Conduction cooling in static He II p
Cross-section: A
Length: L
Power:
Heat Flux:
Gorter-Mellink law:
Experimental work of Bon Mardion, Claudet & Seyfert:
    m ≈ 3.4
    tabulation of X(T)
Note 1: this is a non-linear formula for conduction  use proper units!
Note 2: m = 1 for classical solid conduction (Fourier’s law)

## Slide 36: Thermal conduction integral function of He II p

## Slide 37: Conduction cooling: a numerical example
A = 1 cm2
L = 1 m = 100 cm (Units!)
T1 = 1.9 K  X(T1) = 200
T2 = 1.8 K  X(T2) = 360
Then: q3.4.L = 360 - 200  q3.4 = 1.6  q = 1.15 W/cm2
.
.
.
Comparison with "good solid conductor", e.g. Copper
with k = thermal conductivity at 1.8 K
Cu type | k [W/m.K] | DT [K] | L [m] | q [mW/cm2]
OFHC | 120 | 0.1 | 1 | 1.2
DHP | 3 | 0.1 | 1 | 0.03
He II conducts heat 1000 times better than OFHC Cu

## Slide 38: Steady-state conduction duct in He II
From 1.80 K to 1.90 K

## Slide 39: Tore Supra tokamak at CEA Cadarache, France

## Slide 40: He II p conduction cooling of Tore Supra coils

## Slide 41: He IIp conduction cooling of 45 T hybrid magnet NHFML Tallahassee

## Slide 42: Heat transfer across electrical insulation of LHC superconducting cable
Conduction in polyimide

## Slide 43: The LHC: 1716 superconducting magnets cooled at 1.9 K in 3 km long strings: how to transport the heat over such distances?

## Slide 44: Conduction cooling of accelerator string: the fin problem
Distance : z
Linear heat load: x
G-M law applied on dz:
Energy conservation:

then,

Calling Qtot the total heat load on the string of length L:
Hence,

## Slide 45: Conduction in He II with linear applied heat load
From 1.80 K to 1.90 K

## Slide 46: Cooling the LHC magnet strings by two-phase flow of He II s
Fixed temperature
Small flow, no pump
Monophase
Excellent thermal conductivity
Good dielectric strength

## Slide 47: Two-phase Flow of Saturated He II (Mandhane, Gregory & Aziz flow map)

## Slide 48: Investigation of two-phase He II s flow (CEA Grenoble, France)
LHC nominal operation
Phenomenology
Stability
Pressure drop
Heat transfer at wall

## Slide 49: LHC magnet cross-section

## Slide 50
Temperature profile of LHC sector
3.3 km

## Slide 51: Contents
Introduction to superfluid helium
Superfluid helium as a technical coolant
Practical cooling schemes
Refrigeration below 2 K
Specific technology for He II systems
Applications

## Slide 52: Challenges of power refrigeration at 1.8 K
Compression > 80
Compression of large mass flow-rate of He vapor across high pressure ratio
intake He at maximum density, i.e. cold
Need contact-less, vane-less machine  hydrodynamic compressor
Compression heat rejected at low temperature  thermodynamic efficiency

## Slide 53: Warm pumping unit for LHC magnet tests 3 stages of Roots + 1 stage rotary-vane pumps 6 g/s @ 10 mbar (1/160 of LHC!)

## Slide 54
Operating ranges of volumetric & hydrodynamic compressors
Pressure
ratio
Flow
N1
N2
N3
Pressure
ratio
Flow
N1
N2
N3
Stall line
Choke line
Volumetric (ideal)
Hydrodynamic
Speed N1 < N2 < N3
Speed limit

## Slide 55: Cycles for refrigeration below 2 K
“Integral Cold”
Compression
“Mixed”
Compression
“Warm”
Compression
Sub-cooling
heat exchanger
~ 2 kPa

## Slide 56
Flow compliance of “mixed” compression
N2
N3
Stall line
Choke line
Volumetric
P inter
Flow
P out (fixed)
P inter
P in (fixed)
Hydrodynamic
Volumetric
For fixed overall inlet & outlet conditions, coupling of the two machines
via P inter maintains the operating point in the allowed range
N1
Flow (variable)

## Slide 57: Simplified flow-schemes of the 1.8 K refrigeration units of LHC

## Slide 58: Cold hydrodynamic helium compressors
Air Liquide
IHI

## Slide 59: Specific features of LHC cold compressors
Axial-centrifugal
Impeller (3D)
Fixed-vane
diffuser
3-phase induction
Electrical motor
(rotational speed:
200 to 700 Hz)
Active
magnetic
bearings
300 K under
atmosphere
Cold under
vacuum
Inlet
Outlet
Pressure ratio
2 to 3.5
Spiral volute

## Slide 60: Performance of LHC cold compressors

## Slide 61: Warm subatmospheric screw compressors
125 g/s @ 0.6 bar
or
4600 m3/h @ 15 °C
Mycom
Kaeser
125 g/s @ 0.35 bar
or
2 x 3900 m3/h @ 15 °C

## Slide 62
Isothermal efficiency of warm subatmospheric compressors
Isothermal
efficiency

## Slide 63: C.O.P. of LHC 1.8 K units
0
200
400
600
800
1000
Air Liquide
IHI-Linde
COP [W@RT / W@1.8K]
4.5 K refrigerator part
1.8 K refrigeration unit part
Carnot Limit

## Slide 64: Contents
Introduction to superfluid helium
Superfluid helium as a technical coolant
Practical cooling schemes
Refrigeration below 2 K
Specific technology for He II systems
Applications

## Slide 65: Efficiency of Joule-Thomson expansion
Sub-cooling | T1’ [K] | H3-H2 [J/g] | H3-H0 [J/g] | [%]
without | 4.5 | 12.6 | 23.4 | 54
with | 2.2 | 20.4 | 23.4 | 87
Sub-cooling efficiency :
Enthalpy of pure liquid

## Slide 66: Subcooling before J-T expansion
1
2
2
1’
3
0

## Slide 67: Prototypes of subcooling HX for LHC
Stainless Steel Plate
Perforated
Copper Plates
with SS Spacers
SS Coiled Tubes
Mass-flow: 4.5 g/s
DP VLP stream: < 1 mbar
Sub-cooling T: < 2.2 K
DATE
SNLS
Romabau

## Slide 68: Protection against air inleaks
Motor shaft of warm sub-atmospheric compressors placed at the discharge side to work above atmospheric pressure.
For sub-atmospheric circuits which are not under guard vacuum or not completely welded, apply helium guard protection on dynamic seal of valves, on instrumentation ports, on safety relief valves and on critical static seals

## Slide 69: Contents
Introduction to superfluid helium
Superfluid helium as a technical coolant
Practical cooling schemes
Refrigeration below 2 K
Specific technology for He II systems
Applications

## Slide 70: High-field magnets for high-frequency NMR 900 MHz  21.2 T

## Slide 71: The European X-ray FEL, DESY, Hamburg (Germany)
Very brilliant, ultra-short (100 fs) pulses of X-rays down to 0.1 nm
Based on s.c. e linac
Beam energy 17.5 GeV
Beam power 600 kW
Linac length 1.7 km
928 superconducting RF cavities operated at 2 K
Refrigeration 2.5 kW @ 2 K

## Slide 72: European Spallation Source, Lund (Sweden)
  5 MW long pulse source
    ≤2 ms pulses
    ≤20 Hz
    Protons (H+)
    Low losses
    High reliability, >95%
    2.5 GeV

## Slide 73: International Linear Collider (ILC)
e+ e- linear collider
Collision energy 500 GeV c.m. initially, later upgrade to ~1 TeV c.m.
Overall length 31 km
Key technology: SC RF cavities
Global Design Effort
No central laboratory
World-wide collaboration
Site-specific studies conducted on sample sites

## Slide 74: Conclusion
From a laboratory curiosity and a hot research topic in condensed-matter physics, superfluid helium has become a state-of-the-art cryogen for cooling large superconducting devices such as high-energy accelerators, tokamaks and research magnets
Projects such as TORE SUPRA, CEBAF, SNS and LHC have triggered vigorous development programmes in laboratories and industry concerning flow and heat transfer, refrigeration techniques, instrumentation and engineering
Superfluid helium remains an enabling technology for NMR magnets and future large projects using high-field superconducting devices, e.g. the European X-FEL, ESS, ILC. The unique hydrodynamic properties of the fluid can also be used per se, e.g. in turbulence research

## Slide 75: Application range of low-pressure He compressors
~ 20 000 m3/h @ 15 °C