## Slide 1
Modeling & Simulations - Part 2
Advanced numerical methods for plasma acceleration
Jean-Luc Vay
Lawrence
Berkeley
National
Laboratory
High Gradient Wakefield Accelerator
11-22 March 2019 – Sesimbra, Portugal
The
CERN
Accelerator
School

## Slide 2: Outline
Challenge: range of space & time scales
Quasistatic approximation
Boosted frame approach
High-order & spectral Maxwell solvers
Mitigation of numerical Cherenkov
Mesh refinement
Conclusion

## Slide 3: Can plasma-based accelerators lead to compact, cheaper colliders?
Tens-to-thousands of plasma accelerator stages
needed for a 1-to-30 TeV e--e+ collider.
Current state-of-the-art in experiments & modeling is 1 stage.
Success depends critically on progress in technology & modeling.
Laser-driven collider concept
Particle beam-driven collider concept

## Slide 4: Plasma accelerators are challenging to model
Short driver+wake propagates through long plasma
 Many time steps.
E.g., for a 10 GeV LPA scale stage:
~1mm wavelength laser propagates into ~1m plasma  millions of time steps needed (even with moving window)
Simulations (in 2D) can take days for 1 stage (at insufficient resolution for collider beam quality).
For multi-TeV collider, need for ×10s-1000s stages ×10s-1000s (high res. 3D) ×10s (ensembles)!
Need for advanced in algorithms, reduced models, supercomputing!
Very small features:  Many grid cells.
wake
driver
plasma

## Slide 5: Outline
Challenge: range of space & time scales
Quasistatic approximation
Boosted frame approach
High-order & spectral Maxwell solvers
Mitigation of numerical Cherenkov
Mesh refinement
Conclusion

## Slide 6: Quasistatic approximation uses separation of scales
Driver and accelerated beams:
Very stiff  long space & time scales
Plasma electrons and protons:
Very mobile  short space & time scales
 treat beams and plasmas separately*.
*P. Sprangle, E. Esarey and A. Ting, Phys. Rev. Lett. 64, 2011 (1990)

## Slide 7: Quasistatic approximation uses separation of scales
2-D slice of plasma (fast)
3-D e-beam + driver
(slow: frozen during interaction)
Fast time scale - 2-D slice of plasma is stepped “backward” (with small steps) through the beam field and its self-field (solving iteratively 2-D Poisson-like equations at each step).

## Slide 8: Quasistatic approximation uses separation of scales
2-D slab of plasma (fast)
3-D e-beam + driver + wake
(slow: frozen during interaction)
Fast time scale - 2-D slice of plasma is stepped “backward” (with small steps) through the beam field and its self-field (solving iteratively 2-D Poisson-like equations at each step).

## Slide 9: Quasistatic approximation uses separation of scales
2-D slab of plasma (fast)
3-D e-beam + driver + wake
(slow: frozen during interaction)
Fast time scale - 2-D slice of plasma is stepped “backward” (with small steps) through the beam field and its self-field (solving iteratively 2-D Poisson-like equations at each step).

## Slide 10: Quasistatic approximation uses separation of scales
Fast time scale - 2-D slice of plasma is stepped “backward” (with small steps) through the beam field and its self-field (solving iteratively 2-D Poisson-like equations at each step).
Slow time scale - 3-D beam is pushed far down the plasma with large time steps.
2-D slab of plasma (fast)
3-D e-beam + driver + wake
(slow: frozen during interaction)
repeat

## Slide 11: Outline
Challenge: range of space & time scales
Quasistatic approximation
Boosted frame approach
High-order & spectral Maxwell solvers
Mitigation of numerical Cherenkov
Mesh refinement
Conclusion

## Slide 12: Space & time scales can also be bridged with full PIC
Use Lorentz boosted frame instead of Lab frame*
# time steps a L/l
l
L
Lorentz
Transform
g
l’=lg(1+b)
L’=L/g
# time steps a L’/l’
*J.-L. Vay, Phys. Rev. Lett. 98, 130405 (2007).
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 13: Space & time scales can also be bridged with full PIC
plasma
Lorentz
Transform
g
l’=lg(1+b)
L’=L/g
Speedup = (L’/l’)/(L/ l) = g2(1+b) For g=100, speedup > 10,000!
# time steps a L/l
l
L
# time steps a L’/l’
Price to pay:
Physics looks different in boosted frame and lab frame  need to transform between boost & lab frame.
Potential numerical instabilities (numerical Cherenkov)  solve Maxwell in Galilean frame (see below).
wake
driver
plasma
wake
driver
Lab frame
Lorentz boosted frame
Use Lorentz boosted frame instead of Lab frame*
*J.-L. Vay, Phys. Rev. Lett. 98, 130405 (2007).
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 14: Care needed to ensure frame-independent initial conditions
-vboost
z’,t’=LT(z,t)
frozen
active
-vboost
Initial conditions known in lab frame:
  Lorentz transform to boosted frame.
  Perform injection of particle & laser beams through a moving plane.
Also need to reconstruction output data in lab frame.

## Slide 15
Time
Time
Laser field on axis
Laser field on axis
Lab frame
Wake frame
Hyperbolic rotation from Lorentz Transformation converts laser…
…spatial oscillations into
time beating
(Laser injected at entrance of plasma)

## Slide 16: Outline
Challenge: range of space & time scales
Quasistatic approximation
Boosted frame approach
High-order & spectral Maxwell solvers
Mitigation of numerical Cherenkov
Mesh refinement
Conclusion

## Slide 17: High-order/spectral solvers are useful for various reasons
Electron bunch travel faster than EM waves in simulation
 emits unphysical NCR
 can degrade beam.
Courtesy Rémi Lehe
Reduce numerical dispersion effects
Remove numerical Cherenkov (NC) effects
Radiation (NCR)
Instability (NCI)
Plasma travels near speed-of-light in boosted frame
 couples with slower EM waves
and aliases
 instability.
Longitudinal electric field
laser
plasma

## Slide 18
Non-Standard FD solvers offer some tunability
1J. B. Cole, IEEE Trans. Microw. Theory Tech. 45 (1997).
2M. Karkkainen et al., Proc. ICAP, Chamonix, France (2006).
3A. Pukhov, J. Plasma Physics 61 (1999) 425.
NS-FDTD (Karkkainen/Lehe)
No dispersion along axes
cDt/Dx=1
FDTD (Yee)
cDt/Dx~0.7
No dispersion along diag.
NSFD1,2: weighted average of quantities transverse to FD
Adaptations to PIC3,4,5
a
b
b
b
b
g
g
g
g
-a
-b
-b
-b
-b
-g
-g
-g
-g
Dx
Lehe6 algorithm:
4J.-L. Vay et al, J. Comput. Phys. 230 (2011) 5908.
5B. Cowan et al, PRST-AB 16 (2013) 041303.
6R. Lehe et al, PRST-AB 16 (2013) 021301.
kDx
wDx/c
kDx
wDx/c
18

## Slide 19
cDt/Dx~0.45
Higher order
Kronecker d pulse
cDt/Dx~0.045
Accurate but Expensive
(with leapfrog integrator)
Arbitrary-order Maxwell solver offers higher flexibility in accuracy
smaller time steps
19
Numerical dispersion becomes
superluminous
Isotropic

## Slide 20
F-1
F
F-1
F
FDTD cDt/Dx~0.45
PSTD cDt/Dx~0.045
Finite-Difference Time-Domain
(FDTD)
Pseudo-Spectral Time-Domain
(PSTD)
PSTD is limit of high-order FDTD when ninfinity.
PSTD cDt/Dx~0.45
PSTD converges to exact solution (on grid) for Dt0.
F=FFT
Pseudo-spectral solvers offer infinite order spatial derivatives
20

## Slide 21
Pseudo-Spectral Analytical Time-Domain1 (PSATD)
1I. Haber,R. Lee,H. Klein & J. Boris,Proc. Sixth Conf. on Num. Sim. Plasma, Berkeley, CA, 46-48 (1973)
PSATD cDt/Dx=50
1 time step
F-1
F
F-1
F
with
F-1
F
Easy to implement arbitrary-order n with PSATD (k=k⚯  kn).
Analytical time integration in Fourier space offers exact solution
21

## Slide 22: Outline
Challenge: range of space & time scales
Quasistatic approximation
Boosted frame approach
High-order & spectral Maxwell solvers
Mitigation of numerical Cherenkov
Mesh refinement
Conclusion

## Slide 23
PSATD can also apply to time integration in Galilean frame
Original idea by Manuel Kirchen (PhD student at U. Hamburg) Concept and applications: Kirchen et al., Phys. Plasmas 23, 100704 (2016)
Use Galilean coordinates that follow the relativistic plasma.
+ integrate analytically, assuming
is constant over one timestep.
Derivation of the algorithm: Lehe et al., Phys. Rev. E 94, 053305 (2016)
Standard PSATD PIC
Galilean PSATD PIC
23

## Slide 24
Galilean PSATD is stable for uniform relativistic flow
  Analysis
  Simulation
Uniform plasma streaming in 2D periodic box
Standard PSATD
Galilean PSATD
  Instability growth rate
Lehe et al., Phys. Rev. E 94, 053305 (2016)
24

## Slide 25
And is also the most stable for plasma acceleration simulations
25

## Slide 26: Outline
Challenge: range of space & time scales
Quasistatic approximation
Boosted frame approach
High-order & spectral Maxwell solvers
Mitigation of numerical Cherenkov
Mesh refinement
Conclusion

## Slide 27: Mesh refinement enables “zooming” on regions of interest
e.g. around small features and/or sharp gradients
But mesh refinement (MR) requires special care with PIC, especially EM-PIC!

## Slide 28
Mesh refinement implies:
 jump of resolution at coarse-fine interface,
 some procedure for coupling the solutions at the interface.
Consequences:
- loss of symmetry: self-force,
- loss of conservation laws,
- EM: waves reflection.
Issues arising with mesh refinement and PIC

## Slide 29
Poisson eq.: boundary value problem.
 can use following simple procedure:
  solve on coarse grid,
  interpolate on fine grid boundaries,
  solve on fine grid.
Ln
Ln+1
Refinement levels
Mesh refinement with electrostatic PIC
29

## Slide 30
Ln
Ln+1
Refinement levels
Poisson eq.: boundary value problem.
 can use following simple procedure:
  solve on coarse grid,
  interpolate on fine grid boundaries,
  solve on fine grid.
Mesh refinement with electrostatic PIC
30

## Slide 31
Ln
Ln+1
Refinement levels
Poisson eq.: boundary value problem.
 can use following simple procedure:
  solve on coarse grid,
  interpolate on fine grid boundaries,
  solve on fine grid.
Mesh refinement with electrostatic PIC
31

## Slide 32
Ln
Ln+1
Refinement levels
Poisson eq.: boundary value problem.
 can use following simple procedure:
  solve on coarse grid,
  interpolate on fine grid boundaries,
  solve on fine grid.
Mesh refinement with electrostatic PIC
Simple but problem of spurious “self-force arises near fine-to-coarse boundary.
32

## Slide 33
One charged macroparticle in a box with metallic BC
centered
not centered
Illustration of spurious “self-force” issue with one particle
33

## Slide 34
The macroparticle is attracted by its image from the closest metallic wall.
Illustration of spurious “self-force” issue with one particle
34

## Slide 35
Specular reflection is applied at the boundary.
Illustration of spurious “self-force” issue with one particle
35

## Slide 36
0
1
0
0
2
0
0
3
0
0
4
0
0
5
0
0
Timestep
0
1
0
2
0
3
0
Position
No refinement
The particle moves
up and down.
Physical solution
Illustration of spurious “self-force” issue with one particle
36

## Slide 37
2
5
2
6
X
Time
0
1
0
0
2
0
0
3
0
0
4
0
0
5
0
0
Timestep
0
1
0
2
0
3
0
Position
No refinement
MR patch
Now add a refinement patch.
MR quad. interp.
MR linear interp.
 Particle is trapped in patch by “spurious self-force”
Illustration of spurious “self-force” issue with one particle
37

## Slide 38
Spurious self-force decreases rapidly
in patch
Log(e) [a.u.]
-1
-2
-3
-4
-5
-6
y
x
e
Map of spurious self-force as a function of particle position in refinement patch
Mesh refinement field
Physical field
32x32 refinement patch
Magnitude of “self-force” decreases fast with distance
38

## Slide 39
1 – solve on coarse grid,
2 – interpolate on fine grid boundaries,
3 – solve on fine grid,
4 – disregard fine grid solution close to edge when gathering force onto particles.
Thickness of buffer region provides user control of relative magnitude of spurious force.
Add buffer region surrounding refined area
Ln
Ln+1
Buffer region
(Solve field in buffer but gather force from underlying coarse parent grid)
Enabling a simple mitigation strategy
39

## Slide 40
Example with 2 and 4 guard cells buffer region
0
1
0
0
2
0
0
3
0
0
4
0
0
5
0
0
Timestep
0
1
0
2
0
3
0
Position
No refinement
MR no buffer
MR patch
Illustration of mitigation with one particle test
No buffer:
Particle trapped in patch.
40

## Slide 41
0
1
0
0
2
0
0
3
0
0
4
0
0
5
0
0
Timestep
0
1
0
2
0
3
0
Position
No refinement
MR no buffer
MR patch
MR buffer 2 cells
Example with 2 and 4 guard cells buffer region
With buffer:
no more trapping
Illustration of mitigation with one particle test
41

## Slide 42
0
1
0
0
2
0
0
3
0
0
4
0
0
5
0
0
Timestep
0
1
0
2
0
3
0
Position
No refinement
MR no buffer
MR patch
MR buffer 2 cells
MR buffer 4 cells
Buffer region is very effective.
Example with 2 and 4 guard cells buffer region
With buffer:
no more trapping
4 guard cells better than 2
Illustration of mitigation with one particle test
42

## Slide 43
Consider, e.g., 1d wave equation (natural units)
staggered on a regular space time grid using finite-difference time-domain (FDTD) centered scheme
o o o o o o
o o o o o o
o o o o o o
o o o o o o
o o o o o o
j-2 j-1 j j+1 j+1 x
t
i
i+1
i+2
dx
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
i-2
i-1
o : E
+ : B
dt
Additional problems occur with electromagnetic waves

## Slide 44
o o o o o o o o
o o o o o o o o
o o o o o o o o
o o o o o o o o
o o o o o o o o
j-5 j-4 j-3 j-2 j-1 j j+1 j+2 j+3 x
grid 1
grid 2
t
i
i+1
i+2
dx1
+
+
+
+
+
+
+
+
+
+
+
+
dx2=3dx1
+
+
+
+
+
+
+
+
+
+
+
+
i-2
i-1
o, + : finite-difference at positions ≠j
o : finite-volume (=uncentered FD) at j
Interface
+
+
+
+
or
(method 1)
(method 2)
Assume coupling of two grids using uncentered FD

## Slide 45
o o o o o o o o
o o o o o o o o
o o o o o o o o
o o o o o o o o
o o o o o o o o
j-5 j-4 j-3 j-2 j-1 j j+1 j+2 j+3 x
grid 1
grid 2
t
i
i+1
i+2
dx1
+
+
+
+
+
+
+
+
+
+
+
+
dx2=3dx1
+
+
+
+
+
+
+
+
+
+
+
+
i-2
i-1
o, + : finite-difference at positions ≠j
o : ‘jump’ inside fine grid at j
Interface
+
+
+
+
(method 3)
Or jumping over cells in fine grid to obtain centered FD

## Slide 46
o: E, x:B
+
+
+
+
+
+
l ≤ lNyquist of coarse grid are reflected with amplification of total energy!
Test to measure spurious reflection R at interface at j of signal injected on fine grid.
l
Reflection
Total energy
R
R2+T2
method 1
method 2
method 3
method 1
method 2
method 3
All methods give total reflection of unresolved wavelength

## Slide 47
Termination of patches with Perfectly Matched Layers (PML) to avoid spurious reflections
Buffer zone used for mitigating spurious self-force
Ln
Ln+1
a
f
c
s
a
Main grid: Fn(a)
Inside patch at Ln+1:
Fn+1(a) = I[Fn(s)-Fn+1(c)]+Fn+1(f)
absorbing layer (PML)
a = auxilliary
f = fine
c = coarse
Solution: decouple grids + absorbing layers around patches
47

## Slide 48
Ln
Ln+1
Ln+2
a
f
c
a
f
c
s
s
a
Main grid: Fn(a)
Inside patch at Ln+1:
Fn+1(a) = I[Fn(s)-Fn+1(c)]+Fn+1(f)
Inside patch at Ln+2:
Fn+2(a) = I[Fn+1(s)-Fn+2(c)]+Fn+2(f)
Example with two levels of refinement
absorbing layer (PML)
a = auxilliary
f = fine
c = coarse
Procedure is recursive enabling multiple levels of MR
48

## Slide 49
64x160
128x320
256x640
512x1280
High resolution is needed to capture details.
Ion beam
Plasma
Slab XZ simulations
Example: simulation of wake of non-relativistic ion beam

## Slide 50
512x1280
Mesh ref.
2 levels
fields only
low resolution + MR
2 levels
fields+ particles
3-D
Speedup x10 in 3D (using the same time steps for all refinement levels).
Example: simulation of wake of non-relativistic ion beam

## Slide 51
Simulations with small MR patch recover results using finer grid over the entire box.
Laser driven
Particle beam driven
3-D
Example: simulation of plasma-based accelerator in 3-D

## Slide 52: Movies from 3-D simulations with mesh refinement
Laser driven
Particle beam driven
Witness beam
Driver beam
Movies by Maxence Thevenet
Longitudinal electric fields
Longitudinal electric fields
ne=1019/cc, acceleration~100 MeV
Details of simulations: J.-L. Vay et al, NIM A, in press, Proc. EAAC 2017 https://doi.org/10.1016/j.nima.2018.01.035
Warp-X

## Slide 53
Things look a bit more complicated on another case…

## Slide 54: 2-D fieldmaps from simulation without mesh refinement
No refinement.
Fine resolution everywhere.
Transverse electric field
Longitudinal electric field

## Slide 55: Spurious effect of mesh refinement with FDTD solver
Spurious oscillations:
Same time step used for each grid but Dz is different.
 numerical dispersion is different on coarse and fine grids.
Transverse electric field
Longitudinal electric field

## Slide 56: Subcycling (or spectral solvers) can mitigate effect
Spurious oscillations:
due to numerical dispersion.
Fixes:
Subcycling (push fields and particles on fine grid twice as often as on coarse grid).
Pseudo-spectral Maxwell solver (in development)
Transverse electric field
Longitudinal electric field

## Slide 57: Outline
Challenge: range of space & time scales
Quasistatic approximation
Boosted frame approach
High-order & spectral Maxwell solvers
Mitigation of numerical Cherenkov
Mesh refinement
Conclusion

## Slide 58: Conclusion
Wide range of space & time scales render computer simulations of plasma-based accelerators very challenging.
  The quasistatic approx. & boosted frame full PIC can bridge the range of scales.
For full PIC, high-order pseudo-spectral solvers offer:
  Negligible numerical dispersion.
  No num. Cherenkov inst. via integration in Galilean frame moving with the plasma.
Mesh refinement has potential to offer additional savings:
  Requires special care (spurious effects at transition) and further developments.
Other methods (not discussed) are also used, in addition:
  E.g. RZ solver + azimuthal spectral decomposition, laser envelope, …

## Slide 59: Thank you for your attention. Questions?

## Slide 60: Extras

## Slide 61
For the velocity component, the Boris pusher writes
which decomposes into
one acceleration + one rotation + one acceleration
with
with
Integration of Newton-Lorentz: Leapfrog Boris pusher
Position update
Note time-centering!

## Slide 62
Assuming E and B such that E+v×B=0:
meaning that pusher is consistent with (E+v×B=0) only if E=B=0, and is thus inaccurate for e.g. ultra-relativistic beams.
However Boris pusher fails for ultra-relativistic beams

## Slide 63
Replace Boris velocity pusher
  Velocity push:
with
  Velocity push:
Looks implicit but solvable analytically
with
A Lorentz invariant particle pusher can be constructed

## Slide 64
F=1
F=2
(output in F=1)
Lab frame
particle cycling in constant B field
Boosted frame g=2
ExB drift adds to gyration
X analytic New Boris Boris tan(a/a) cor.
Y analytic New Boris Boris tan(a/a) cor.
X analytic New Boris Boris tan(a/a) cor.
Y analytic New Boris Boris tan(a/a) cor.
Test of Lorentz invariance of particle pusher
Lorentz invariance  better accuracy with ExB drifts.
Many other particle pushers exist (RK, Higuera-Cary, etc.), each with advantages/disadvantages.
Choice depends on physics to be studied.