## Slide 1: Neutrino Factory by Zunbeltz, Davide, Margarita, Wolfgang
IDS proposal

## Slide 2: Neutrino Factory - Our Specs
4 MW beam power
2 - 8 GeV kinetic energy
5 bunches of 3 ns length
50-60 Hz rep rate
Target

## Slide 3: Neutrino Factory: ¿our? Approach
H- Linac
Laser assisted charge- exchange Injection
5 GeV
Accumulator Ring
Compressor Ring
Target
R. Garoby, E. Benedetto, M. Aiba, M. Meddahi
CERN, Geneva, Switzerland

## Slide 4: 5 GeV Linac as Proton Driver
H- 50Hz Penning Source
Chopping at 3MeV
SC only after DTL -> save cost
Step in frequency after DTL -> reduce footprint
5GeV
H- Source
RFQ
Chopper
DTL
LEBT
PIMS (SC)
160MeV
80 MeV
3 MeV
3 MeV
45 keV
LowBeta (SC)
HighBeta (SC)
352 MHz
704 MHz
Linac4/SPL…

## Slide 5: Linac Time Structure
H- Ion Source 50 Hz rep rate
Batch length: 140 ns
(50 linac bunches)
Gaps of 60 ns (chopper)
…
480 µs
20 ms
5 batches / accumulator turn
2400 batches (1014 protons) / pulse
After
Chopper

## Slide 6: H- – Injection
Laser assisted to avoid foil
Transverse painting to reduce SC effects

## Slide 7: Accumulation and Compression
H- Linac
5 GeV
Accumulator Ring
(Circ: ~300 m )
Compressor Ring
Target
Injection into Acc-Ring (480 turns)
Accumulation: transverse x and y phase-space painting
No RF in Accumulator Ring (Isochronous)
Slippage Factor = 0

## Slide 8: Bunch Compression
Required bunch length 3ns
Bunch rotation in two ways
  Fast bunch compression with voltage detuning
  Dephasing of the longitudinal bucket
  Consider ¼ of synchroton period
M. Aiba

## Slide 9: Extraction - Target
Fast extraction
Tungsten rotating wheel target
H- Linac
Charge- Exchange Injection
5 GeV
Acumulator Ring
Compressor Ring
Target

## Slide 10: Conclusion
Linac length/energy
Laser assisted H- stripping to avoid foil damage
Accumulator + Compressor vs All-In-One
longitudinal requirements contradictory
Avoid ramping of circular machines
Use multi turn injection to achieve required bunch current -power

## Slide 11: Green Field
Hot target cooling water flows through a generator providing part of the electricity needed by the accelerator facility

## Slide 12: Green Field
Hot target cooling water flows through a generator providing part of the electricity needed by the accelerator facility
Locate neutrino factory next to nice mountains to provide nice skiing and hiking area for scientists…

## Slide 13: Extra slides

## Slide 14: Linac as proton driver
Parameters:
  Output Energy 5GeV
  70mA peak current
  35 % chopping factor
  2.4% duty cycle -> 480 us pulse length
  Num. particles per bunch 1.14 x10 9
  Num. Bunches per pulse =50