## Slide 1: Radioactive Ion Beams
CW
0.5 MW (for protons)
1 GeV (for protons)
p to U
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao

## Slide 2: Contents
Frag vs ISOL
Overview & Layout
Components:
  Superconducting Drive beam cyclotron (RF,cryo,magnets)
  Target
  Stripping / cooling
  Spectrometer
  RFQ (-> possible exit to low-E experiment)
  Post-acceleration cyclotron
  Instrumentation
Conclusion
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao

## Slide 3: Fragmentation vs ISOL
ISOL
ISOL:
Compact and flexible
Wide variety of users
Possible upgrade for fragmentation machine
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
1

## Slide 4: Beams of Ions from the Gigavolt – Megawatt Advanced Cyclotron
Reduce costs by sharing magnetic field
Superconducting main+trim coils for power saving
RFQ
Stripper
Target
Spectrometer
Proton source
RFQ
Transfer line
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
2

## Slide 5: Beams of Ions from the Gigavolt – Megawatt Advanced Cyclotron (BIGMAC)
Drive beam
Radioactive beam
Stripper
Target
Spectrometer
RFQ
Proton source
Injection (bend or tune energy)
Low energy experiments
High energy experiments
/ fragmentation
RFQ
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
3

## Slide 6: Sector magnets
Based on RIKEN magnets
Adapted for dual beam chamber
Field strength 3T
Extraction radius 1.5m
Magnet radius 3m
Height 6m
Protons to 1 GeV
Radioactive ions to ~100 MeV / u
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
4

## Slide 7: RF resonators
Independent systems for protons and RIs
100 MHz resonators for protons
Tunable 20-50 MHz for RI.
4 cavities for acceleration
1 for flat-topping (increase long. acceptance)
Independent powering (tetrodes)
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
5

## Slide 8: Extraction
Movable stretched-wire septum (up to 150 kV)
Beam channel 15 mm
Off-center injection for Betatron oscillations
Extraction loss 0.01%
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
6

## Slide 9: Target, stripping, separation
TARGET
Rotating target: different target materials, change target in case of damage
Remote handling
Helium gas cooling
STRIPPING
Foil stripper (rotating)
Laser stripping
SEPARATION
Dipole spectrometer
Beam dumps
Slit + collimators
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
7

## Slide 10: Instrumentation
Drive beam:
  Current transformers
  Faraday cups (for commissioning)
  Feschenko monitor
  Beam loss monitors
  Wire scanner (low intensity only)
  Electron jet scanner
Transfer lines: BPMs, BLMs, residual gas ionisation PMT
RI beam: OTR screen (possible pepperpot)
Radiation monitors
e- gun
collector
p+
H0
Scintillator
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
8

## Slide 11: Conclusion
Multipurpose
  Solid state physics & biology
  Medical isotope production
  Nucleosynthesis for astrophysics
Compact
Efficient
Low cost
Chiara, Manuel, Adam, Hui
May 2011, CAS, Bilbao
i’m lovin’ it…
9