## Slide 1: HINOMA injection system for fcc-ee
group 1-CASE STUDY A
Helen Barminova, Irina Avvakumova, Nicholas Evans,
Olaf Dressler, Mariusz Sapinski, Aurelio Berjillos

## Slide 2
After 7 days of work we start seeing light at the end of the tunnel…
…but we remain vigilant, it could still be a train!

## Slide 3
Δp/p <X
Beam lifetime 1h
Dynamic acceptance
15σ
1,5 km Straight section
Beam energy
175 GeV
Circunference= 100Km
Olaf
Mariusz
+
HINOMA??
=
45,6 GeV
Operation mode
Aurelio
Global view
Helen
Irina
Nicholas
Case A: Design a top‐up injection system for an high‐energy circular collider, e.g. FCC--‐ee

## Slide 4: Intensity replenishment for Luminosity stabilization
Instantaneous luminosity: N2(t) / 4πσ2
Let’s assume that = N2(t)= N0exp(-t/τ)
We would like to keep instantaneous luminosity constant to the level:
r=1-L(t0+∆t)/L(t0) = 0.01 (for instance),
where ∆t is top-up injection period.
r=1- exp(-2(t0 +∆t /τ))/exp(-2t0 /τ))=1-exp(-2(∆t /τ))
∆t =-½ τ ln(1-r),example results:
r | ∆t
0.1% | 1.8 s
1% | 18 s
2% | 36 s
5% | 92 s

## Slide 5: Conventional injection
Longitudinal Separation
Transverse Separation
OUR CASE

## Slide 6: Optimum parameters jIn
CONSIDERATIONS
Momentum acceptance: ±2%
Energy spread: 0.14%
Luminosity constant r= 1% , Δt= 18 s
Injection energy= 178.855 GeV
Injected beam charge: 4.81897x1010

## Slide 7: A-2: hardware considerations
Window Frame Ferrite Kicker
Lambertson Septum Magnet

## Slide 8: A-3:Failure scenario
Energy stored in a beam is: 390 kJ in 175 GeV collider case - enough to boil 2-6 eggs
2 MJ in 45.6 GeV collider case - enough to boil 10-30 eggs
(depending how you like your eggs)
However, if you try to boil eggs too fast:
LHC stored beam: 360 MJ/beam
2 MJ – can melt 2.8 kg of copper

## Slide 9
Questions?