## Slide 1: Mechanical & Material Aspects - Tutorial Group 3
Presented by Marco MORRONE

## Slide 2: Project outline
Design the mechanical system of a room temperature [operating] vacuum system for a circular collider with high intensity proton beams.
Inner diameter [circular aperture] = 100mm
Length of vacuum chamber = 10m
Operating temperature = 20°C
Maximum temperature = 230°C
External pressure = atmospheric pressure [1 atm]
Internal pressure = <10-9 mbar
No magnetic field

## Slide 3: Temperature induced Forces
Thermal deformation
Thermal expansion
Thermal stress
Material | Thermal deformation | dl [mm] | Thermal stress [MPa] | sigma y [MPa] | Cost [€/kg]
Copper OF | 0.00357 | 35.7 | 410.55 | 35 | ~25-40
Aluminium | 0.00462 | 46.2 | 355.74 | 393 | ~15
Stainless steel 316 L | 0.00336 | 33.6 | 655.2 | 240 | ~11-32
Titanium Grade 5 | 0.001869 | 18.69 | 214.94 | 880 | ~50
The bellows are needed to allow the thermal expansion and for alignment purposes.

## Slide 4: Structural stability
For the 316 L ss chamber the minimum thickness to avoid the tube to collapse is around 1 mm.
The thickness decided for the chamber is 1.5 mm (only available thickness for d=100 standard tube).
Hoop stress: =3.3 MPa
Longitudinal stress:

## Slide 5: Chamber supports
-2x sliding supports
-1 x fixed support
250 mm
250mm
4750 mm
4750 mm
250 mm
250 mm
1000 mm

## Slide 6: Finite elements modelling
Self-weight deformation
0.47 mm
0.47 mm
Displacement magnification:
x 1100
Weight chamber: 36.2 Kg
2 x Bellow + flanges: 3.2 Kg
TOTAL = 42.6 Kg

## Slide 7: Bellows specification
  Total chamber expansion during bake-out = 33.6 mm
  2x individual bellows chambers to be installed at each end of the chamber
  Using standard industry item
Spec:
    UHV specification
    316L bellow hydroformed
    DN100CF 316LN ESR 3D forged flanges (1x rotatable)
    Øinner 100mm
    Convolutions needed = 2*thermal displacement / convolution stroke (6.5 mm) = 11

## Slide 8: Bellows specification

## Slide 9: Chamber Manufacture
  Stainless steel tube [Ø100mm],
    Typical length of tube 6m,
    100% weld penetration orbital 6 + 4 m (due to length)
  Internal welding DN100CF flanges
  Fixed support bracket to be mounted on the chamber
  Leak detection
  UHV cleaning to CERN specification EDMS:1626970
  Copper electroplating to reduce the impedance seen by the beam
  NEG coating for distributed pumping.

## Slide 10: Chamber Max 4 - Experiment room

## Slide 11: Chamber Max 4 - Experiment room

## Slide 12: Chamber Max 4 - Experiment room

## Slide 13: 3D model of the vacuum system

## Slide 14: 3D model of the vacuum system

## Slide 15: 3D model of the vacuum system

## Slide 16: 3D model of the vacuum system
weld

## Slide 17: 3D model of the vacuum system

## Slide 18: 3D model of the vacuum system

## Slide 19: Technical drawing

## Slide 20: Technical drawing

## Slide 21: Meet the Team: Tutorial Group 3
GSI

## Slide 22: References
  Materials & Properties I: Introduction. CAS, Vacuum for Particle Accelerators 2017 Dr. Stefano SGOBBA (CERN)
  Materials & Properties II: Thermal & Electrical Characteristics. CAS, Vacuum for Particle Accelerators 2017 Dr. Cedric GARION (CERN)
  Surface Cleaning & Finishing. CAS, Vacuum for Particle Accelerators 2017 Dr. Mauro TABORELLI (CERN)

## Slide 23: Material selection
 | Copper OF annealed | Al-6082-T6 | Stainless steel 316L | Titanium Ti-6Al-4V (Grade 5)
Density | 8950 kg/m3 | 2830 kg/m3 | 7970 kg/m3 | 4430 kg/m3
Young’s modulus | 115 GPa | 77 GPa | 195 GPa | 115 GPa
Yield strength | 35 MPa | 393 MPa | 240 MPa | 880 MPa
Thermal expansion coefficient | 17 · 10-6 1/K | 22 · 10-6 1/K | 16 · 10-6 1/K | 8.9 · 10-6 1/K

## Slide 24
Esr to reduce inclusions