## Slide 1: Instabilities in High Energy Colliders I
Oliver Boine-Frankenheim,
TU Darmstadt and GSI, Darmstadt
Contents:
Part 1: Collective forces on beam particles: Wakefields, Impedances and electron clouds
Part 2: Modes of oscillation in bunches, Instabilities and thresholds
Part 3: Landau damping and instability cures

## Slide 2: Introduction
Beam instabilities (as covered in this presentation) are driven by the electromagnetic interaction with the accelerator environment (-> wakefields/impedances) and by electron clouds.
Above a certain intensity threshold the beam’s oscillation amplitude increases
exponentially and the beam is either lost at the wall (transverse instabilities) or
from the rf bucket (longitudinal) and/or the emittance increases.
Presently, heat loads and instabilities are one of the main beam quality and intensity limitation in particle accelerators for high intensity and brightness !
Finding “cures” for instabilities is one of the major challenges in beam physics and accelerator technology for future machines.
High energy beams: Beam instabilities are a ‘current effect’. However, synchrotron radiation, photoelectrons or other high energy effects affect instability thresholds.

## Slide 3: Some Literature (used for this lecture)
Books on beam instabilites:
A. Chao, Physics of collective beam instabilities in high energy accelerators (1993)
B. Zotter, S. Kheifets, Impedances and Wakes in High Energy Particle Accelerators(1998)
K.Y. Ng, Physics of intensity dependent beam instabilities (2006)
….
Overview articles and lectures:
B. Zotter, F. Sacherer, Transverse instabilities of relativistic particle beams (1976)
E. Metral et al., Beam instabilities in hadron synchrotrons, Trans. Nucl. Sci. IEEE (2016)
…..

## Slide 4: Electromagnetic forces acting on bunches
e-
Electron clouds:
created wall emission and other mechanisms.
-> heat loads, emittance growth and instabilities
beam pipe
Bunch
Wake fields and impedances:
-> heat loads and instabilities
Image current
(lab system)
Incoherent space charge:
(in the rest system of the beam)
-> beam intensity and emittance limits
Beam-beam interaction:
Can cause coherent instabilities.
In this lecture: Focus on instabilities driven by
wake fields and electron clouds.
Beyond this lecture: Interplay of different mechanisms.

## Slide 5: Maxwell‘s equations and Lorentz force
+ boundary conditions at the walls
(resistive) beam pipe section
Bunch
Rigid bunch approximation
The beam traverses the structure rigidly.
Impulse approximation
The EM force continuously acting on a test charge is lumped in a single kick after the passage through the structure.

## Slide 6: Wake fields
T. Weiland and R. Wanzenberg, “Wake Fields and Impedances,” in CERN Accelerator School (CAS), 1993. 20, 28, 99
L. Palumbo, V. G. Vaccaro, and M. Zobov, “Wake Fields and Impedance,” in Cern Accelerator School, 1994. 20
z
s
Transverse:
Longitudinal:

## Slide 7: Wake functions
Ng (2006)
Longitudinal:
For a test particle in a bunch:
(Voltage kick or Wake potential)
Line density:
Transverse:
(horizontal kick)
For a test particle in a bunch:
: local bunch offset

## Slide 8: Reminder: Charged particle in free space
ake
Electric field:
pancaked field
Image charges/currents
follow the particle
A.Chao (1993)
Remark:
No wake (without bends)

## Slide 9: Wake field in a resistive beam pipe
A.Chao (1993)
K. Bane (1991)
Longitudinal wake field
Finite conductivity:
z
z
Energy loss of a bunch:
Longitudinal:
Transverse:
: line density

## Slide 10: Wake potential: Numerical example
Longitudinal cut
Dispersively lossy ferrite material
10 cm
Magnitude of the electric field, logarithmic color scale
Wake potential (convolution of wake function with line density)
Beam line density (a.u.)
CST Particle Studio®
Uwe

## Slide 11: Panofsky-Wenzel Theorem (PWT)
+ Impulse approximation
+ Rigid bunch approximation
Transverse:
For
Boundaries do not matter !
PWT connects transverse and longitudinal wakes.
For
Wake functions:

## Slide 12: Impedances
PWT:
Fourier transforms of the wake functions:
Impedances:
Bench measurements (with wires)
Frequency-domain (FD) EM simulations
Beam stability: Perturbation theory
Wake functions:
Time-domain (TD) EM simulations
Beam stability: Simulations in TD
]
]
Other properties:
PWT:
Example: cylindrical (thick) beam pipe
(skin depth)
pipe radius

## Slide 13: Impedances and current/offset modulations
induced voltage:
beam particle
current modulation:
Transverse impedance (divided by length):
Offset oscillations
beam pipe
beam
image currents
By
Deflecting dipolar
force:

## Slide 14: Longitudinal impedance: Heat load
beam pipe
From impedance (see e.g. A. Chao):
Bad conductor
Example: resistive wall
Energy loss of a bunch (per length):
Temperature in LHC injection kicker (ferrite loaded). One
needs to wait until it cools down to reinject (B. Salvant, 2012)
(line
density)
bunch spacing
Heat load:

## Slide 15: Transverse impedances: LHC and FCC-hh beam pipes
b=0.014 m
b=0.02 m
(Thick) resistive wall impedance
FCC
LHC
few kHz
kHz
Obtained with an impedance solver in the FD (U. Niedermayer, D. Astapovych)
At sufficiently high frequencies
(a few 100 Hz) only the vacuum
regions have to be meshed.

## Slide 16: Electron clouds
    Secondary Electron Emission can drive an avalanche multiplication effect filling the beam chamber with an electron cloud
    Proton bunch
    e- is emitted (photoelectric effect)
    Secondary Electron Emission
Affects mainly machines operating with positively charged particles
G. Iadarola
Bunches at the end of the train interact
with a (‘low density’) saturated e-cloud
Transverse instabilities
Transverse emittance blow-up
Energy loss -> Heat load on the cryogenic system

## Slide 17: Remark: Plasma densities and temperatures
lightning
Electron clouds
eV
Electron clouds:

## Slide 18: Electron cloud as a dielectric medium ?
(electron plasma dielectric function)
(electron plasma frequency)
Poisson equation
Unfortunatelly not: Requires „linear response“. A short LHC proton bunch
represents a strong perturbation for the „low density electron plasma“
and results in a (very) nonlinear response. Would work at higher electron densities.
See e.g. A. Al-Khateeb et al.,
Screening of the resistive-wall impedance by a cylindrical electron plasma
NJP (2008)

## Slide 19: Secondary Emission Yield (SEY)
Secondary Emission Yield (SEY)
el: Elastic scattered
se: Secondaries
Measured total SEY from a Cu surface
as a function of the electron energy
(from R. Cimino at al, Phys. Rev. Lett. (2004))
Beam induced scrubbing reduces
the SEY (but can take weeks).
e-Capture
e-Energy gain
e-Multiplication
Short bunch
Beam pipe
reflected e

## Slide 20: Coating and impedance
Coatings, like carbon and laser treatment, can reduce the SEY to values below 1.
Valizadeh et al., Appl. Phys. Lett. (2014)
Beam pipe + a thin resistive layer
Enlarged impedance at
Arsenyev, FFC week (2017)
Cu samples: (a) untreated and (b) laser treated.

## Slide 21: Electron cloud interaction with rigid bunches
beam pipe
Short (< 10 ns) proton
bunch (N=1011)
e-cloud
e-Multiplication (SEY model)
reflected e
Force on the bunch:
Space charge field (e-cloud):
Electric field of the rigid bunch:
(Line density)
Example result for
Electron equation of motion:
Relativistic momenta:
Simulation codes for electron cloud interaction with bunch trains or long bunches: pyCloud, openecloud, ….

## Slide 22: Longitudinal e-cloud wake field and energy loss
Energy loss of a short bunch in an
(initially homogeneous) electron cloud:
J. Esteban-Müller, E. Shaposhnikova
bunch energy
loss measured
in LHC during
scrubbing runs
rf phase shift vs. bunch intensity

## Slide 23: Transverse e-cloud wake function
e--cloud
Ohmi, Zimmermann, PRE (2001)
one displaced
bunch slice
Transverse wake function can be
approximated as a resonator:
resonant e-frequency:
coupling parameter:
amplitude:
Obtain parameters by fit to simulations !
Remarks:
- Not a wake function, but a response function.
- More complicate in dipoles or quadrupoles.

## Slide 24: Summary and conclusions: Part I
Electromagnetic interaction with the accelerator environment is described through wake functions or impedances -> forces on the beam particles
Panofsky-Wenzel Theorem (PWT) links longitudinal and transverse forces.
Longitudinal wake function / impedance: Energy loss and heat load
Electron cloud buildup by multipacting can be suppressed by sufficiently long scrubbing or coatings, which increase the impedance at high frequencies.
The force on the beam particles can (in some cases) be described by electron cloud wake functions. The parameters for the wakes are obtained from fits to simulation results.
High beam energies:
small beam sizes , weak space charge (and image) effects.