## Slide 1: Instabilities in High Energy Colliders II
Oliver Boine-Frankenheim,
TU Darmstadt and GSI, Darmstadt
Contents:
Part 1: Collective forces on beam particles: Wakefields, Impedances and electron clouds
Part 2: Modes of oscillation in bunches, Instabilities and thresholds
Part 3: Landau damping and instability cures

## Slide 2: Introduction
Electromagnetic (EM) interaction of the beam with its surroundings can be described by impedances or wake fields. For rough estimates also the interaction with electron cloud can be described by wake functions (see Part 1).
Impedances/Wakefields cause complex coherent tune shifts and (above some threshold intensity) unstable coherent beam oscillations (Part 2).
Cures: Impedance reduction, Landau damping and tune spread (Part 3), feedback systems,..
Focus on high energy beams in rings and transverse instabilities in this lecture.

## Slide 3: (Reduced) 3D beam physics model
(horizontal betatron oscillations)
(synchrotron oscillations)
(frequency slip factor)
3D beam density:
Line density:
Nonlinear terms:
Landau damping
(Wakes and impedances)
Collective forces:
(longitudinal electric field)
(Energy)

## Slide 4: Transverse tune shifts (2D or coasting beam)
x
y
s
Betatron oscillations with beam induced forces:
Assuming small offsets:
(only horizontal)
Beam offset oscillations (coherent):
Incoherent tune shift:
Coherent tune shift:

## Slide 5: Instability growth rate (coasting beams)
(Thick wall) resistive wall impedance:
(skin depth)
Instability growth rate:
(function)
Betatron sideband :
Offset oscillations:
(from Part 1)
: revolution frequency

## Slide 6: Bunched beams: Transverse head-tail modes
(betatron oscillations)
(synchrotron oscillations)
k=1:
k=0:
head-tail oscillations
Signal:
‚rigid‘ mode
Stable (for single bunches) !
Sacherer (1974)
betatron
sidelines
Power spectrum
of head-tail modes

## Slide 7: Head-tail modes: Chromatic phase shift
Traveling wave pattern !
Sacherer (1974)
Unstable !
(head-tail phase shift)
(Chromatic tune shift)
bunch head
bunch tail
(betatron phase shift)
z
Unstable head-tail oscillations in the CERN PS
Spectrum:
bunch length

## Slide 8: Transverse coupled-bunch instabilities
Example: Coupled „rigid“ bunch mode
Coasting beam:
Sacherer (1974)
Effective impedance:
Number of bunches
Growth rate for mode k:
(chromatic frequency shift)

## Slide 9: Transverse coupled-bunch instabilities II
for a smooth impedance and
rigid (k=0) oscillations:
Positive/negative chromaticity above/below transition shifts all modes
towards the positive frequency side. Mode k = 0 becomes stable, but
mode k = 1 may be unstable because it samples more negative Z than
positive. No head-tail instability for compensated chromaticity.
Sacherer (1974)
if only one sideband matters:
(form factor)

## Slide 10: Resistive wall instability: Growth rates for LHC and FCC-hh
b=0.014 m
b=0.02 m
(Thick) resistive wall impedance
growth time at 3.3 TeV:
approx. 200 turns
at 50 TeV:
approx. 800 turns
LHC at 7 TeV:
approx. 2000 turns
Growth rate:
FCC
LHC
few kHz
kHz
Damping by feedback or Landau damping -> Instability thresholds (Part 3)

## Slide 11: Two-particle model: Single bunch break up
Tail
Head
(z)
R. Cappi et al. (2000)
Observation in the CERN PS near transition
Two-particle coupled betatron oscillations:
New coordinates:
Solution:
Linear growth !
Linac
Assume that you have corrected chromaticity
and a (working) feedback system for the „rigid“
coupled bunch instability (or you have a linac).

## Slide 12: Two-particle model: Strong head-tail instability
Change of position in z every:
Instability threshold !
Mode coupling !
A. Chao
rigid
A. Chao (p. 181): It is straightforward to show that ….
(low intensity)
Synchrotron oscillations suppress beam breakup !

## Slide 13: More general: Transverse Mode Coupling Instabilities (TMCI)
B. Salvant et. al. 2008
Experiments / Simulations

## Slide 14
Contents:
Part 1: Collective forces on beam particles: Wakefields, Impedances and electron clouds
Part 2: Modes of oscillation in bunches, instabilities and thresholds
Part 3: Landau damping and instability cures

## Slide 15: Landau damping (LD)
Very simple picture (in beams):
Lev Davidovich Landau, On the vibration of the electronic plasma, JETP (1946)
Cédric Villani, Fields medal for (nonlinear) Landau damping, 2010
-> instability thresholds
reversible (see beam/plasma echoes)
LD of plasma waves:
still a very active field of research !
( rms tune spread due
to octupoles, beam-beam.....)
Remark: In this short lecture only nonlinearities will
be discussed as a source of the tune spread.
Detailed LD analysis requires: Vlasov equation + Poisson equation
LD of transverse beam oscillations:
D. Möhl , F. Ruggiero et al.

## Slide 16: (Nonlinear) tune shifts from octupoles
LHC: 168 dedicated octupoles
for Landau damping
Magnet field:
octupole
strength
rms emittances
normalized amplitudes
Betatron oscillations (incoherent):
Tune shifts (integrated):
Beam distribution:
rms tune spread:

## Slide 17: Dispersion relation
[1] H. G. Hereward, CERN 65-20 (1965)
[2] J. S. Berg, F. Ruggiero, CERN SL-AP-96-71 (1996)
(bare tunes)
(octupoles)
(impedances)
Driven (nonlinear) betatron oscillations:
Used from previous slides:
real coherent shift
growth or damping rate
Ansatz:
Remark [1]: 1D beam response
2D dispersion relation [2]:
Solve for

## Slide 18: Application to LHC: Stability diagram
Tune distribution
Stability curve
Numerical damping rate:

## Slide 19: Landau damping at very high energies
The good news:
The OK news:
(tune spread required for LD)
The bad news:
(tune spread provided by octupoles)
(instability growth rate)
circumference
length of magnet
normalized emittance
# of magnets
From LHC to FCC-hh: 72 x 168 octupoles

## Slide 20: Landau damping by electron lenses
Similar to the beam-beam force !
Tune shift induced by a
counter-propagating electron beam:
Electron lenses
dc e-beam
Bunch
Matched transverse beam radii.
Gaussian electron
beam provides a
nonlinear tune shift.
Example: One e-lens (l=2 m, Ie=1 A) in LHC would
provide a tune spread similar to the 168 octupoles.
V. Shiltsev et al., PRL (2017)

## Slide 21: Summary and Conclusions: Parts 2+3
Some aspects of transverse beam instabilities with a focus on hadrons and rings were covered.
Landau damping due to the nonlinear tune shifts was discussed.
Besides studies of “passive” Landau damping, active feedback systems are a very active field of R&D and might be able to cure most instabilities in the future.
The study of the interplay of impedances, electron clouds, beam-beam, ... becomes even more relevant as the machines are operated close to the intensity limits.
Computer simulations (particle tracking, Vlasov solvers) are essentials tools to study such more complex scenarios.

## Slide 22
Backup

## Slide 23: Two-particle model: application to e-cloud