## Slide 1: RF Cavity Design
Erk Jensen
CERN BE/RF
CERN Accelerator School
Accelerator Physics (Advanced level)
Trondheim 2013

## Slide 2: Overview
DC versus RF
  Basic equations: Lorentz & Maxwell, choice of frequency, RF breakdown, breakdown rate
Some theory: from waveguide to pillbox
  rectangular waveguide, waveguide dispersion, group and phase velocity, modes, equations, standing waves … waveguide resonators, round waveguides, Pillbox cavity
Accelerating gap
  Principle, ferrite cavity, Finemet® cavity, drift tube linac
Characterizing a cavity
  Accelerating voltage, transit time factor
  Resonance frequency, shunt impedance,
  Beam loading, loss factor, RF to beam efficiency,
  Transverse effects, Panofsky-Wenzel, higher order modes, PS 80 MHz cavity (magnetic coupling)
More examples of cavities
  PEP II, LEP cavities, PS 40 MHz cavity (electric coupling),
Many gaps
  Why?
  Example: side coupled linac, LIBO
Travelling wave structures
  Brillouin diagram, iris loaded structure, waveguide coupling
Superconducting Accelerating Structures
  RF superconductivity, elliptical multi-cell cavity, low- geometries, cryomodule
Cavity fabrication techniques
  Materials (Cu, Nb)
  Forming techniques
  joining techniques
  Specific techniques developed for SCRF

## Slide 3: DC versus RF

## Slide 4: DC versus RF
DC accelerator
RF accelerator
potential

## Slide 5: Lorentz force
A charged particle moving with velocity through an electromagnetic field experiences a force .
The total energy of this particle is , the kinetic energy is .
The role of acceleration is to increase .
Change of (by differentiation):
Note: Only the electric field can change the particle energy!

## Slide 6: Maxwell’s equations (in vacuum)
Why not DC?
    DC (): , which is solved by
    Limit: If you want to gain 1 MeV, you need a potential of 1 MV!
Circular machine: DC acceleration impossible since
    With time-varying fields:
World’s highest energy Van-de-Graaff Generator on Daresbury Lab campus

## Slide 7: Maxwell’s equations in vacuum (contd.)
Source-free:
curl (rot, ) of 3rd equation and of 1st equation:
Using the vector identity and the 4th Maxwell equation, this yields:
i.e. the 4-dimensional Laplace equation.

## Slide 8: Choice of frequency
Size:
  Linear dimensions scale as , volume as .
  amount of material, mass, stiffness, tolerances, …
  Outer radius of elliptical cavity .
Beam interaction:
  increases with – but also for HOMs!
  short bunches are easier with higher .
Technology:
  superconducting: BCS resistance .
  Power sources available?
  Max. accelerating voltage?

## Slide 9: Breakdown limit – -dependence
surface field, in vacuum, Cu surface, room temperature
Note: More recent experimental data show much less -dependence!
E.g.: http://prl.aps.org/abstract/PRL/v90/i22/e224801

## Slide 10: Breakdown rate!
In an accelerator with many structures, the breakdown rate (BDR) must be much smaller than the number of structures.
E.g.: CLIC target (results in 1% for 30 km)
Empirically, the breakdown rate can be described with the dependence , where
  : formation energy required to form a dislocation (void),
  : the volume change due to the dislocation.
This is a very steep dependence on the surface field!
Parameters:

## Slide 11: From waveguide to pillbox

## Slide 12: Homogeneous plane wave
Wave vector :
the direction of is the direction of propagation,
the length of is the phase shift per unit length.
behaves like a vector.
z
x
Ey
φ

## Slide 13: Wave length, phase velocity
The components of are related to the wavelength in the direction of that component as etc. , to the phase velocity as .
z
x
Ey

## Slide 14: Superposition of 2 homogeneous plane waves
+
=
Metallic walls may be inserted where without perturbing the fields. Note the standing wave in -direction!
z
x
Ey
This way one gets a hollow rectangular waveguide

## Slide 15: Rectangular waveguide
Fundamental (TE10 or H10) mode
in a standard rectangular waveguide.
Example: “S-band” : 2.6 GHz ... 3.95 GHz,
Waveguide type WR284 (2.84” wide), dimensions: 72.14 mm x 34.04 mm.
Operated at .
electric field
magnetic field
power flow:
power flow
power flow

## Slide 16: Waveguide dispersion
What happens with different waveguide dimensions (different width a)?
1: a = 52 mm, f/fc = 1.04
cutoff
f = 3 GHz
2:
a = 72.14 mm, f/fc = 1.44
3:
a = 144.3 mm, f/fc = 2.88
1
2
3

## Slide 17: Phase velocity
1: a = 52 mm, f/fc = 1.04
f = 3 GHz
2:
a = 72.14 mm, f/fc = 1.44
3:
a = 144.3 mm, f/fc = 2.88
The phase velocity is the speed with which the crest or a zero-crossing travels in z-direction.
Note on the three animations on the right that, at constant f, it is .
Note that at , !
With , !
cutoff
1
2
3

## Slide 18: Summary waveguide dispersion and phase velocity:
e.g.: TE10-wave in rectangular waveguide:
In a general cylindrical waveguide:
In a hollow waveguide: phase velocity > c, group velocity < c

## Slide 19: Rectangular waveguide modes
TE10
TE20
TE01
TE11
TM11
TE21
TM21
TE30
TE31
TM31
TE40
TE02
TE12
TM12
TE41
TM41
TE22
TM22
TE50
TE32
plotted: E-field

## Slide 20: Radial waves
Also radial waves may be interpreted as superposition of plane waves.
The superposition of an outward and an inward radial wave can result in the field of a round hollow waveguide.

## Slide 21: Round waveguide
f/fc = 1.44
TE11 – fundamental
TM01 – axial field
TE01 – low loss

## Slide 22: Circular waveguide modes
TE11
TM01
TE21
TE21
TE11
TE31
TE31
TE01
TM11
plotted: E-field

## Slide 23: General waveguide equations:
Transverse wave equation (membrane equation): .
 | TE (or H-) modes | TM (or E-) modes
Boundary condition: |  | 
longitudinal wave equations (transmission line equations): |  | 
Propagation constant: |  | 
Characteristic impedance: |  | 
Ortho-normal eigenvectors: |  | 
Transverse fields: |  | 
Longitudinal fields: |  | 
 | TE (or H-) modes | TM (or E-) modes
Boundary condition: |  | 
longitudinal wave equations (transmission line equations): |  | 
Propagation constant: |  | 
Characteristic impedance: |  | 
Ortho-normal eigenvectors: |  | 
Transverse fields: |  | 
Longitudinal fields: |  | 

## Slide 24: Special cases: rectangular and round waveguide
Rectangular waveguide: transverse eigenfunctions
Round waveguide: transverse eigenfunctions
where in both cases
TE (H-) modes: | 
TM (E-) modes: | 
TE (H-) modes: | 
TM (E-) modes: | 
TE (H-) modes: | 
TM (E-) modes: | 
TE (H-) modes: | 
TM (E-) modes: | 

## Slide 25: Waveguide perturbed by notches
“notches”
Reflections from notches lead to a superimposed standing wave pattern.
“Trapped mode”
Signal flow chart

## Slide 26: Short-circuited waveguide
TM010 (no axial dependence)
TM011
TM012

## Slide 27: Single WG mode between two shorts
short circuit
short circuit
Eigenvalue equation for field amplitude :
Non-vanishing solutions exist for :
With , this becomes .
Signal flow chart

## Slide 28: Simple pillbox
electric field (purely axial)
magnetic field (purely azimuthal)
(only 1/2 shown)
TM010-mode

## Slide 29: Pillbox cavity field (w/o beam tube)
The only non-vanishing field components :
h
Ø 2a

## Slide 30: Pillbox with beam pipe
electric field
magnetic field
(only 1/4 shown)
TM010-mode
One needs a hole for the beam pipe – circular waveguide below cutoff

## Slide 31: A more practical pillbox cavity
electric field
magnetic field
(only 1/4 shown)
TM010-mode
Round of sharp edges (to reduce field enhancement!)

## Slide 32: Accelerating gap

## Slide 33: Accelerating gap
gap voltage
We want a voltage across the gap!
The limit can be extended with a material which acts as “open circuit”!
Materials typically used:
  ferrites (depending on f-range)
  magnetic alloys (MA) like Metglas®, Finemet®, Vitrovac®…
resonantly driven with RF (ferrite loaded cavities) – or with pulses (induction cell)
It cannot be DC, since we want the beam tube on ground potential.
Use
The “shield” imposes a
  upper limit of the voltage pulse duration or – equivalently –
  a lower limit to the usable frequency.

## Slide 34: Ferrite cavity
CERN PS Booster, ‘98
0.6 – 1.8 MHz
< 10 kV gap
NiZn ferrites

## Slide 35: Finemet® Cavity
Finemet® is a magnetic alloy exhibiting wideband frequency response and large magnetic field saturation level; it allows building wide-band cavities.
Compared to ferrite cavities, no bias is needed!
Example: the CERN PSB 5-gap system:
frequency response: (0.6 … 4) MHz
5 gap prototype
… installed in PSB ring 4
Single Finemet® ring on its cooling plate

## Slide 36: Gap of PS cavity (prototype)

## Slide 37: Drift Tube Linac (DTL) – how it works
For slow particles !
E.g. protons @ few MeV
The drift tube lengths
can easily be adapted.
electric field

## Slide 38: Drift tube linac – practical implementations

## Slide 39: Characterizing a cavity

## Slide 40: Acceleration voltage & R-upon-Q
I define . The exponential factor accounts for the variation of the field while particles with velocity are traversing the gap (see next page).
With this definition, is generally complex – this becomes important with more than one gap. For the time being we are only interested in .
The proportionality constant defines the quantity called R-upon-Q:
The square of the acceleration voltage is proportional to the stored energy .
Attention, different definitions are used!
Attention, also here different definitions are used!

## Slide 41: Transit time factor
h/l
The transit time factor is the ratio of the acceleration voltage to the (non-physical) voltage a particle with infinite velocity would see.
The transit time factor of an ideal pillbox cavity (no axial field dependence) of height (gap length) h is:
Field rotates by 360° during particle passage.

## Slide 42: Shunt impedance
The proportionality constant defines the quantity “shunt impedance”
The square of the acceleration voltage is proportional to the power loss .
Attention, also here different definitions are used!
Traditionally, the shunt impedance is the quantity to optimize in order to minimize the power required for a given gap voltage.

## Slide 43: Cavity resonator - equivalent circuit
R
Cavity
Generator
IG
Z
P
C=Q/(Rw0)
Vacc
Beam
IB
L=R/(Qw0)
L
C
: coupling factor
R: Shunt impedance
: R-upon-Q
Simplification: single mode

## Slide 44: Resonance

## Slide 45: Reentrant cavity
Example: KEK photon factory 500 MHz - R probably as good as it gets -
this cavity optimized
pillbox
R/Q: 111 Ω 107.5 Ω
Q: 44270 41630
R: 4.9 MΩ 4.47 MΩ
Nose cones increase transit time factor, round outer shape minimizes losses.
nose cone

## Slide 46: Loss factor
0
5
1
0
1
5
2
0
t f0
-
1
0
1
Voltage induced by a single charge q:
R
R/b
Cavity
Beam
C=Q/(Rw0)
V (induced)
IB
L=R/(Qw0)
L
C
Energy deposited by a single charge q:
Impedance seen by the beam

## Slide 47: Summary: relations Vgap, W, Ploss
Energy stored inside the cavity
Power lost in the cavity walls
gap voltage
Ploss
Vgap
W
R-upon-Q
Shunt impedance
Q factor

## Slide 48: Beam loading – RF to beam efficiency
The beam current “loads” the generator, in the equivalent circuit this appears as a resistance in parallel to the shunt impedance.
If the generator is matched to the unloaded cavity, beam loading will cause the accelerating voltage to decrease.
The power absorbed by the beam is , the power loss .
For high efficiency, beam loading shall be high.
The RF to beam efficiency is .

## Slide 49: Beam Loading – allows efficiency
full beam loading – optimum efficiency
choice for CLIC main beam
eta
acceleration

## Slide 50: Characterizing cavities
Resonance frequency
Transit time factor
  field varies while particle is traversing the gap
Shunt impedance
  gap voltage – power relation
Q factor
R/Q
  independent of losses – only geometry!
loss factor
Linac definition
Circuit definition

## Slide 51: Example Pillbox:

## Slide 52: Pillbox: dipole mode
electric field
magnetic field
(only 1/4 shown)
TM110-mode

## Slide 53: Panofsky-Wenzel theorem
For particles moving virtually at v=c, the integrated transverse force (kick) can be determined from the transverse variation of the integrated longitudinal force!
W.K.H. Panofsky, W.A. Wenzel: “Some Considerations Concerning the Transverse Deflection of Charged Particles in Radio-Frequency Fields”, RSI 27, 1957]
Pure TE modes: No net transverse force !
Transverse modes are characterized by
the transverse impedance in ω-domain
the transverse loss factor (kick factor) in t-domain !

## Slide 54: CERN/PS 80 MHz cavity (for LHC)
inductive (loop) coupling, low self-inductance

## Slide 55: Higher order modes
Example shown:
80 MHz cavity PS for LHC.
Color-coded:

## Slide 56: Higher order modes
IB
R3, Q3,w3
R2, Q2,w2
R1, Q1,w1
...
...
external dampers
n1
n3
n2

## Slide 57: Higher order modes (measured spectrum)
without dampers
with dampers

## Slide 58: More examples of cavities

## Slide 59: PS 19 MHz cavity (prototype, photo: 1966)

## Slide 60: Examples of cavities
PEP II cavity
476 MHz, single cell,
1 MV gap with 150 kW,
strong HOM damping,
LEP normal-conducting Cu RF cavities,
350 MHz. 5 cell standing wave + spherical cavity for energy storage, 3 MV

## Slide 61: CERN/PS 40 MHz cavity (for LHC)
example for capacitive coupling
cavity
coupling C

## Slide 62: RF power sources

## Slide 63: RF Power sources
Thales TH1801, Multi-Beam Klystron (MBK), 1.3 GHz, 117 kV. Achieved:
48 dB gain, 10 MW peak, 150 kW average, η = 65 %
> 200 MHz: Klystrons
Tetrode IOT UHF Diacrode®
< 1000 MHz: grid tubes
pictures from http://www.thales-electrondevices.com
48 dB:
Gun
Input
Cavity
Collector
Output
Cavity
Magnet
Window
Intermediate
cavities
electrons bunching

## Slide 64: RF power sources

## Slide 65: Example of a tetrode amplifier (80 MHz, CERN/PS)
22 kV DC anode voltage feed-through with λ/4 stub
18 Ω coaxial output (towards cavity)
coaxial input matching circuit
tetrode cooling water feed-throughs
400 kW, with fast RF feedback

## Slide 66: Many gaps

## Slide 67: What do you gain with many gaps?
The R/Q of a single gap cavity is limited to some 100 Ω. Now consider to distribute the available power to n identical cavities: each will receive P/n, thus produce an accelerating voltage of . The total accelerating voltage thus increased, equivalent to a total equivalent shunt impedance of .
1
2
3
n
P/n
P/n
P/n
P/n

## Slide 68: Standing wave multicell cavity
Instead of distributing the power from the amplifier, one might as well couple the cavities, such that the power automatically distributes, or have a cavity with many gaps (e.g. drift tube linac).
Coupled cavity accelerating structure (side coupled)
The phase relation between gaps is important!

## Slide 69: Example of Side Coupled Structure
A 3 GHz Side Coupled Structure to accelerate protons out of cyclotrons from 62 MeV to 200 MeV
Medical application:
treatment of tumours (proton therapy)
Prototype of Module 1 built at CERN (2000)
Collaboration CERN/INFN/TERA Foundation
LIBO (= Linac Booster)

## Slide 70: LIBO prototype
This Picture made it to the title page of CERN Courier vol. 41 No. 1 (Jan./Feb. 2001)

## Slide 71: Travelling Wave Structures

## Slide 72: Brillouin diagram Travelling wave structure
synchronous
2p
w L/c
speed of light line,
w = b /c
p
p/2
p
p/2
b L
0
0
p/2
p
2p/3

## Slide 73: Iris loaded waveguide
1 cm
30 GHz structure
11.4 GHz structure (NLC)

## Slide 74: Disc loaded structure with strong HOM damping “choke mode cavity”
Dimensions in mm

## Slide 75: Power coupling with waveguides
¼ geometry shown
Input coupler
Output coupler
Travelling wave structure
(CTF3 drive beam, 3 GHz)
shown: Re {Poynting vector} (power density)

## Slide 76: 3 GHz Accelerating structure (CTF3)

## Slide 77: Examples (CLIC structures @ 11.4, 12 and 30 GHz)
“T18” reached 105 MV/m!
“HDS” – novel fabrication technique

## Slide 78: Superconducting Accelerating Structures

## Slide 79: RF Superconductivity
Best described by BCS (Bardeen- Cooper-Schrieffer) Theory
Surface resistance .
is not zero - is finite.
Good values are some .
Typical performance plot of a SC cavity:
From prst-ab.aps.org/abstract/PRSTAB/v3/i9/e092001

## Slide 80: Elliptical multi-cell cavities
The elliptical shape was found as optimum compromise between
  maximum gradient ()
  suppression of multipactor
  mode purity
  machinability
Operated in -mode, i.e. cell length is exactly .
It has become de facto standard, used for ions and leptons! E.g.:
  ILC/X-FEL: 1.3 GHz, 9-cell cavity
  SNS (805 MHz)
  SPL/ESS (704 MHz)
  LHC (400 MHz*))
D. Proch: SRF 1993 *)
*): accelconf.web.cern.ch/accelconf/SRF93/papers/srf93g01.pdf‎
At : , .

## Slide 81: LHC SC RF, 4 cavity module, 400 MHz
installed in LHC IP4, 2 MV/cavity
LHC spare module stored in CERN’s SM18

## Slide 82: Small superconducting cavities (example RIA, Argonne)
Some pictures from Shepard et al.: “Superconducting accelerating structures for a multi-beam driver linac for RIA”, Linac 2000, Monterey.
fork cavity
QWR
¼-wave-resonator
“lollipop” cavity
spoke cavity
split ring cavity
fork cavity

## Slide 83: SC Cavity Cryomodule examples
RF Power Coupler
Bulk Niobium 5Cells cavity
Helium Tank
CEA’s tuner
Hom Coupler
Bi-phase helium tube
Magnetic shielding
Inter-cavity support
Bellows
Double walled tube
HIE-Isolde (radioactive isotopes post-accelerator), 101 MHz, 5-cavity CM
SPL/ESS 704 MHz CM (partial view)
¼ wave cavity
ILC/X-FEL 1.3 GHz, 8 cavity CM

## Slide 84: SPL Cryomodule assembly sequence
1- String of dressed cavities from clean room
2- Mounting of magnetic shields
3- Mounting of tuners and inter-cavity supports
Design by CNRS-IPNO
(courtesy of S.Rousselot)
4- Mounting of cryogenic distribution
5- Mounting of coupler cooling line
6- Mounting of thermal shield
7- Insertion in vacuum vessel
8- Closing vacuum vessel
Rossana Bonomi (CERN)

## Slide 85: HL-LHC Crab Cavity test CM
crab cavity
He vessel manufacturing
2-cavity string
He vessel
Cryomodule
magnetic shield
thermal shield
T. Jones, S. Pattalwar
Presently under study!

## Slide 86: Cavity Fabrication techniques

## Slide 87: Materials
Selection criteria
  Electrical conductivity
  Secondary emission yield
  mechanical stiffness/hardness
  thermal conductivity, thermal expansion
  machining & joining techniques
  vacuum tight, low outgassing rate
  creep resistance,
  magnetic permeability
  radiation hardness
  fatigue stress
  …
Important: specify what you need and what you can measure/control at reception!

## Slide 88: OFE copper
Most room temperature cavities are made from copper (SLAC, CERN LEP, etc., B-factories) – (but still with plenty of exceptions, aluminium PEP).
Solid OFE*) copper was used in LEP injector linac and the NC linear collider studies (NLC, JLC, CLIC). It is used for NC linacs today (Linac4, CLIC & CTF, linac based light sources and medical linacs).
Copper becomes soft after annealing (or brazing). It is hardened by deformation (forging).
The copper for the LEP storage cavities and for CERN’s S-Band waveguides contain 0.1% silver (Cu-OFS), which increases the creep resistance by a factor 5.
“official names”: copper OFE Grade 1 (ASTM B224-98 oxygen free electronic, ISO 431 Cu-OFE, UNS C10100)
*) also called OFHC – oxygen free high conductivity

## Slide 89: Galvanic Cu plating of stainless steel
Anodes made from Pt coated Ti, adapted to the inner shape of the cavity.
Inside surface of the electroplated cavity
In the surface-chemistry lab: the cavity itself was used as container

## Slide 90: Niobium
Magnets use NbTi or Nb3Sn, SC Cavities use mainly Nb!
Pure Nb has a high critical magnetic field ()
Nb has a high transition temperature ().
It is chemically inert (surface covered by oxide layer)
It can be machined and deep-drawn
It is available as bulk and sheet material in any size, fabricated by forging and rolling
Large grain sizes (often favoured) obtained by e-beam melting
Instead of bulk or sheet Nb, Nb can also be coated (e.g. by sputtering) on Cu – CERN has built the LEP, LHC and HIE-Isolde cavities with this technique. Advantages: thermal stability, material cost, optimisation of possible; disadvantages: difficult technology to master, lower .
Nb ingot after EBM at Heraeus (D)

## Slide 91: Dielectrics
Aluminium oxide, AL2O3, aka Alumina, is often used in vacuum/RF windows and vacuum feed-throughs.
Isostatically pressed AL2O3 is used for leak-tightness (LEP power couplers, e.g.).
To reduce multipactor, it is often coated with titanium or titanium nitride (TiN).
Other window materials: Sapphire, BeO, quartz, diamond …)
Silicon carbide (SiC), C-loaded AlN have been effectively used as RF absorbers inside vacuum.
Different ferrites are used as absorbers and to use their variable magnetic permeability.
Coax transition through alumina window with traces of breakdown

## Slide 92: Metal forming
Typical surface finish for classical machining operations

## Slide 93: Turning
Classical industrial technique; cheap and accurate, gives excellent surface finish. Applies to a wide range of cavity dimensions (frequencies).
NB.:
Cutting fluids should be oil-free and sulphur free.
High-speed machining with diamond tools can be made with alcohol or even dry.
Diamond-turned Cu disks with 30-GHz cavities. Precise control of surface finish down to N1.
Part of the PS 40 MHz cavity after raw machining

## Slide 94: 5-axis milling
Direct 5-axis milling of cooling water circuit groove in PEPII cavity.

## Slide 95: EDM (Electric discharge machining)
Machines el. conductors (metals, alloys, carbides, graphite etc.) by creating sparks with temperatures of 8,000 to 12,000 °C. The part and the electrode are immersed in a dielectric liquid, usually water or mineral oil. There are two types of EDM, die sinking and wire cutting.
die sinking
wire cutting
wire cutting of the iris slots of SICA (slotted iris – constant aperture) disks for CERN’s CTF3 drive beam accelerator

## Slide 96: Fabrication of Nb sheets at
Nb ingot
Pressing
1st EB melting
2nd, 3rd … EB melting
Separate from base plate
Forging
Milling
Rolling
Polishing
Rolling
Cutting
Annealing
Levering
Chemical polishing
Inspections: (ICP-AES, Gas analysis, RRR, grain size, hardness tensile stress …)

## Slide 97: Other forming techniques
Forging, pressing, deep drawing, …
Spinning, planing, rolling, …
lapping, polishing, electropolishing, …
Electroforming, hydroforming, explosion forming
Powder metal techniques, 3-D printing
Sputtering
…

## Slide 98: Joining techniques
TIG welding
double joint: inner for vacuum,
out for mechanical stability
EB welding
Microstructure of the EB welding area grain size (50 ÷ 2000) μm

## Slide 99: Advances in SCRF Technology
Preparing for EP (inserting cathode)
Clean room assembly (JLAB)
Photos: Rongli Geng
C. Antoine: CAS SC 2013

## Slide 100: Thank you very much!