## Slide 1: Beam instabilities (I)
Giovanni Rumolo
in CERN Accelerator School, Advanced Level, Warsaw
Wednesday 30.09.2015

## Slide 2: What is a beam instability?
What is a beam instability?
  A beam becomes unstable when a moment of its distribution exhibits an exponential growth (e.g. mean positions <x>, <y>, <z>, standard deviations sx, sy, sz, etc.) – resulting into beam loss or emittance growth!
z
y
x
And similar definitions for
2

## Slide 3: What is a beam instability?
What is a beam instability?
  A beam becomes unstable when a moment of its distribution exhibits an exponential growth (e.g. mean positions <x>, <y>, <z>, standard deviations sx, sy, sz, etc.) – resulting into beam loss or emittance growth!
z
y
x
Beam Position Monitor
Stable beam

## Slide 4: What is a beam instability?
What is a beam instability?
  A beam becomes unstable when a moment of its distribution exhibits an exponential growth (e.g. mean positions <x>, <y>, <z>, standard deviations sx, sy, sz, etc.) – resulting into beam loss or emittance growth!
z
y
x
Unstable beam
Beam Current Transformer
DI
Beam Position Monitor

## Slide 5: What is a beam instability?
What is a beam instability?
  A beam becomes unstable when a moment of its distribution exhibits an exponential growth (e.g. mean positions <x>, <y>, <z>, standard deviations sx, sy, sz, etc.) – resulting into beam loss or emittance growth!
Unstable beam
Beam Current Transformer
DI
Beam Position Monitor
Beam Profile Monitor
Beam Profile Monitor

## Slide 6: Why study beam instabilities?
What is a beam instability?
  A beam becomes unstable when a moment of its distribution exhibits an exponential growth (e.g. mean positions <x>, <y>, <z>, standard deviations sx, sy, sz, etc.) – resulting into beam loss or emittance growth!
Why study beam instabilities?
  The onset of a beam instability usually determines the maximum beam intensity that a machine can store/accelerate (performance limitation)
Typical situation
  A beam centroid instability appears when the intensity is raised above a certain threshold
  The threshold can be optimized by an accurate choice of the machine settings
z
y
x

## Slide 7: Why study beam instabilities?
What is a beam instability?
  A beam becomes unstable when a moment of its distribution exhibits an exponential growth (e.g. mean positions <x>, <y>, <z>, standard deviations sx, sy, sz, etc.) – resulting into beam loss or emittance growth!
Why study beam instabilities?
  The onset of a beam instability usually determines the maximum beam intensity that a machine can store/accelerate (performance limitation)
  Understanding the type of instability limiting the performance, and its underlying mechanism, is essential because it:
    Allows identifying the source and possible measures to mitigate/suppress the effect
    Allows dimensioning an active feedback system to prevent the instability

## Slide 8: Types of beam instabilities
Beam instabilities occur in both linear and circular machines
  Longitudinal plane (z,d)
  Transverse plane (x,y,x’,y’)
Beam instabilities can affect the beam on different scales
  Cross-talk between bunches
    The unstable motion of subsequent bunches is coupled
    The instability is consequence of another mechanism that builds up along the bunch train
  Single bunch effect
  Coasting beam instabilities

## Slide 9: Example of multi-bunch instability
They can affect the beam on different scales
  Cross-talk between bunches
    The unstable motion of subsequent bunches is coupled
    The instability is consequence of another mechanism that builds up along the bunch train
  Single bunch effect

## Slide 10: Example of multi-bunch instability
They can affect the beam on different scales
  Cross-talk between bunches
    The unstable motion of subsequent bunches is coupled
    The instability is consequence of another mechanism that builds up along the bunch train
  Single bunch effect

## Slide 11: Example of single bunch instability
They can affect the beam on different scales
  Cross-talk between subsequent bunches
    The instability builds up along a bunch train
    The instability is consequence of another mechanism that builds up along the bunch train
  Single bunch effect

## Slide 12: Instability loop
Multi-bunch beam
s
Interaction with the external environment
Equations of motion of the beam particles
Additional electromagnetic field acting on the beam, besides RF and external magnetic fields

## Slide 13: Instability loop
Multi-bunch beam
s
Interaction with the external environment
Equations of motion of the beam particles
Additional electromagnetic field acting on the beam, besides RF and external magnetic fields
Noise

## Slide 14: Instability loop
Multi-bunch beam
s
Interaction with the external environment
Equations of motion of the beam particles
Additional electromagnetic field acting on the beam, besides RF and external magnetic fields
Noise

## Slide 15: Some examples of beam-environment interaction
Interaction of the beam with the external environment
Beam self-fields
  Set of Maxwell’s equations with
    The beam as the source term
    Boundary conditions given by the accelerator component in which the beam propagates
Fields from another beam
  Set of Maxwell’s equations with
    The other beam as the source term
    Boundary conditions given by the chamber in which the encounter between the beams takes place
The electron/ion cloud
  Electron/ion production and accumulation
  Poisson’s equation with
    The electron cloud as the source term
    Boundary conditions given by the chamber in which the electron cloud builds up
Additional electromagnetic field acting on the beam, besides RF and external magnetic fields

## Slide 16: Electro-magnetic beam-environment interaction
Interaction of the beam with the external environment
Beam self-fields
  Set of Maxwell’s equations with
    The beam as the source term
    Boundary conditions given by the accelerator component in which the beam propagates
Need of a mathematical framework to describe the effects of the self-induced fields on the beam
Time domain: Wake fields
Frequency domain: Beam coupling impedances

## Slide 17: Wake fields (general)
z
z
2b
z
Source, q1
Witness, q2
  While source and witness ( qi d(s-ct) ), distant by z<0, move in a perfectly conducting chamber, the witness does not feel any force (g >> 1)
  When the source encounters a discontinuity (e.g., transition, device), it produces an electromagnetic field, which trails behind (wake field)
    The source loses energy
    The witness feels a net force all along an effective length of the structure, L
L

## Slide 18: Wake fields (general)
2b
Source, q1
Witness, q2
L
  Not only geometric discontinuities cause electromagnetic fields trailing behind sources traveling at light speed.
  For example, a pipe with finite conductivity causes a delay in the induced currents, which also produces delayed electromagnetic fields
    No ringing, only slow decay
    The witness feels a net force all along an effective length of the structure, L
  In general, also electromagnetic boundary conditions other than PEC can be the origin of wake fields.
z
Notes: This is like a Green function, we need to define which is the pulse response (in time domain), in which we are interested!

## Slide 19: 1. The longitudinal plane
z
dp/p0

## Slide 20: Longitudinal wake function: definition
2b
z
Source, q1
Witness, q2
L
Notes: This is like a Green function, we need to define which is the pulse response (in time domain), in which we are interested!

## Slide 21: Longitudinal wake function: properties
  The value of the wake function in 0, W||(0), is related to the energy lost by the source particle in the creation of the wake
  W||(0)>0 since DE1<0
  W||(z) is discontinuous in z=0 and it vanishes for all z>0 because of the ultra-relativistic approximation
W||(z)
z

## Slide 22: The energy balance
  In the global energy balance, the energy lost by the source splits into
    Electromagnetic energy of the modes that remain trapped in the object
      Partly dissipated on lossy walls or into purposely designed inserts or HOM absorbers
      Partly transferred to following particles (or the same particle over successive turns), possibly feeding into an instability!
    Electromagnetic energy of modes that propagate down the beam chamber (above cut-off), which will be eventually lost on surrounding lossy materials
What happens to the energy lost by the source?

## Slide 23: The energy balance
  In the global energy balance, the energy lost by the source splits into
    Electromagnetic energy of the modes that remain trapped in the object
      Partly dissipated on lossy walls or into purposely designed inserts or HOM absorbers
      Partly transferred to following particles (or the same particle over successive turns), possibly feeding into an instability!
    Electromagnetic energy of modes that propagate down the beam chamber (above cut-off), which will be eventually lost on surrounding lossy materials
What happens to the energy lost by the source?
  The energy loss is very important because
    It causes beam induced heating of the beam environment (damage, outgassing)
    It feeds into both longitudinal and transverse instabilities through the associated EM fields

## Slide 24: Longitudinal impedance
  The wake function of an accelerator component is basically its Green function in time domain (i.e., its response to a pulse excitation)
    Very useful for macroparticle models and simulations, because it can be used to describe the driving terms in the single particle equations of motion!
  We can also describe it as a transfer function in frequency domain
  This is the definition of longitudinal beam coupling impedance of the element under study
[W]
[W/s]

## Slide 25: Longitudinal impedance: resonator
W||
Re[Z||]
Im[Z||]
T=2p/wr
wr
  The frequency wr is related to the oscillation of Ez, and therefore to the frequency of the mode excited in the object
  The decay time depends on how quickly the stored energy is dissipated (quantified by a quality factor Q)

## Slide 26: Longitudinal impedance: resonator
W||
Re[Z||]
Im[Z||]
  In general, the impedance will be composed of several of these resonator peaks
  Other contributors to the global impedance can also have different shapes, e.g. the resistive wall

## Slide 27: Longitudinal wake & impedance Equations of the resonator

## Slide 28: Longitudinal impedance: cavity
  A more complex example: a simple pill-box cavity with walls having finite conductivity
  Several modes can be excited
    Below the pipe cut-off frequency the width of the peaks is only determined by the finite conductivity of the walls
    Above, losses also come from propagation in the chamber
Re[Z||]
Im[Z||]
Note W||(0)<0, CST uses opposite convention!!

## Slide 29: Longitudinal impedance: cavity
  Evolution of the electromagnetic fields (Ez) in the cavity while and after the beam has passed

## Slide 30: Single bunch effects
W||
Re[Z||]
Im[Z||]

## Slide 31: Single bunch effects
W||

## Slide 32: Multi bunch effects
Re[Z||]
Im[Z||]

## Slide 33: Multi bunch effects
W||

## Slide 34: Multi bunch effects
Dz

## Slide 35: Single bunch vs. Multi bunch
  A short-lived wake, decaying over the length of one bunch, can only cause intra-bunch (head-tail) coupling
  It can be therefore responsible for single bunch instabilities
W||
Re[Z||]
Im[Z||]

## Slide 36: Single bunch vs. Multi bunch
  A long-lived wake field, decaying over the length of a bunch train or even more than a turn, causes bunch-to-bunch or multi-turn coupling
  It can be therefore responsible for multi-bunch or multi-turn instabilities
Re[Z||]
Im[Z||]
W||

## Slide 37
Detailed calculations:
  Energy loss
  Robinson instability
Qualitative descriptions:
  Coupled bunch instabilities
  Single bunch modes
[1] “Physics of Collective Beam Instabilities in High Energy Accelerators”, A. W. Chao

## Slide 38: Energy loss of a bunch (single pass)
  The energy kick DE(z) on each particle e in the witness slice l(z)dz is the integral of the contributions from the wakes left behind by all the preceding el(z’)dz slices (sources)
  The total energy loss DE of the bunch can then be obtained by integrating DE(z) l(z) over the full bunch extension
Bunch head
Bunch tail

## Slide 39: Energy loss of a bunch (multi-pass)
  The total energy loss DE of the bunch can still be obtained by integrating DE(z) over the full bunch extension
  DE(z) this time also includes contributions from all previous turns, spaced by multiples of the ring circumference C

## Slide 40: Energy loss per turn: stable phase shift
  The RF system has to compensate for the energy loss by imparting a net acceleration to the bunch
  Therefore, the bunch readjusts to a new equilibrium distribution in the bucket and moves to a synchronous angle DFs
Above transition
Below transition

## Slide 41: Example Gaussian bunch and power loss with a broad-band resonator impedance
can be calculated with Z||(w) = Z||Res(w) from previous slide in the two limiting cases
Need to expand Re[Z||(w)] for small w
Can assume |l(w)| constant over Re[Z||(w)]

## Slide 42: Single particle equations of the longitudinal motion in presence of wake fields
  The single particle in the witness slice l(z)dz will feel the force from the RF, from the bunch own space charge, and that associated to the wake
  The wake contribution can extend to several turns
Bunch head
Bunch tail
External RF
Wake fields

## Slide 43: The Robinson instability
  To illustrate the Robinson instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear synchrotron oscillations in absence of the wake forces)
    The bunch additionally feels the effect of a multi-turn wake
z
dp/p0
Unperturbed: the bunch executes synchrotron oscillations at ws

## Slide 44: The Robinson instability
z
dp/p0
The perturbation changes ws
The perturbation also changes the oscillation amplitude
Unstable motion
  To illustrate the Robinson instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear synchrotron oscillations in absence of the wake forces)
    The bunch additionally feels the effect of a multi-turn wake

## Slide 45: The Robinson instability
z
dp/p0
The perturbation also changes the oscillation amplitude
Damped motion
  To illustrate the Robinson instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear synchrotron oscillations in absence of the wake forces)
    The bunch additionally feels the effect of a multi-turn wake

## Slide 46: The Robinson instability
We assume that the wake can be linearized on the scale of a synchrotron oscillation
  To illustrate the Robinson instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear synchrotron oscillations in absence of the wake forces)
    The bunch additionally feels the effect of a multi-turn wake

## Slide 47: The Robinson instability
  The term S W||(kC) only contributes to a constant term in the solution of the equation of motion, i.e. the synchrotron oscillation will be executed around a certain z0 and not around 0. This term represents the stable phase shift that compensates for the energy loss
  The dynamic term proportional to z(t)-z(t-kT0) ≈kT0dz/dt will introduce a “friction” term in the equation of the oscillator, which can lead to instability!

## Slide 48: The Robinson instability
  We assume a small deviation from the synchrotron tune
  Re(W - ws)  Synchrotron tune shift
  Im(W - ws)  Growth/damping rate, only depends on the dynamic term, if it is positive there is an instability!
x
x
Complex frequency shift

## Slide 49: The Robinson instability
Re[Z||]
Im[Z||]
wr ≈ hw0
  We assume the impedance to be peaked at a frequency wr close to hw0 >> ws (e.g. RF cavity fundamental mode or HOM)
  Only two dominant terms are left in the summation at the RHS of the equation for the growth rate
  Stability requires that h and D[Re Z||(hw0)] have different signs
Stability criterion 

## Slide 50: The Robinson instability
Stability criterion 
 | wr < hw0 | wr > hw0
Above transition (h>0) | stable | unstable
Below transition (h<0) | unstable | stable

## Slide 51: The Robinson instability
  Other types of impedances can also cause instabilities through the Robinson mechanism
  However, a smooth broad-band impedance with no narrow structures on the w0 scale cannot give rise to an instability
    Physically, this is clear, because the absence of structure on w0 scale in the spectrum implies that the wake has fully decayed in one turn time and the driving term in the equation of motion also vanishes

## Slide 52: Other longitudinal instabilities
The Robinson instability occurs for a single bunch under the action of a multi-turn wake field
  It contains a term of coherent synchrotron tune shift
  It results into an unstable rigid bunch dipole oscillation
  It does not involve higher order moments of the bunch longitudinal phase space distribution
Other important collective effects can affect a bunch in a beam
  Potential well distortion (resulting in synchronous phase shift, bunch lengthening or shortening, synchrotron tune shift/spread)
  Coupled bunch instabilities
  High intensity single bunch instabilities (e.g. microwave instability)
  Coasting beam instabilities (e.g. negative mass instability)
To be able to study these effects we would need to resort to a more detailed description of the bunch(es)
  Vlasov equation (kinetic model)
  Macroparticle simulations

## Slide 53: Coupled bunch modes
M bunches can exhibit M different modes of coupled rigid bunch oscillations in the longitudinal plane
z
Mode 0

## Slide 54: Coupled bunch modes
M bunches can exhibit M different modes of coupled rigid bunch oscillations in the longitudinal plane
z
Mode 1

## Slide 55: Coupled bunch modes
M bunches can exhibit M different modes of coupled rigid bunch oscillations in the longitudinal plane
Any rigid coupled bunch oscillation can be decomposed into a combination of these basic modes
z
Mode 0

## Slide 56: Coupled bunch modes
z
Mode 1
M bunches can exhibit M different modes of coupled rigid bunch oscillations in the longitudinal plane
Any rigid coupled bunch oscillation can be decomposed into a combination of these basic modes

## Slide 57: Coupled bunch modes
M bunches can exhibit M different modes of coupled rigid bunch oscillations in the longitudinal plane
Any rigid coupled bunch oscillation can be decomposed into a combination of these basic modes
This modes can become unstable under the effect of long range wake fields
z
Mode 2

## Slide 58: Single bunch modes
In a similar fashion, a single bunch exhibits a double infinity of natural modes of oscillation, with rather complicated phase space portraits.
Whatever perturbation on the bunch phase space distribution can be expanded as a series of these modes
Oscillation modes as observed at a wall current monitor

## Slide 59: Single bunch modes
In a similar fashion, a single bunch exhibits a double infinity of natural modes of oscillation, with rather complicated phase space portraits.
Whatever perturbation on the bunch phase space distribution can be expanded as a series of these modes
One of these modes or a combination of them can become unstable under the effect of a short range wake field
In particular, the frequencies of these modes shift with intensity, and two of the modes can merge above a certain threshold, causing a microwave instability!

## Slide 60: Macroparticle simulation
We have simulated the evolution of an SPS bunch under the effect of a longitudinal broad band impedance lumped in one point of the ring
SPS ring:
Transverse  1-turn map M
Longitudinal  kick from sinusoidal voltage

## Slide 61: Macroparticle simulation
We have simulated the evolution of an SPS bunch under the effect of a longitudinal broad band impedance lumped in one point of the ring
Two different intensity values have been simulated
  Low intensity  below instability threshold, but potential well distortion is visible in terms of stable phase shift and bunch lengthening
  High intensity  above microwave instability threshold

## Slide 62: Macroparticle simulation
We have simulated the evolution of an SPS bunch under the effect of a longitudinal broad band impedance lumped in one point of the ring
Two different intensity values have been simulated
  Low intensity  below instability threshold, but potential well distortion is visible in terms of stable phase shift and bunch lengthening
  High intensity  above microwave instability threshold

## Slide 63: Conclusions (part I)
Beam instability
  Manifests itself like an exponential coherent motion resulting in beam loss or emittance blow up
  Can be caused by self induced EM fields
  Can be described in the framework of wake fields/beam coupling impedances
Longitudinal effects
  Energy loss
  Dipole instability (Robinson), excitation of coupled bunch & single bunch modes
Tomorrow  transverse wake fields/beam coupling impedances and instabilities