## Slide 1: Beam instabilities (II)
Giovanni Rumolo
in CERN Accelerator School, Advanced Level, Warsaw
Thursday 01.10.2013

## Slide 2: Summary of the first part
What is a beam instability?
  A beam becomes unstable when a moment of its distribution exhibits an exponential growth (e.g. mean positions <x>, <y>, <z>, standard deviations sx, sy, sz, etc.) – resulting into beam loss or emittance growth!
Instabilities are caused by the electro-magnetic fields trailing behind charged particles moving at the speed of light
  Origin: discontinuities, lossy materials
  Described through wake functions and beam coupling impedances
Longitudinal plane
  Energy loss and potential well distortion
    Synchronous phase shift
    Bunch lengthening/shortening, synchrotron tune shift
  Instabilities
    Robinson instability (dipole mode)
    Coupled bunch instabilities
    Single bunch instabilities

## Slide 3: 2. The transverse plane

## Slide 4: Transverse wake function: definition
2b
z
Source, q1
Witness, q2
L
  In an axisymmetric structure (or simply with a top-bottom and left-right symmetry) a source particle traveling on axis cannot induce net transverse forces on a witness particle also following on axis
  At the zero-th order, there is no transverse effect
  We need to introduce a breaking of the symmetry to drive transverse effect, but at the first order there are two possibilities, i.e. offset the source or the witness
Notes: This is like a Green function, we need to define which is the pulse response (in time domain), in which we are interested!

## Slide 5: Transverse dipolar wake function: definition
2b
z
Source, q1
Witness, q2
L
Dx1 (or Dy1)
Notes: This is like a Green function, we need to define which is the pulse response (in time domain), in which we are interested!

## Slide 6: Transverse quadrupolar wake function: definition
2b
z
Source, q1
Witness, q2
L
Dx2 (or Dy2)
Notes: This is like a Green function, we need to define which is the pulse response (in time domain), in which we are interested!

## Slide 7: Transverse dipolar wake function
  The value of the transverse dipolar wake functions in 0, Wx,y(0), vanishes because source and witness particles are traveling parallel and they can only – mutually – interact through space charge, which is not included in this framework
  Wx,y(0--)<0 since trailing particles are deflected toward the source particle (Dx1 and Dx’2 have the same sign)

## Slide 8: Transverse dipolar wake function
  The value of the transverse dipolar wake functions in 0, Wx,y(0), vanishes because source and witness particles are traveling parallel and they can only – mutually – interact through space charge, which is not included in this framework
  Wx,y(0--)<0 since trailing particles are deflected toward the source particle (Dx1 and Dx’2 have the same sign)
  Wx,y(z) has a discontinuous derivative in z=0 and it vanishes for all z>0 because of the ultra-relativistic approximation
Wx,y(z)
z

## Slide 9: Transverse quadrupolar wake function
  The value of the transverse quadrupolar wake functions in 0, WQx,y(0), vanishes because source and witness particles are traveling parallel and they can only – mutually – interact through space charge, which is not included in this framework
  WQx,y(0--) can be of either sign since trailing particles can be either attracted or deflected even more off axis (depends on geometry and boundary conditions)

## Slide 10: Transverse quadrupolar wake function
  The value of the transverse quadrupolar wake functions in 0, WQx,y(0), vanishes because source and witness particles are traveling parallel and they can only – mutually – interact through space charge, which is not included in this framework
  WQx,y(0--) can be of either sign since trailing particles can be either attracted or deflected even more off axis (depends on geometry and boundary conditions)
  Wx,y(z) has a discontinuous derivative in z=0 and it vanishes for all z>0 because of the ultra-relativistic approximation
WQx,y(z)
z

## Slide 11: Transverse impedance
  The transverse wake function of an accelerator component is basically its Green function in time domain (i.e., its response to a pulse excitation)
    Very useful for macroparticle models and simulations, because it relates source perturbations to the associated kicks on trailing particles!
  We can also describe it as a transfer function in frequency domain
  This is the definition of transverse beam coupling impedance of the element under study
[W/m]
[W/m/s]
** m-1 refers then to a transverse offset and does not represent a normalization per unit length of the structure
* linear terms retained, however coupling terms are neglected (usually small in symmetric structures)

## Slide 12: Transverse impedance: resonator
  Shape of wake function can be similar to that in longitudinal plane, determined by the oscillations of the trailing electromagnetic fields
  Contrary to longitudinal impedances, Re[Zx,y] is an odd function of frequency, while Im[Zx,y] is an even function
Re[Zx,y]
Im[Zx,y]

## Slide 13: Transverse wake & impedance Equations of the resonator

## Slide 14: Transverse impedance: kicker
  An example: magnetic kickers are usually large contributors to the transverse impedance of a machine
  It is a broad band contribution
    No trapped modes
    Losses both in vacuum chamber and ferrite (kicker heating and outgassing)
Im[Zx,y]
Re[Zx,y]
Dipolar

## Slide 15: Transverse impedance: kicker
  An example: magnetic kickers are usually large contributors to the transverse impedance of a machine
  It is a broad band contribution
    No trapped modes
    Losses both in vacuum chamber and ferrite (kicker heating and outgassing)
Im[ZQx,y]
Re[ZQx,y]
Quadrupolar

## Slide 16: Transverse impedance: kicker
  Evolution of the electromagnetic fields (Ey) in the kicker while and after the beam has passed

## Slide 17: Transverse impedance: kicker
  Evolution of the electromagnetic fields (Hx) in the kicker while and after the beam has passed

## Slide 18: Transverse impedance: resistive wall
  The case of a conductive pipe with an arbitrary number of layers with specified EM properties can be solved semi-analytically
  Layers sometimes required for impedance, but also for other reasons (e.g. coating against electron cloud or for good vacuum)
b
L = 1 m

## Slide 19: Transverse impedance: resistive wall
Source terms (displaced point charge traveling along s with speed v) in cylindrical coordinates and frequency domain:

## Slide 20: Transverse impedance: resistive wall
Source terms (displaced point charge traveling along s with speed v) in cylindrical coordinates and frequency domain:
Expansion in longitudinal modes
Expansion in azimuthal modes

## Slide 21: Transverse impedance: resistive wall
Maxwell’s equations combine into the wave equations:
We can seek solutions as expansions of longitudinal and azimuthal modes (for both E and B)

## Slide 22: Transverse impedance: resistive wall
It can be demonstrated that he components of the force on the witness charge only depends on Es

## Slide 23: Transverse impedance: resistive wall
r1
=r1
The equations for the coefficients of the azimuthal modes of Es must be solved in all the media and the conservation of the tangential components of the fields is applied at the boundaries between different layers
 E.g. ImpedanceWake2D code (N. Mounet) can calculate impedances and then wakes by inverse Fourier transform. It can deal with both round and flat structures

## Slide 24: Transverse impedance: resistive wall
  An interesting example: a 1 m long Cu pipe with radius b=2 cm and thickness t = 4mm in vacuum
b
t

## Slide 25: Transverse impedance: resistive wall
b
t
3 frequency regions of interest:
Below 0.1 kHz, impedance is basically purely imaginary, EM field is shielded by image charges  Indirect space charge

## Slide 26: Transverse impedance: resistive wall
b
t
3 frequency regions of interest:
Between 10 kHz and 1 THz, the EM field is fully attenuated in the Cu layer and the impedance is like the one calculated assuming infinitely thick wall

## Slide 27: Transverse impedance: resistive wall
b
t
3 frequency regions of interest:
Between 10 kHz and 1 THz, the EM field is fully attenuated in the Cu layer and the impedance is like the one calculated assuming infinitely thick wall

## Slide 28: Transverse impedance: resistive wall
b
t
3 frequency regions of interest:
Above 1 THz, there is a resonance (100 THz region). In this region also ac conductivity should be taken into account

## Slide 29: Transverse impedance: resistive wall
b
t
Correspondingly, in time domain, the wake exhibits different behaviours in short and long range
Medium-long range
Short range
In the range of tenths of ns up to fractions of ms (e.g. bunch length to several turns for the SPS) monotonically decaying wake
From behind the source to ~1ps the wake has an oscillatory behaviour, associated to the high frequency resonance

## Slide 30: Transverse impedance: resistive wall (infinitely thick wall)
with
valid only in the range
valid in the corresponding range of frequencies
b

## Slide 31: Transverse impedance: resistive wall (infinitely thick wall)
b
a
b

## Slide 32: Transverse impedance: resistive wall (infinitely thick wall)
b
a
b
Ylongitudinal ≈ 1
Yydipolar
Yxdipolar
Yxquadrupolar
Yyquadrupolar

## Slide 33: Single particle equations of the transverse motion in presence of dipolar wake fields
  The single particle in the witness slice l(z)dz will feel the external focusing forces and that associated to the wake in s0
  Space charge here neglected
  The wake contribution can extend to several turns
Bunch head
Bunch tail
External Focusing
Wake fields

## Slide 34: Beam deflection kick
x0
x
y
Off-axis traversal of symmetric chamber
x
y
Traversal of asymmetric chamber
or

## Slide 35: Beam deflection kick
x0
x
y
Off-axis traversal of symmetric chamber
x
y
Traversal of asymmetric chamber
or
  The beam deflection kicks
    Are the transverse equivalent of the energy loss in the longitudinal plane
    Can be responsible for intensity dependent orbit variations
    Cause z-dependent orbits and can determine tilted equilibrium bunch distributions for long bunches

## Slide 36: The Rigid Bunch Instability
  To illustrate the rigid bunch instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear betatron oscillations in absence of the wake forces)
    Longitudinal motion is neglected
    Smooth approximation  constant focusing + distributed wake
  In a similar fashion as was done for the Robinson instability in the longitudinal plane we want to
    Calculate the betatron tune shift due to the wake
    Derive possible conditions for the excitation of an unstable motion

## Slide 37: The Rigid Bunch Instability
  To illustrate the rigid bunch instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear betatron oscillations in absence of the wake forces)
    Longitudinal motion is neglected
    Smooth approximation  constant focusing + distributed wake
Comes from the definition of Zy

## Slide 38: The Rigid Bunch Instability
  We assume a small deviation from the betatron tune
  Re(W - wb)  Betatron tune shift
  Im(W - wb)  Growth/damping rate, if it is positive there is an instability!

## Slide 39: The Rigid Bunch Instability
Re[Zy]
Im[Zy]
wr ≈ hw0
  We assume the impedance to be peaked at a frequency wr close to hw0 (e.g. RF cavity fundamental mode or HOM)
  Defining the tune ny=ny + Dby with -0.5<Dby<0.5, we can easily express the only two leading terms left in the summation at the RHS of the equation for the growth rate

## Slide 40: The Rigid Bunch Instability
  We assume the impedance to be peaked at a frequency wr close to hw0 (e.g. RF cavity fundamental mode or HOM)
  Defining the tune ny=ny + Dby with -0.5<Dby<0.5, we can easily express the only two leading terms left in the summation at the RHS of the equation for the growth rate

## Slide 41: The Rigid Bunch Instability
 | wr < hw0 | wr > hw0
Tune above integer (Dby>0) | unstable | stable
Tune below integer (Dby<0) | stable | unstable

## Slide 42: The Rigid Bunch Instability
  We assume the impedance to be of resistive wall type, i.e. strongly peaked in the very low frequency range ( 0)
  Using the same definitions for the tune as before, we can easily express the only two leading terms left in the summation at the RHS of the equation for the growth rate
Re [Zy]

## Slide 43: The Rigid Bunch Instability
  Using the same definitions for the tune as before, we can easily express the only two leading terms left in the summation at the RHS of the equation for the growth rate
Re [Zy]
Always stable

## Slide 44: The Rigid Bunch Instability
  Using the same definitions for the tune as before, we can easily express the only two leading terms left in the summation at the RHS of the equation for the growth rate
Re [Zy]
Always unstable

## Slide 45: The Rigid Bunch Instability
  Using the same definitions for the tune as before, we can easily express the only two leading terms left in the summation at the RHS of the equation for the growth rate
Re [Zy]
Always unstable
This is the reason why most of the running machines are usually operated with a fractional part of the tunes below 0.5!
In practice, tunes above the half integer can be used, if the resistive wall instability is Landau damped (refer to W. Herr’s lectures!) or efficiently suppressed with a feedback system

## Slide 46: The Strong Head Tail Instability (aka Transverse Mode Coupling Instability)
  To illustrate TMCI we will need to make use of some simplifications:
    The bunch is represented through two particles carrying half the total bunch charge and placed in opposite phase in the longitudinal phase space
    They both feel external linear focusing in all three directions (i.e. linear betatron focusing + linear synchrotron focusing).
    Zero chromaticity (Q’x,y=0)
    Constant transverse wake left behind by the leading particle
    Smooth approximation  constant focusing + distributed wake
  We will
    Calculate a stability condition (threshold) for the transverse motion
    Have a look at the excited oscillation modes of the centroid

## Slide 47: The Strong Head Tail Instability (aka Transverse Mode Coupling Instability)
  To illustrate TMCI we will need to make use of some simplifications:
    The bunch is represented through two particles carrying half the total bunch charge and placed in opposite phase in the longitudinal phase space
    They both feel external linear focusing in all three directions (i.e. linear betatron focusing + linear synchrotron focusing)
    Zero chromaticity (Q’x,y=0)
    Constant transverse wake left behind by the leading particle
    Smooth approximation  constant focusing + distributed wake
z
dp/p0
z
Wy
-W0
Particle 1 (+Ne/2)
Particle 2 (+Ne/2)

## Slide 48: The Strong Head Tail Instability (aka Transverse Mode Coupling Instability)
  To illustrate TMCI we will need to make use of some simplifications:
    The bunch is represented through two particles carrying half the total bunch charge and placed in opposite phase in the longitudinal phase space
    They both feel external linear focusing in all three directions (i.e. linear betatron focusing + linear synchrotron focusing)
    Zero chromaticity (Q’x,y=0)
    Constant transverse wake left behind by the leading particle
    Smooth approximation  constant focusing + distributed wake
z
dp/p0
z
Wy
-W0
Particle 1 (+Ne/2)
Particle 2 (+Ne/2)

## Slide 49: The Strong Head Tail Instability (aka Transverse Mode Coupling Instability)
  During the first half of the synchrotron motion, particle 1 is leading and executes free betatron oscillations, while particle 2 is trailing and feels the defocusing wake of particle 1

## Slide 50: The Strong Head Tail Instability (aka Transverse Mode Coupling Instability)
  During the first half of the synchrotron motion, particle 1 is leading and executes free betatron oscillations, while particle 2 is trailing and feels the defocusing wake of particle 1
  During the second half of the synchrotron period, the situation is reversed

## Slide 51: The Strong Head Tail Instability (aka Transverse Mode Coupling Instability)
  We solve with respect to the complex variables defined below during the first half of synchrotron period
  y1(s) is a free betatron oscillation
  y2(s) is the sum of a free betatron oscillation plus a driven oscillation with y1(s) being its driving term
Free oscillation term
Driven oscillation term

## Slide 52: The Strong Head Tail Instability Transfer map
  Second term in RHS equation for y2(s) negligible if ws<<wb
  We can now transform these equations into linear mapping across half synchrotron period

## Slide 53: The Strong Head Tail Instability Transfer map
  In the second half of synchrotron period, particles 1 and 2 exchange their roles
  We can therefore find the transfer matrix over the full synchrotron period for both particles
  We can analyze the eigenvalues of the two particle system

## Slide 54: The Strong Head Tail Instability Stability condition
  Since the product of the eigenvalues is 1, the only condition for stability is that they both be purely imaginary exponentials
  From the second equation for the eigenvalues, it is clear that this is true only when sin(f/2)<1
  This translates into a condition on the beam/wake parameters

## Slide 55: The Strong Head Tail Instability Stability condition
  Proportional to p0  bunches with higher energy tend to be more stable
  Proportional to ws  the quicker is the longitudinal motion within the bunch, the more stable is the bunch
  Inversely proportional to by  the effect of the impedance is enhanced if the kick is given at a location with large beta function
  Inversely proportional to the wake per unit length along the ring, W0/C  a large integrated wake (impedance) lowers the instability threshold

## Slide 56: The Strong Head Tail Instability Mode frequencies
The evolution of the eigenstates follows:
Eigenfrequencies:
They shift with increasing intensity
l = 0
l = -1
Unstable region

## Slide 57: The Strong Head Tail Instability Mode frequencies
The evolution of the eigenstates follows:
Eigenfrequencies:
They shift with increasing intensity
l = 0
l = -1
That’s the reason why this type of instability is called Transverse Mode Coupling Instability!
Unstable region

## Slide 58: The Strong Head Tail Instability Why TMCI?
  For a real bunch, modes exhibit a more complicated shift pattern
  The shift of the modes can be calculated via Vlasov equation or can be found through macroparticle simulations
Simplified calculation for a short bunch
Full calculation for a relatively long SPS bunch (red lines) + macroparticle simulation (white traces)

## Slide 59: The Strong Head Tail Instability Experimental observation
SPS MDs in 2013

## Slide 60: The Strong Head Tail Instability Experimental observation
SPS MDs in 2013

## Slide 61: The Head Tail Instability
  To illustrate the head-tail instability we will need to make use of some simplifications:
    The bunch is represented through two particles carrying half the total bunch charge and placed in opposite phase in the longitudinal phase space
    They both feel external linear focusing in all three directions (i.e. linear betatron focusing + linear synchrotron focusing).
    Chromaticity is different from zero (Q’x,y≠0)
    Constant transverse wake left behind by the leading particle
    Smooth approximation  constant focusing + distributed wake
  We can
    Show that this system is intrinsically unstable
    Calculate the growth time of the excited oscillation modes

## Slide 62: The Head Tail Instability Equations of motion
  As for the TMCI, during the first half of the synchrotron motion, particle 1 is leading and executes free betatron oscillations, while particle 2 is trailing and feels the defocusing wake of particle 1
  During the second half of the synchrotron period, the situation is reversed
Difference!  now the frequency of free oscillation is modulated by the momentum spread, d(s)

## Slide 63: The Head Tail Instability Oscillation modes
  Similarly to the solution for the Strong Head Tail Instability, we obtain the transport map
Complex number!
+ mode is “in-phase” mode  the two particles oscillate in phase (wb)
- mode is “out-phase” mode  the two particles oscillate in opposition of phase (wb ± ws)
Weak beam intensity:

## Slide 64: The Head Tail Instability Growth/damping time
  Inversely proportional to p0  bunches with higher energy tend to be less affected by impedances
  Proportional to N  the more intense is the bunch, the more sensitive it is
  Proportional to bunch length  this depends on the chosen shape of the wake
  Proportional to xy  higher chromaticity enhances the head-tail effect
  Inversely proportional to h  faster synchrotron motion stabilizes (lowest rise times close to transition crossing!)
  Proportional to the wake per unit length along the ring, W0/C  a large integrated wake (impedance) gives a stronger effect

## Slide 65: The Head Tail Instability Growth/damping time
 | xy>0 | xy<0
Above transition (h>0) | damped | unstable
Below transition (h<0) | unstable | damped
Mode 0 (+)
 | xy>0 | xy<0
Above transition (h>0) | unstable | damped
Below transition (h<0) | damped | unstable
Mode 1 (–)

## Slide 66: The Head Tail Instability
The head-tail instability is unavoidable in the two-particle model
  Either mode 0 or mode 1 is unstable
  Growth/damping times are in all cases identical
Fortunately, the situation is less dramatic in reality
  The number of modes increases with the number of particles we consider in the model (and becomes infinite in the limit of a continuous bunch)
  The instability conditions for mode 0 remain unchanged, but all the other modes become unstable with much longer rise times when mode 0 is stable
 | xy>0 | xy<0
Above transition (h>0) | damped | unstable
Below transition (h<0) | unstable | damped
 | xy>0 | xy<0
Above transition (h>0) | unstable | damped
Below transition (h<0) | damped | unstable
Mode 0
All modes >0

## Slide 67: The Head Tail Instability
The head-tail instability is unavoidable in the two-particle model
  Either mode 0 or mode 1 is unstable
  Growth/damping times are in all cases identical
Fortunately, the situation is less dramatic in reality
  The number of modes increases with the number of particles we consider in the model (and becomes infinite in the limit of a continuous bunch)
  The instability conditions for mode 0 remain unchanged, but all the other modes become unstable with much longer rise times when mode 0 is stable
  Therefore, the bunch can be in practice stabilized by using the settings that make mode 0 stable (x<0 below transition and x>0 above transition) and relying on feedback or Landau damping (refer to W. Herr’s lectures) for the other modes
To be able to study these effects we would need to resort to a more detailed description of the bunch
  Vlasov equation (kinetic model)
  Macroparticle simulations

## Slide 68: A glance into the head-tail modes
Different transverse head-tail modes correspond to different parts of the bunch oscillating with relative phase differences. E.g.
  Mode 0 is a rigid bunch mode
  Mode 1 has head and tail oscillating in counter-phase
  Mode 2 has head and tail oscillating in phase and the bunch center in opposition

## Slide 69: A glance into the head-tail modes (as seen at a wide-band BPM)
 l=0 
Q’=0
Q’≠0
 l=1 
 l=2 

## Slide 70: A glance into the head-tail modes (experimental observations)
The mode that gets first excited in the machine depends on
  The spectrum of the exciting impedance
  The chromaticity setting
Head-tail instabilities are a good diagnostics tool to identify and quantify the main impedance sources in a machine

## Slide 71: Macroparticle simulation
We have simulated the evolution of a long PS bunch under the effect of a transverse resistive wall impedance lumped in one point of the ring
We have used parameters at injection (below transition!) and three different chromaticity values: xx,y= ±0.15, -0.3
PS ring:
Transverse  1-turn map M with chromaticity
Longitudinal  kick from sinusoidal voltage
Re[Zx,y]
Im[Zx,y]

## Slide 72: Macroparticle simulation
We have simulated the evolution of a long PS bunch under the effect of a transverse resistive wall impedance lumped in one point of the ring
We have used parameters at injection (below transition!) a chromaticity values: xx,y= 0.15

## Slide 73: Macroparticle simulation
We have simulated the evolution of a long PS bunch under the effect of a transverse resistive wall impedance lumped in one point of the ring
We have used parameters at injection (below transition!) a chromaticity values: xx,y= -0.15

## Slide 74: Macroparticle simulation
We have simulated the evolution of a long PS bunch under the effect of a transverse resistive wall impedance lumped in one point of the ring
We have used parameters at injection (below transition!) a chromaticity values: xx,y= -0.3

## Slide 75: Conclusions
A particle beam can be driven unstable by its interaction with its own induced EM fields
  Longitudinal, transverse
  Multi-bunch, single bunch
Simplified models within the wake/impedance framework can be adopted to explain the mechanism of the instability
  Stability criteria involving beam/machine parameters
  Growth/damping times
More sophisticated tools are necessary to describe in deeper detail the beam instabilities (kinetic theory, macroparticle simulations)

## Slide 76: Fortunately ….
In real life beam stability is eased by some mechanisms so far not included in our simplified linearized models
  Spreads and nonlinearities stabilize (Landau damping, refer to W. Herr’s lecture)
    Longitudinal: momentum spread, synchrotron frequency spread
    Transverse: chromaticity, betatron tune spreads (e.g from machine nonlinearities, enhanced with purposely higher order fields)
  Active feedback systems are routinely employed to control/suppress instabilities
    Coherent motion is detected (pick-up) and damped (kicker) before it can degrade the beam
    Sometimes bandwidth/power requirements can be very stringent
  Impedance localization and reduction techniques are applied to old accelerators as well as for the design of new accelerators to extend their performance reach!

## Slide 77: Thank you for your attention Many thanks to H. Bartosik, G. Iadarola, K. Li, N. Mounet, B. Salvant, R. Tomás, C. Zannini for material, discussions, suggestions, inspiration, review, help & support and to A. Chao for his book!

## Slide 78: The Head Tail Instability Equations of motion
  Let’s first write the solution without wake field assuming a linear synchrotron motion and particles in opposite phase (z1=-z2)
  It is already clear that head and tail of the bunch exhibit a phase difference given by the chromatic term
is the head-tail phase shift

## Slide 79: The Head Tail Instability Equations of motion
  The free oscillation is the correct solution for y1(s) in the first half synchrotron period
  For y2(s) we assume a similar type of solution, allowing for a slowly time varying coefficient
  Substituting into the equation of motion this yields

## Slide 80: The Head Tail Instability Transfer map
  For small head-tail shifts, we can expand the exponential in Taylor series and find an expression for y2(s)
  We can write a transfer map over the first half of synchrotron period in the same form as was done for the study of the TMCI
  This time ϒ is a complex parameter!