## Slide 1: Timing and Synchronization
H. Schlarb
DESY
  Outline:
  Introduction / Motivation
  Jitter source for beam arrival times
  Microwave properties and components
  RF Controls
  Synchronization references
  Beam feedbacks for FELs

## Slide 2
Introduction / Motivation

## Slide 3: Types of synchronization signals
There are various types of signals, frequently confused
Trigger signals (digital subsystems, CPU) ~ 100 ps
(10-100Hz)
Clocks (digital subsystems, ADC, DAC, CPU) ~ 5–20 ps
(1-100MHz)
Analog (RF phase reference, VM, LO) ~ 50fs – 1ps
(~0.1-10 GHz)
Optical (laser, diagnostics, experiment) < 10 fs
  e.g. laser pulse train
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 4: Scope of precision synchronization
Synchronization reach into many different physics/engineering
disciplines and requires wide range of technologies
Radio Frequency:
different types of oscillators (quartz, SAW, dielectric)
phase detectors / mixer / multiplier /divider
low noise amplifier / limiting amplifier / filters / direction couplers
cables / connectors / PCB design / waveguides / RF structure / LLRF / HLRF
Optics & Lasers:
laser oscillator/pulse shaping/amplification/wavelength conversion
fiber optics / fiber optics devices / opto-electronic devices / photo-detection
laser sources (DFB/harmonic mode-lock/passive & active mode)
non-linear optics / opto-mechanics / free-space optics / pump-modules
Environmental control:
temperature / humidity / air pressure / vibration / ground motion / EMI / EMC
Controls & control theory:
multiple feedbacks / PLL theory / automation / SISO / MIMO / …
Longitudinal electron beam dynamics
velocity / magnetic bunch compression/ harmonic cav./collective effects/….
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 5: New demands on synchronization system
Accelerator development from ns pulse duration to < 100 fs for FELs
 time scale has changed from ps to fs
 accelerator facility length scale ~ 100 – 3.5km
FELs based on exponential growth
 precision control on beam parameter required
 large bunch compression factor (tolerances LLRF!)
Beam based diagnostics on arrival & pulse shape
 important for automation
 accelerator commissioning and sub-system debugging
Pump-probe experiments (optical laser <-> FEL beam)
 knowledge on photon arrivals to one another crucial
 efficiency of experiments & dynamic range of detectors
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 6: Motivation: Pump-probe experiments
Classical setup:
Variable delay
pump
probe
Probe = flash
Pump
Shot pulses fs ps
Knowledge of time delay is crucial!
Same source
Pump pulse initiate reaction, probe pulse records current state.
Atomic / Molecular Physics/ Solid state dynamics
FELs: two different sources: FEL beam and optical laser
Comments: 1) measured at experiment  post analysis
<1 fs  dynamic range of photon arrival detector!!!
2) for small event rates  not possible
 active synchronization required

## Slide 7: New demands on synchronization system
Accelerator development from ns pulse duration to < 100 fs for FELs
 time scale has changed from ps to fs
 accelerator facility length scale ~ 100 – 3.5km
FELs based on exponential growth
 precision control on beam parameter required
 large bunch compression factor (tolerances LLRF!)
Beam based diagnostics on arrival & pulse shape
 important for automation
 accelerator commissioning and sub-system debugging
Pump-probe experiments (optical laser <-> FEL beam)
 knowledge on photon arrivals to one another crucial
 efficiency of experiments & dynamic range of detectors
Seeding & slicing and bunch manipulation
 essential for success
 opens new opportunities for FEL mode and FEL pulse control
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 8: Motivation: seeding with higher harmonics
Ti:Sa Laser
Gas cell
800nm
30nm
undulator
Separation
100kW
>1 GW
Experiment
Electron beam
Temporal overlap
New class of experiments:
Electron beam is seeded or manipulated using external laser
Timing of FEL pulse defined by now by seed (laser)
Requirements:
Temporal overlap between electron bunch & seed pulse essential ~ 10-50 fs
Particular high demands on synchronization to pump-probe laser ~ 1-5 fs
Gain 104
Generic layout of seeding a single pass FEL
Transfer line ~ 30-100m, << 10 fs
Ti:Sa Laser
t
t

## Slide 9: New demands on synchronization system
Accelerator development from ns pulse duration to < 100 fs for FELs
 time scale has changed from ps to fs
 accelerator facility length scale ~ 100 – 3.5km
FELs based on exponential growth
 precision control on beam parameter required
 large bunch compression factor (tolerances LLRF!)
Beam based diagnostics on arrival & pulse shape
 important for automation
 accelerator commissioning and sub-system debugging
Pump-probe experiments (optical laser <-> FEL beam)
 knowledge on photon arrivals to one another crucial
 efficiency of experiments & dynamic range of detectors
Seeding & slicing and bunch manipulation
 essential for success
 opens new opportunities for FEL mode and FEL pulse control
Novel accelerator technology & linear colliders
 e.g. Plasma Wake Field accelerators: wavelength ~ 10-100um
 next linear collider 30-50 km with sub-100fs synchr. demand
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 10: Arrival time of electron bunch
Electron beam transport through accelerator
E = 1 GeV 
Lorentz factor  = E/m0c2
  1 - = 0.999999869
1
22
0 m
1000 m
T = 435fs between light pulse and electron beam (T=3.33s)
Typical energy deviation E/E < 0.1%  t < 0.8 fs 
T
Typical orbit deviation x < 50m  t < 0.04 fs 
Light pulse
Elec. bunch
10 m
Defines start
Predicts arrival
 Beam transport over large (straight) distances is no problem!!!

## Slide 11: Synchronization & free running clocks
Prediction of arrival using atomic clocks
0 m
1000 m
Desired prediction accuracy ~ 10 fs:
Problem: drift during long measurement time ~ 1000sec
T
Elec. bunch
Defines start
Predicts arrival

## Slide 12: Synchronization & free running clocks
Prediction of arrival using atomic clocks
0 m
1000 m
Desired prediction accuracy ~ 10 fs:
Problem: drift during long measurement time ~ 1000sec
T
Elec. bunch
Defines start
Predicts arrival
Precision of clock: = ~ 10-17 
t
t
f
f
Resynchronization required
Best optical clocks have achieved df/f ~ 10-18
Correspond s to loss of ~1sec since big bang (4e17sec)
But by far not good enough of longer time scales &
very expensive / labor intensive

## Slide 13: Synchronization & free running clocks
Prediction of arrival using atomic clocks
0 m
1000 m
Desired prediction accuracy ~ 10 fs:
Problem: drift during long measurement time ~ 1000sec
T
Elec. bunch
Defines start
Predicts arrival
Precision of clock: = ~ 10-17 
t
t
f
f
Resynchronization required
Resynchronization requires constant propagation time of signal 
Detector with femtosecond accuracy (short & long term) 
Light pulse
?

## Slide 14: Synchronization & resynchronized clocks
Laser pulses transported in length-stabilized optical fibers
What are the requirements for the optical reference source?
0 m
1000 m
t
Elec. bunch
Fiber laser provides excellent stability on short time scales 
But drifts due to environmental changes over long time scales 
tl - tr
PZT
t
t
f
f
Desired length stabilization ~ 1m (3fs)  = ~ 310-10 
Round trip time t ~ 10s (ng=1.5)
x
x
Fiber laser ~ 216MHz
Optical fiber
Mirror
Light pulse
?
Low noise
RF Osc.
Rubidium
Clock
Stability (1s)
f/f ~ 10-11
Aging (year)
f/f ~ 510-10
Requires locking of the fiber laser to an atomic clock (Rb sufficient) 

## Slide 15
Jitter source for
beam arrival times

## Slide 16: Sources of timing jitter in linear accelerator
RF gun
Accelerator
Undulator

Photo-cathode
laser
Pump-probe
laser
Long/transverse beam quality
Arrival time jitter at entrance to undulator
Sources of timing jitter (uncorrelated): t = [ (wj j)2 ]1/2
  Photo-cathode laser w ~ 40-60%
  RF phase of RF gun (non-relativistic electrons) w ~ 60-40%
  Seed and Pump-probe laser w ~ 100%
Seed
laser

## Slide 17: Sources of timing jitter in linear accelerator
RF gun
Accelerator
Undulator

bunch compressor
Main Linac
Photo-cathode
laser
Pump-probe
laser
Sources of timing jitter (uncorrelated): t = [ (wj j)2 ]1/2
  Photo-cathode laser w ~ 40-60%
  RF phase of RF gun (non-relativistic electrons) w ~ 60-40%
  Seed and Pump-probe laser w ~ 100%
Seed
laser
Vacc
Energy chirp + energy dependent path length
z/c
Long/transverse beam quality
Arrival time jitter at entrance to undulator

## Slide 18: Sources of timing jitter in linear accelerator
RF gun
Accelerator
Undulator

bunch compressor
Main Linac
Photo-cathode
laser
Pump-probe
laser
Sources of timing jitter (uncorrelated): t = [ (w t,I)2 ]1/2
  Photo-cathode laser w < 5%
  RF phase of RF gun (non-relativistic electrons) w < 5%
  Seed and Pump-probe laser w ~ 100%
  RF amplitude and phase w ~ 100%
Seed
laser
Timing jitter
behind BC
Voltage
XFEL: 3.3 ps/%
FLASH: 5.5ps/%
2 ps/deg
L-band
0.05 ps/ps
C=20
Phase
Incoming
compression
factor
C ~5 … 20
A/
stabilize Ipeak
THz
Long/transverse beam quality
Arrival time jitter at entrance to undulator

## Slide 19: Sources of timing jitter in linear accelerator
RF gun
Accelerator
BC1
Accelerator
A1/1
Several compressor stages
BC2
Main Linac
A2/2
R56,1/E1
R56,2/E2
Recursive case 0
Jitter from BC1 remains + additive jitter!
-5
-4
-3
-2
-1
0
1
2
3
4
5
-5
-4
-3
-2
-1
0
1
2
3
4
5
Bunch
head
Chirp E’1
wake
case1
Remark: long. wakefields helps to remove
energy chirp from first accelerator section
dE/E
z/z

## Slide 20: Microwave properties and components
Microwave properties
and components
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 21: Microwave properties and components
Microwave signal with noise
polar coordinates:
Cartesian coordinates:
See also: Enrico Rubiola FEMTO-ST Institute http://rubiola.org
Offset / modulation frequency:
Voltage spectral density:
[V2/Hz]
[1/Hz]
[rad2/Hz]
carrier
-1
-0.5
0
0.5
1
-1.5
-1
-0.5
0
0.5
1
1.5
time t/T0
signal
n
(t)
For RF sources usually the
amplitude noise spectral density
is much small than the
phase noise spectral density
S << Sϕ
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 22: Phase noise & timing jitter
Timing jitter:
Phase noise:
dBc = dB relative to carrier
10 log [|L(fm)|] dBc/Hz
IEEE standard 1139-1999
[rad2/Hz]
ϕrms= [rad]
[sec2/Hz]
Independent of carrier frequency
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 23: Microwave properties and components
Courtesy: M. Hoffmann
Phase noise spectrum is systems finger print
Thermal noise floor
S = kBT ~ -174 dBm/Hz
kB= Boltzmann constant
T = Temperature [K]
P0 = + 10dBm
Lth = 0.5*S/P0
= 187 dBc/Hz
~ f-1
~ f-3
~ f0
spurious
Inter. filter
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 24: Microwave properties and components
Courtesy: M. Hoffmann
Measurement of absolute phase noise:
Device under test
o
i
K(i- o)
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 25: Microwave properties and components
Measurement of absolute phase noise:
Courtesy: M. Hoffmann
DUT
2 statistically
independent
measurements
+ corr.
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 26: Microwave properties and components
Mixer & phase detector:
GND
RF
LO
IF
 double the frequency
+ DC offset (if f LO = f RF )
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 27: Microwave properties and components
Mixer & phase detector:
If LO and RF frequency equal  lower sideband at DC, upper sideband at 2f
If phase is 0 deg between LO and RF  amplitude detector (in phase) I
If phase is 90 deg between LO and RF  phase detector (in quadrature) Q
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 28: Microwave properties and components
Mixer & phase detector:
Passive Mixers (FET):
Active Gilbert-mixers:
+ High linearity
+ Low NF
Large LO drive needed
(additional phase noise)
- Higher LO/RF crosstalk
+ High conversion gain
+ Low LO drive needed
+ Low LO/RF crosstalk
- Normal NF
- Additional 1/f-noise
Compromise between noise and linearity :
- Intermodulation effects
- Higher harmonics
IP3
Non-linearity
Noise floor
Noise
IP2
Spurious Free
Dynamic Range (SFDRout)
Dynamic Range (DRout)
- Filtering of distortions
Filtering of distortions :
Kd = U/(ϕLO-ϕRF)  300mV/rad
Conversion loss
~ 7-10dB
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 29: Microwave properties and components
S ϕ,out = 20 log(fin/fout) + Sϕ,in
S ϕ,out = -20 log(fin/fout) + Sϕ,in
S ϕ,out = Sϕ1,in +Sϕ2,in
S ϕ,out = Sϕ,in + (AM PM)
Analog to digital:
ADC
Clock
fin, in
fclk, clk
Preserves timing fluctuations
fin, in
S ϕ,out = Sϕ,in +Sϕ,clk
Remark: IF= |(f1-f2)| << f1,f2
large gear ratio = f/IF allows for precision meas.
Remark: no IF, no gear ratio!
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 30: Microwave properties and components
Mixer preserves phase noise
Digital down conversion
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 31: RF field detector arrangements
31
ΔA/A=0.003%
Δ=0.002o
Resolution: Factor of 5 improved primarily by ADC improvements
B=1MHz
RF receiver developments & noise limitations
Noise balanced (LO/Front-end/ADC)
Intermediate frequency [10MHz, 50MHz]:
CLK
BPF
DDC
CIC Filter
Calibration
Front-End <-150dBc/Hz
LNA
LO and CLK Generation
Reference
ADC
Single Channel Receiver
ADC+ DDC -147dBc/Hz
-150dBc/Hz
AM
PM
< 0.0018°, 4fs
-150dBc/Hz
LO-Generation
Down-converter
10 ch. 16bit ADC
Integrated MicroTCA Crate system
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 32: Microwave properties and components
Reference tracking for mixer drift removal
Mixer phase drifts ~ 0.2/K
Mixer amplitude drifts ~ 0.2%/K
+ dependence on humidity on PCBs
Remark: mixer drift not equal (one PCB, temp.)
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 33: Microwave properties and components
Courtesy: K. Czuba
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 34: Phase drifts in coaxial cables
Courtesy: K. Czuba, ISE/WUT
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 35: RF signals essential for electron beam synchr.
RF signal (irrelevant how they are provide) have to transported into create system
Internal calibration scheme can be applied
Many tap points (European XFEL ~ 100-1000)
Rack and create design critical
Courtesy: K. Czuba, ISE/WUT
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 36
RF controls
RF Controls

## Slide 37: RF control of short RF pulses (NRF)
37
For RF pulse duration ~ 2-3 us
  no intra-pulse FB possible
  feed forward control define RF stability
Main factors:
  LLRF drive signal
    RF reference / PLL
    IQ modulator (vector modulator)
    Preamplifier
  Temperature stability acc. Structure < 0.01K
  Stability of HV modulator
Feedback applied Pulse-to-Pulse
  Using For/Ref/Probe signal to remove
  temp. drifts of cavities/waveguides..
  Multi-cavities  vector sum control
RF System @ SACLA
T. Inagaki, IPAC11, MOPC018
T. Ohshima, 8th Annual. ACC Society of Japan
dV/V~310-4
d ~ 0.03
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 38: RF control of long RF pulses (SRF)
38
ADC boards
LLRF CTRL
POWER
MODULE
MCH
CPU
Timing
MTCA.4 Shelf: FLASH/E-XFEL
SRF-LLRF feedback control loop
E-stability (SR-3DBC2)
800us
Energy stability
dE/E = 5E-5.
1 RF station, 8 cav.
New features obs.
Single 1nC bunch transients
7/9-pi mode instabl.
FLASH operation:
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 39
Reference distribution

## Slide 40
Synchronization - Reference distribution schemes …
Various approaches:
1) RF distribution
~
f ~ 100MHz …GHz
t f
t f
=
2) Carrier is optically
~
MZT
f ~ GHz
3) Carrier is optically + detection
f ~ 200 THz
standard
reflectometer
interferometer
~
MO
LO
4) Pulsed optical source
f ~ 5 THz
OXC
Mode locked
Laser
SLAC
FLASH
E-XFEL
SwissFEL
SLAC
FERMI
(LBNL)
SACLA
FERMI
FLASH
E-XFEL
SwissFEL
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 41
Which system is the best ????
Performance
Reliability
Costs
RF System
Pulsed system
CW optical
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 42: Synchronization – Pulsed optically, overall scheme
Narrow
Band.
Direct/
Interferometer
EOMs/
Seeding
Two color bal.
Opt. cross-corr.
End-station
Laser
MLO
MO-RF
Laser pulse
Arrival beam/laser
DWC/Kly
A &  cavity
Desired point-to-point stability ~ 10 fs
<5fs
Direct
Distribution
LO-RF
Optical link
Optical link
<5fs
<5fs
Optical link
FB
EDFL, soliton, t~200fs, f=216MHz
SESAM, P > 100mW,
phase noise < 5fs (1kHz)
Free space distribution
+ EDFA
Dispersion comp.,
Polarization contr.,
Collinear bal. opt.
cross-corr.
Other lasers
Main issue: robustness, stability and maintainability  Prototype at FLASH
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 43: Synchronization – Pulsed optically, example FLASH
Optical synchronization system @ FLASH using mode locked laser
Master Laser
~ 5fs phase noise
Link stabilization
Slop ~ 60as/mV
TiSa opt. cross-corr. ~ 5fs rms

## Slide 44: Synchronization – Pulsed optical, fiber link
216 MHz
Er-doped
fiber laser
J. Kim et al., Opt. Lett. 32, 1044-1046 (2007)
Det 1
Det 2
-
Balanced optical cross-correlator
Courtesy: F.X. Kaernter)
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 45: Synchronization – Pulsed optical, link limitations
Drifts instability of long single mode optical fiber links:
 Limitation due to Polarization Mode Dispersion (PMD)
Numerical simulation for XFEL Fibers ~ 50fs/km
Measurements fiber test bench (Hall 2) PMD ~200fs/km
In-loop
Out-of-loop
Correction
Particular critical for long links…
Options:
Active PMD compensation (large bandwidth)
Polarization Maintain Link (DCF, handling diff.)
Only Link as PM-fiber with SMF appendix
~10fs/h

## Slide 46: Synchronization – Pulsed optical, arrival monitor
uncorrelated jitter
over 4300 shots:
8.4 fs (rms)
Uses optical reference laser pulses (single shot)
Used at FLASH/FERMI/PSI
Key exp. : two BAMs 60m distance
Standard diag. at FLASH

## Slide 47
Direct conversion with photo detector (PD)
Low phase noise (to be proven at end-station)
Temperature drifts (0.4ps/C°)
AM to PM conversion (0.5-4ps/mW)
Potential for improvement
(corporation with PSI)
PD
BPF
laser pulses
frep
f = n*frep
f = n*frep
~
~
~
Time domain
Frequency domain
T = 5ns = 1/frep
Photo Detector
Bandwidth PD
frep
100fs
Phase noise
Sagnac loop interferometer
balanced optical mixer to lock RF osc.
insensitive against laser fluctuation
Very low temperature drifts
Results:
f=1.3GHz jitter & drift < 10 fs rms limited by detection
Remark: much easier at hire frequencies …
MZI based balanced RF lock
new scheme, under investigation
Synchronization – Pulsed optical, RF generation

## Slide 48
Beam based
Feedback systems
Beam based feedback systems

## Slide 49: Ultra-Fast beam based feedbacks
LLRF
LLRF
LLRF
LLRF
Large bunch spacing at FLASH (~ us) allow for intra-bunch feedbacks
Gun
ACC1
3rd
ACC2
ACC3
ACC4
ACC7
~
~
BAM
BAM
BCM
BCM
BAM
BAM
Toroid
Toroid
Toroid
Laser
LLRF

A 
A 
A 
Phase in RF-Gun Ampl. and phase ACC1&ACC39 Ampl and phase ACC23
BC2
BC3
Exit of linac
& out-of-loop
< 22 fs rms
Both intra-train FB on
MIMO controller
Repetitive pkpk deviation < 100fs
Latency of system
2011
Improved FPGA algorithm
Courtesy: S. Pfeiffer
LLRF
LLRF
LLRF
LLRF
Loop delay
System Bandwidth
2012
~ 12 fs rms
Upgrade NRF FB cavity
- Latency ~ 0.7us
- Actuator bandwidth:
NRF 0.5–1.0MHz
- Amplifier Power ~1kW
- Goal: < 5fs rms

## Slide 50: Fast beam based feedbacks & optical lock of TiSa Laser
Demonstration of synchronization for FEL users experiment
Beam based feedback using Bunch Arrival Monitor & optical lock of TiSa laser
FEL pulse arrival measured with laser based THz streaking (A. Cavalieri)
33 fs rms
Residual jitter to be
investigated
(many possible sources!)
S. Schulz, SPIE13

## Slide 51
Thanks for attention

## Slide 52: Synchronization – RF Interferometer scheme
Main issues:
Isolation (coupler)
Parasitic reflection
Limited distance
Careful adjustment (A&)
Inst. End 2013
Same scheme will be implemented for FLUTE@KIT!
Appropriate scheme
for small facilities
Cable
drift
Refl. Output
drift
X 50 reduction 10ps->200fs pkpk
X 500 can be achieved
 const.
Interferometer test setup:
Ed Cullerton, FNAL
e.g. considered for REGAE facility

## Slide 53
Early work NLC (J.Frisch), TESLA (K.Czuba), PSI (S. Hunziker)/I-TECH
Amplitude modulated optical carrier (192THz), fmod~ GHz
Piezo stretcher
Optical delay line
Optical signal
RF signal PD
Noisy RF signal at receiver
Spurious reflections
AM-PM PD conversion
Phase detector drifts
Synchronization – CW optical reflectometer
Rem: Wavelength shift
Instead of phase shifter
IPAC 2010,
primoz.lemut@i-tech.si
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 54: Synchronization – Optical Interferometer
0
0.5
1
1.5
-1
-0.5
0
0.5
1
1.5
2
2.5
3
3.5
4
1560nm
CW
fiber
laser
+50MHz
freq.
shifter
FRM
FRM
100MHz
~
RF source
f = 192THz
f = 192THz + 100MHz
ADC
clock
time
E1, E2, P
P ~ (E1 + E2)(E1 +E2)*
Gear ratio: 200THz/100MHz ~ 2e6
5 fs @200THz == 1 rad == 10ns @ 100MHz
Optical fiber length can be determined to fraction of optical wavelength
Measures phase velocity change across entire fiber
Heterodyne beat
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 55: Microwave properties and components
Mixer & phase detector:
Different response curves when based on digital elements
Example: AD8302, specially low drift, but poor phase noise!
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 56
Phase Lock Loops
Phase lock loop

## Slide 57: Microwave properties and components
Phase locked loops
Phase error e(i-o)
Rem1: PLL always has one
integrator since VCO input
controls the frequency not
the phase  do/dt =  = K0vc
Rem2: To remove phase err. offsets
due to systematic VCO frequency
errors, a second integr. is required
Laplace trans:
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 58: Microwave properties and components
Phase locked loops
Untracked phase noise
Tracked phase noise
Gain peaking
Total phase noise
Follows reference
Free running
oscillator
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 59: Synchronization – Pulsed optical
Locking low-noise microwave oscillator to laser (or visa versa)
RF Oscillator fVCO = n fr, split and delayed
X1
X2
No phase error
With phase error
See: Accelerator 2011, Highlights and Annual Report, DESY
http://www.desy.de/ueber_desy/jahresberichte/index_ger.html
Sketch of effect due to VCO phase shift
< 2.5fs (1Hz-1MHz)
Drift < 14fs pkpk (3.8fs rms)
Residual jitter
Residual drift
Out-of-loop
Out-of-loop

## Slide 60
6 parameters for energy () & bunch length ()
Typical bandwidth 10Hz @ 120 Hz rep-rate
Meas. Response fct.  FB matrix
>10Hz … dedicated FB network!
LCLS: sub. additional effort for 120Hz!
Longitudinal pulse-to-pulse feedback controls
Example: LCLS, similar FERMI /FLASH with arrival FB.
Vmon = MrespVact
Vact,n+1 = Vact,n + G(Mresp) -1Vmon,n
on demand
3-phase
6 time slots
timing system
markers
LBC = const.
acc -b = const.
Follows inj.
arrival time drift
Energy jitter due to arrival jitter
Occasional retuning X-phase
Courtesy: D. Fairley