## Slide 1: LONGITUDINAL DYNAMICS RECAP
Frank Tecker CERN, BE-OP
Advanced Accelerator Physics Course
Warsaw, 27/9-9/10/2015

## Slide 2: Summary of the 2 lectures:
Acceleration methods
Accelerating structures
Linac: Phase Stability + Energy-Phase oscillations
Circular accelerators: Cyclotron / Synchrotron
Dispersion Effects in Synchrotron
Stability and Longitudinal Phase Space Motion
Stationary Bucket
Injection Matching
Including selected topics from Introductory CAS lectures :
  Linacs – Alessandra Lombardi
  RF Systems - Erk Jensen
  Electron Beam Dynamics - Lenny Rivkin

## Slide 3
The accelerating system will depend upon the evolution of the particle velocity along the system
• electrons reach a constant velocity at relatively low energy
• heavy particles reach a constant velocity only at very high energy
-> we need different types of resonators, optimized for different velocities
Particle types and acceleration
Particle rest mass:
electron 0.511 MeV
proton 938 MeV
239U ~220000 MeV
Relativistic gamma factor:
particle kinetic energy W [MeV]
E=E0+W

## Slide 4
normalized velocity
total energy
rest energy
protons
electrons
electrons
protons
Velocity, Energy and Momentum
=> electrons almost reach the speed of light very quickly (few MeV range)
Momentum
normalized velocity
total energy
rest energy

## Slide 5: Acceleration + Energy Gain
Hence, it is necessary to have an electric field E (preferably) along the direction of the initial momentum (z),
which changes the momentum p of the particle.
In relativistic dynamics, total energy E and momentum p are linked by
The rate of energy gain per unit length of acceleration (along z) is then:
and the kinetic energy gained from the field along the z path is:
To accelerate, we need a force in the direction of motion!
Newton-Lorentz Force on a charged particle:
2nd term always perpendicular to motion => no acceleration
- V is a potential - q the charge
May the force
be with you!

## Slide 6: Electrostatic Acceleration
Electrostatic Field:
Force:
Energy gain: W = q ΔV
used for first stage of acceleration: particle sources, electron guns,
x-ray tubes
Limitation: insulation problems
maximum high voltage (~ 10 MV)
750 kV Cockroft-Walton generator at Fermilab (Proton source)
E
DV
vacuum envelope
source
Van-de-Graaf generator at MIT

## Slide 7: Methods of Acceleration: Time varying fields
The electrostatic field is limited by insulation,
the magnetic field does not accelerate.
From Maxwell’s Equations:
The electric field is derived from a scalar potential φ and a vector potential A
The time variation of the magnetic field H generates an electric field E
The solution: => time varying electric fields !
1) Induction
2) RF frequency fields
Consequence: We can only accelerate bunched beam!
or

## Slide 8: Acceleration by Induction: The Betatron
It is based on the principle of a transformer:
- primary side: large electromagnet - secondary side: electron beam.
The ramping magnetic field is used to guide particles on a circular trajectory as well as for acceleration.
Limited by saturation in iron (~300 MeV e-)
Used in industry and medicine, as they are
compact accelerators for electrons
Donald Kerst with the first betatron, invented at the University of Illinois in 1940
coil
beam
vacuum pipe
iron yoke
Bf
B
Bf
E
R
beam
side view
top view
time

## Slide 9: Radio-Frequency (RF) Acceleration
Cylindrical electrodes (drift tubes) separated by gaps and fed by a RF generator, as shown above, lead to an alternating electric field polarity
Synchronism condition L = v T/2
v = particle velocity T = RF period
D.Schulte
Similar for standing wave cavity as shown (with v≈c)
Electrostatic acceleration limited by isolation possibilities => use RF fields
Widerøe-type
structure
Animation: http://www.sciences.univ-nantes.fr/sites/genevieve_tulloue/Meca/Charges/linac.html

## Slide 10: Resonant RF Cavities
Considering RF acceleration, it is obvious that when particles get high velocities the drift spaces get longer and one looses on the efficiency. => The solution consists of using a higher operating frequency.
The power lost by radiation, due to circulating currents on the electrodes, is proportional to the RF frequency. => The solution consists of enclosing the system in a cavity which resonant frequency matches the RF generator frequency.
The electromagnetic power is now constrained in the resonant volume
Each such cavity can be independently powered from the RF generator
Note however that joule losses will occur in the cavity walls (unless made of superconducting materials)

## Slide 11: The Pill Box Cavity
From Maxwell’s equations one can derive the wave equations:
Solutions for E and H are oscillating modes, at discrete frequencies, of types TMxyz (transverse magnetic) or TExyz (transverse electric). Indices linked to the number of field knots in polar co-ordinates φ, r and z.
For l<2a the most simple mode, TM010, has the lowest frequency, and has only two field components:
Ez
Hθ

## Slide 12: The Pill Box Cavity
electric field
magnetic field
(only 1/4 shown)
TM010-mode
One needs a hole for the beam pipe – circular waveguide below cutoff

## Slide 13: Transit time factor
In the general case, the transit time factor is:
Transit time factor defined as:
0 < Ta < 1, Ta  1 for g  0, smaller ωRF
Important for low velocities (ions)
for
Simple model uniform field:
follows:
The accelerating field varies during the passage of the particle
=> particle does not always see maximum field => effective acceleration smaller
Field rotates by 360° during particle passage.

## Slide 14: The Pill Box Cavity (2)
The design of a cavity can be sophisticated in order to improve its performances:
- A nose cone can be introduced in order to concentrate the electric field around the axis
- Round shaping of the corners allows a better distribution of the magnetic field on the surface and a reduction of the Joule losses.
It also prevents from multipactoring effects (e- emission and acceleration).
A good cavity efficiently transforms the RF power into accelerating voltage.
Simulation codes allow precise calculation of the properties.

## Slide 15: Multi-Cell Cavities
Acceleration of one cavity limited => distribute power P over several cells
Each cavity receives P/n
Since the field is proportional √P, you get
1
2
3
n
P/n
P/n
P/n
P/n
Instead of distributing the power from the amplifier, one might as well couple the cavities, such that the power automatically distributes, or have a cavity with many gaps (e.g. drift tube linac).

## Slide 16: Multi-Cell Cavities - Modes
The phase relation between gaps is important!
Coupled harmonic oscillator
=> Modes, named after the phase difference between adjacent cells.
Relates to different synchronism conditions for the cell length L
0
p/2
p
2p/3
Mode | L
0 (2π) | βλ
π/2 | βλ/4
2π/3 | βλ/3
π | βλ/2

## Slide 17: Disc-Loaded Traveling-Wave Structures
When particles gets ultra-relativistic (v~c) the drift tubes become very long unless the operating frequency is increased. Late 40’s the development of radar led to high power transmitters (klystrons) at very high frequencies (3 GHz).
Next came the idea of suppressing the drift tubes using traveling waves. However to get a continuous acceleration the phase velocity of the wave needs to be adjusted to the particle velocity.
solution: slow wave guide with irises ==> iris loaded structure

## Slide 18: The Traveling Wave Case
The particle travels along with the wave, and k represents the wave propagation factor.
wave number
vφ = phase velocity v = particle velocity
If synchronism satisfied:
where Φ0 is the RF phase seen by the particle.
v = vφ and

## Slide 19: Important Parameters of Accelerating Cavities
- Shunt Impedance R
Relationship between electric field E0 and wall losses Pd
Ratio of stored energy Ws and dissipated power Pd
on the walls in one RF cycle
- Quality Factor Q
- function of the geometry and of the surface resistance of the material:
superconducting (niobium) : Q= 1010
normal conducting (copper) : Q=104
depends on - material - cavity mode - geometry
- Average Electric Field E0
Measure of the potential acceleration
Attention: Different definitions are used!

## Slide 20: Important Parameters of Accelerating Cavities (cont.)
- Fill Time tF
Exponential decay of the stored energy Ws due to losses
- standing wave cavities:
time for the field to decrease by 1/e after the cavity has been filled
measure of how fast the stored energy is dissipated on the wall
- travelling wave cavities: time needed for the electromagnetic energy to fill the cavity of length L
vg: velocity at which the energy propagates through the cavity

## Slide 21: Common Phase Conventions
For circular accelerators, the origin of time is taken at the zero crossing of the RF voltage with positive slope
Time t= 0 chosen such that:
1
f1
2
f2
For linear accelerators, the origin of time is taken at the positive crest of the RF voltage
3. I will stick to convention 1 in the following to avoid confusion

## Slide 22: Principle of Phase Stability (Linac)
Let’s consider a succession of accelerating gaps, operating in the 2π mode, for which the synchronism condition is fulfilled for a phase s .
is the energy gain in one gap for the particle to reach the next gap with the same RF phase: P1 ,P2, …… are fixed points.
If an energy increase is transferred into a velocity increase => M1 & N1 will move towards P1 => stable M2 & N2 will go away from P2 => unstable (Highly relativistic particles have no significant velocity change)
For a 2π mode, the electric field is the same in all gaps at any given time.
energy gain
late
early
Notes: Edwin McMillan of UC Berkley, and the Russian V.I. Veksler independently discovered Phase stability in 1945.

## Slide 23
The divergence of the field is zero according to Maxwell :
External focusing (solenoid, quadrupole) is then necessary
Transverse fields
focusing at the entrance and
defocusing at the exit of the cavity.
Electrostatic case: Energy gain inside the cavity leads to focusing
RF case: Field increases during passage => transverse defocusing!
A Consequence of Phase Stability

## Slide 24
- Rate of energy gain for the synchronous particle:
- Rate of change of the phase with respect to the synchronous one:
Leads finally to:
- Rate of energy gain for a non-synchronous particle, expressed in reduced variables, and :
Energy-phase Oscillations (Small Amplitude) (1)

## Slide 25
Combining the two 1st order equations into a 2nd order equation gives the equation of a harmonic oscillator:
with
Stable harmonic oscillations imply:
hence:
And since acceleration also means:
You finally get the result for the stable phase range:
VRF
cos (fs)
acceleration
synchronous phase
Energy-phase Oscillations (Small Amplitude) (2)
Slower for higher energy!

## Slide 26
DE, Dp/p
f
Emittance: phase space area including all the particles
NB: if the emittance contour correspond to a possible orbit in phase space, its shape does not change with time (matched beam)
DE, Dp/p
f
acceleration
deceleration
move
backward
move
forward
The particle trajectory in the phase space (Dp/p, f) describes its longitudinal motion.
reference
Longitudinal phase space
The energy – phase oscillations can be drawn in phase space:

## Slide 27: Longitudinal Dynamics - Electrons
Electrons injected into a TW structure designed for v=c:
at v=c remain at the injection phase.
at v<c will move from injection phase j0 to an asymptotic phase j, which depends on gradient E0 and b0 at injection.
The beam can be injected with an offset in phase, to reach the crest of the wave at b=1
Capture condition, relating gradient E0 and b0 :
Example: l=10cm → Win=150 keV for E0=8 MV/m.
In high current linacs, a bunching and pre-acceleration sections up to 4-10 MeV prepares the injection in the TW structure (that occurs already on the crest)
At relativistic velocity phase oscillations stop – the bunch is frozen longitudinally.
=> Acceleration can be at the crest of the RF for maximum energy gain.

## Slide 28: Bunching with a Pre-buncher
A long bunch coming from the gun enters an RF cavity.
The reference particle is the one which has no velocity change. The others get accelerated or decelerated, so the bunch gets an energy and velocity modulation.
After a distance L bunch gets shorter: bunching effect.
This short bunch can now be captured more efficiently by a TW structure (vϕ=c).

## Slide 29
long.
phase
space
N.Walker
Bunch compression
At ultra-relativistic energies (γ>> 1) the longitudinal motion is frozen. For linear e+/e- colliders, you need very short bunches (few 100-50µm).
Solution: introduce energy/time correlation + a magnetic chicane.
Increases energy spread in the bunch => chromatic effects => compress at low energy before further acceleration to reduce relative DE/E

## Slide 30: Longitudinal Wake Fields - Beamloading
wakefield
RF
Total
φ = 15.5º
Beam induces wake fields in cavities (in general when chamber profile changing)
⇒ decreasing RF field in cavities
(beam absorbs RF power when accelerated)
Particles within a bunch see a decreasing field ⇒ energy gain different within the single bunch
Locating bunch off-crest
at the best RF phase minimises energy spread
Example: Energy gain along the bunch in the NLC linac (TW):

## Slide 31: The Radio-Frequency Quadrupole - RFQ
Initial acceleration difficult for protons and ions at low energy (space charge, low β ⇒ short cell dimensions, bunching needed)
RFQ = Electric quadrupole focusing channel + bunching + acceleration
Alternating electric quadrupole field gives transverse focusing like magnetic focusing channel.
Does not depend on velocity!
Ideal at low β!
+
+
−
−

## Slide 32: The Radio-Frequency Quadrupole - RFQ
Opposite vanes (180º)
The vanes have a longitudinal modulation with period = bl
 this creates a longitudinal component of the electric field.
The modulation corresponds exactly to a series of RF gaps and can provide acceleration.
+
−
Adjacent vanes (90º)
RF Field excitation:
An empty cylindrical cavity can be excited on different modes.
Some of these modes have only transverse electric field (the TE modes), and one uses in particular the “quadrupole” mode, the TE210.
B-field
E-field

## Slide 33: RFQ Design + Longitudinal Phase Space
RFQ design: The modulation period can be slightly adjusted to change the phase of the beam inside the RFQ cells, and the amplitude of the modulation can be changed to change the accelerating gradient  start with some bunching cells, progressively bunch the beam (adiabatic bunching channel), and only in the last cells accelerate.
Longitudinal beam profile of a proton beam along the CERN RFQ2

## Slide 34
Summary up to here…
Acceleration by electric fields, static fields limited => time-varying fields
Synchronous condition needs to be fulfilled for acceleration
Particles perform oscillation around synchronous phase
visualize oscillations in phase space
Electrons are quickly relativistic, speed does not change use traveling wave structures for acceleration
Protons and ions
  RFQ for bunching and first acceleration
  need changing structure geometry

## Slide 35: Summary: Relativity + Energy Gain
RF Acceleration
(neglecting transit time factor)
The field will change during the passage of the particle through the cavity => effective energy gain is lower
Newton-Lorentz Force
Relativistics Dynamics
2nd term always perpendicular to motion => no acceleration

## Slide 36
Circular accelerators
Cyclotron
Synchrotron

## Slide 37
Circular accelerators: Cyclotron
Cyclotron frequency
g increases with the energy  no exact synchronism
if v  c  g  1
Synchronism condition
B = constant
wRF = constant
B
RF generator, wRF
g
Ion source
Extraction electrode
Ions trajectory
Used for protons, ions
Cyclotron Animation
Animation: http://www.sciences.univ-nantes.fr/sites/genevieve_tulloue/Meca/Charges/cyclotron.html

## Slide 38
Synchrocyclotron: Same as cyclotron, except a modulation of wRF
B = constant
  g wRF = constant
wRF decreases with time
The condition:
Allows to go beyond the non-relativistic energies
Cyclotron / Synchrocyclotron
TRIUMF 520 MeV cyclotron Vancouver - Canada
CERN 600 MeV synchrocyclotron

## Slide 39
Constant orbit during acceleration
To keep particles on the closed orbit, B should increase with time
w and wRF increase with energy
E
R
RF generator
B
RF cavity
Synchronism condition
h integer,
harmonic number:
number of RF cycles
per revolution
Circular accelerators: The Synchrotron
RF frequency can be multiple of revolution frequency

## Slide 40
PS (CERN)
Proton Synchrotron
© CERN Geneva
Examples of different proton and electron synchrotrons at CERN
+ LHC (of course!)
LEAR (CERN)
Low Energy Antiproton Ring
© CERN Geneva
© CERN Geneva
EPA (CERN)
Electron Positron Accumulator
Circular accelerators: The Synchrotron

## Slide 41: The Synchrotron
The synchrotron is a synchronous accelerator since there is a synchronous RF phase for which the energy gain fits the increase of the magnetic field at each turn. That implies the following operating conditions:
Energy gain per turn
Synchronous particle
RF synchronism
(h - harmonic number)
Constant orbit
Variable magnetic field
If v≈c, wr hence wRF remain constant (ultra-relativistic e- )
B
injection
extraction
r
R=C/2π
E
Bending
magnet
bending radius

## Slide 42
Energy ramping by increasing the B field (frequency has to follow v):
Since:
The number of stable synchronous particles is equal to the harmonic number h. They are equally spaced along the circumference.
Each synchronous particle satisfies the relation p=eB. They have the nominal energy and follow the nominal trajectory.
Stable phase φs changes during energy ramping
The Synchrotron – Energy ramping

## Slide 43
During the energy ramping, the RF frequency increases to follow the increase of the revolution frequency :
Since the RF frequency must follow the variation of the B field with the law
Hence: ( using )
This asymptotically tends towards when B becomes large compared to which corresponds to
The Synchrotron – Frequency change

## Slide 44: Dispersion Effects in a Synchrotron
If a particle is slightly shifted in momentum it will have a different orbit and the orbit length is different.
The “momentum compaction factor” is defined as:
If the particle is shifted in momentum it will have also a different velocity. As a result of both effects the revolution frequency changes:
p=particle momentum
R=synchrotron physical radius
fr=revolution frequency
E+E
E
cavity
Circumference
2R

## Slide 45: Momentum Compaction Factor
d
x
The elementary path difference from the two orbits is:
leading to the total change in the circumference:
With ρ=∞ in straight sections we get:
< >m means that the average is considered over the bending magnet only
definition of dispersion Dx

## Slide 46: Dispersion Effects – Revolution Frequency
There are two effects changing the revolution frequency: the orbit length and the velocity of the particle
=0 at the transition energy where both effects cancel
definition of momentum compaction factor

## Slide 47: Phase Stability in a Synchrotron
From the definition of  it is clear that an increase in momentum gives - below transition (η > 0) a higher revolution frequency (increase in velocity dominates) while
- above transition (η < 0) a lower revolution frequency (v  c and longer path) where the momentum compaction (generally > 0) dominates.
Stable synchr. Particle for  < 0
above transition
 > 0
energy gain
late
early

## Slide 48: Crossing Transition
At transition, the velocity change and the path length change with momentum compensate each other. So the revolution frequency there is independent from the momentum deviation.
Crossing transition during acceleration makes the previous stable synchronous phase unstable. The RF system needs to make a rapid change of the RF phase, a ‘phase jump’.
In the PS: γtr is at ~6 GeV
In the SPS: γtr= 22.8, injection at γ=27.7
=> no transition crossing!
In the LHC: γtr is at ~55 GeV, also far below injection energy
Transition crossing not needed in leptons machines, why?

## Slide 49
f2
f2 - The particle is decelerated
- decrease in energy - decrease in revolution frequency
- The particle arrives later – tends toward f0
f1 - The particle B is accelerated
- Below transition, an increase in energy means an increase in revolution frequency
- The particle arrives earlier – tends toward f0
f1
f0
Dynamics: Synchrotron oscillations
Simple case (no accel.): B = const., below transition
The phase of the synchronous particle must therefore be f0 = 0.
B

## Slide 50
t (or )
E
higher energy
late arrival
lower energy
early arrival
Particle B performs a synchrotron oscillation around the synchronous particle A
Plotting this motion in longitudinal phase space gives:
Longitudinal Phase Space Motion

## Slide 51
f1
f0
f2
Phase space picture
Synchrotron oscillations – No acceleration
separatrix
stable region
unstable region

## Slide 52
fs
f
stable region
unstable region
separatrix
The symmetry of the case B = const. is lost
Synchrotron oscillations (with acceleration)
2
1
Case with acceleration B increasing
Phase space picture

## Slide 53
Synchrotron motion in phase space
Remark:
Synchrotron frequency much smaller than betatron frequency.
The restoring force is non-linear.
speed of motion depends on position in phase-space
(here shown for a stationary bucket)

## Slide 54
Bucket area: area enclosed by the separatrix
=> longitudinal Acceptance [eVs]
The area covered by particles is the longitudinal emittance.
DE-f phase space of a stationary bucket (when there is no acceleration)
Dynamics of a particle
Non-linear, conservative oscillator  e.g. pendulum
Particle inside the separatrix:
Particle at the unstable fix-point
Particle outside the separatrix:
Synchrotron motion in phase space

## Slide 55: RF Acceptance versus Synchronous Phase
The areas of stable motion (closed trajectories) are called “BUCKET”.
As the synchronous phase gets closer to 90º the buckets gets smaller.
The number of circulating buckets is equal to “h”.
The phase extension of the bucket is maximum for s =180º (or 0°) which correspond to no acceleration . The RF acceptance increases with the RF voltage.

## Slide 56: Longitudinal Motion with Synchrotron Radiation
Synchrotron radiation energy-loss energy dependant:
During one period of synchrotron oscillation:
when the particle is in the upper half-plane, it loses more energy per turn, its energy gradually reduces
- when the particle is in the lower half-plane, it loses less energy per turn, but receives U0 on the average, so its energy deviation gradually reduces
The phase space trajectory spirals towards the origin (limited by quantum excitations)
=> The synchrotron motion is damped toward an equilibrium bunch length and energy spread.
More details in Andy Wolski’s lecture on ‘Low Emittance Machines’
U
0
=
4
3
π
r
e
m
0
c
2
(
)
3
E
4
ρ
ΔE

## Slide 57: Longitudinal Dynamics in Synchrotrons
“Synchrotron Motion”
The RF acceleration process clearly emphasizes two coupled variables, the energy gained by the particle and the RF phase experienced by the same particle. Since there is a well defined synchronous particle which has always the same phase s, and the nominal energy Es, it is sufficient to follow other particles with respect to that particle. So let’s introduce the following reduced variables:
revolution frequency : fr = fr – frs
particle RF phase :  =  - s
particle momentum : p = p - ps
particle energy : E = E – Es
azimuth angle :  =  - s

## Slide 58: First Energy-Phase Equation
For a given particle with respect to the reference one:
Since:
one gets the 1st order equation:
and
particle ahead arrives earlier
=> smaller RF phase
qs
Dq
R
v

## Slide 59: Second Energy-Phase Equation
The rate of energy gained by a particle is:
The rate of relative energy gain with respect to the reference particle leads to the second energy-phase equation:
deriving and combining
This second order equation is non linear. Moreover the parameters within the bracket are in general slowly varying with time.
We will study some cases in the following…

## Slide 60: Small Amplitude Oscillations
(for small )
with
Let’s assume constant parameters Rs, ps, s and :
Consider now small phase deviations from the reference particle:
and the corresponding linearized motion reduces to a harmonic oscillation:
where s is the synchrotron angular frequency

## Slide 61
Stability is obtained when s is real and so s2 positive:
Stability condition for ϕs
VRF
cos (fs)
acceleration
deceleration
Stable in the region if
 < tr
 < tr
 > tr
 > tr

## Slide 62: Large Amplitude Oscillations
For larger phase (or energy) deviations from the reference the second order differential equation is non-linear:
(s as previously defined)
Multiplying by and integrating gives an invariant of the motion:
which for small amplitudes reduces to:
(the variable is , and s is constant)
Similar equations exist for the second variable : Ed/dt

## Slide 63: Large Amplitude Oscillations (2)
Second value m where the separatrix crosses the horizontal axis:
Equation of the separatrix:
When  reaches -s the force goes to zero and beyond it becomes non restoring. Hence -s is an extreme amplitude for a stable motion which in the
phase space( ) is shown as
closed trajectories.

## Slide 64: Energy Acceptance
From the equation of motion it is seen that reaches an extreme
when , hence corresponding to .
Introducing this value into the equation of the separatrix gives:
That translates into an acceptance in energy:
This “RF acceptance” depends strongly on s and plays an important role for the capture at injection, and the stored beam lifetime.
It’s largest for s=0 and s=π (no acceleration, depending on ).
Need a higher RF voltage for higher acceptance.

## Slide 65: RF Acceptance versus Synchronous Phase
The areas of stable motion (closed trajectories) are called “BUCKET”.
As the synchronous phase gets closer to 90º the buckets gets smaller.
The number of circulating buckets is equal to “h”.
The phase extension of the bucket is maximum for s =180º (or 0°) which correspond to no acceleration . The RF acceptance increases with the RF voltage.

## Slide 66: Stationnary Bucket - Separatrix
This is the case sins=0 (no acceleration) which means s=0 or  . The equation of the separatrix for s=  (above transition) becomes:
Replacing the phase derivative by the (canonical) variable W:
and introducing the expression for s leads to the following equation for the separatrix:
with C=2Rs
W

0

2
Wbk

## Slide 67: Stationnary Bucket (2)
Setting = in the previous equation gives the height of the bucket:
The area of the bucket is:
Since:
one gets:
This results in the maximum energy acceptance:

## Slide 68: Bunch Transfer - Effect of a Mismatch
When you transfer the bunch from one RF system to another, the shape of the phase space and the bunch need to match.
Mismatch example: Injected bunch: short length and large energy spread after 1/4 synchrotron period: longer bunch with a smaller energy spread.
W
W


For larger amplitudes, the angular phase space motion is slower (1/8 period shown below) => can lead to filamentation and emittance growth
stationary bucket
accelerating bucket
W.Pirkl
restoring force is non-linear
W
W



## Slide 69: Effect of a Mismatch (2)
Evolution of an injected beam for the first 100 turns.
For a matched transfer, the emittance does not grow (left).
matched beam
mismatched beam – bunch length

## Slide 70: Effect of a Mismatch (3)
Evolution of an injected beam for the first 100 turns.
For a mismatched transfer, the emittance increases (right).
matched beam
mismatched beam – phase error

## Slide 71: Bunch Matching into a Stationnary Bucket
A particle trajectory inside the separatrix is described by the equation:
W

0

2
Wbk
Wb

m
2-m
s=
The points where the trajectory crosses the axis are symmetric with respect to s=

## Slide 72: Bunch Matching into a Stationnary Bucket (2)
Setting    in the previous formula allows to calculate the bunch height:
or:
This formula shows that for a given bunch energy spread the proper matching of a shorter bunch (m close to , small) will require a bigger RF acceptance, hence a higher voltage
For small oscillation amplitudes the equation of the ellipse reduces to:
Ellipse area gives the longitudinal emittance of

## Slide 73: Bunch Rotation
Phase space motion can be used to make short bunches.
Start with a long bunch and extract or recapture when it’s short.
initial beam

## Slide 74: Capture of a Debunched Beam with Fast Turn-On

## Slide 75: Capture of a Debunched Beam with Adiabatic Turn-On

## Slide 76: Potential Energy Function
The longitudinal motion is produced by a force that can be derived from a scalar potential:
The sum of the potential energy and kinetic energy is constant and by analogy represents the total energy of a non-dissipative system.

## Slide 77: Hamiltonian of Longitudinal Motion
Introducing a new convenient variable, W, leads to the 1st order equations:
The two variables ,W are canonical since these equations of motion can be derived from a Hamiltonian H(,W,t):

## Slide 78
Summary
Cyclotrons/Synchrocylotrons for low energy
Synchrotrons for high energies constant orbit, rising field and frequency
Particles with higher energy have a longer orbit (normally) but a higher velocity
  at low energies (below transition) velocity increase dominates
  at high energies (above transition) velocity almost constant
Particles perform oscillations around synchronous phase
  synchronous phase depending on acceleration
  below or above transition
bucket is the region in phase space for stable oscillations
matching the shape of the bunch to the bucket is important

## Slide 79: Bibliography
M. Conte, W.W. Mac Kay An Introduction to the Physics of particle Accelerators
        (World Scientific, 1991)
P. J. Bryant and K. Johnsen The Principles of Circular Accelerators and Storage Rings
        (Cambridge University Press, 1993)
D. A. Edwards, M. J. Syphers An Introduction to the Physics of High Energy Accelerators
        (J. Wiley & sons, Inc, 1993)
H. Wiedemann Particle Accelerator Physics
(Springer-Verlag, Berlin, 1993)
M. Reiser Theory and Design of Charged Particles Beams
        (J. Wiley & sons, 1994)
A. Chao, M. Tigner Handbook of Accelerator Physics and Engineering
        (World Scientific 1998)
K. Wille The Physics of Particle Accelerators: An Introduction
        (Oxford University Press, 2000)
E.J.N. Wilson An introduction to Particle Accelerators
        (Oxford University Press, 2001)
And CERN Accelerator Schools (CAS) Proceedings
In particular: CERN-2014-009
Advanced Accelerator Physics - CAS

## Slide 80: Acknowledgements
I would like to thank everyone for the material that I have used.
In particular (hope I don’t forget anyone):
- Joël Le Duff (from whom I inherited the course)
- Erk Jensen
- Alessandra Lombardi
- Maurizio Vretenar
- Rende Steerenberg
- Gerald Dugan
- Heiko Damerau
- Werner Pirkl
- Genevieve Tulloue
- Mike Syphers
- Daniel Schulte
- Roberto Corsini
- Roland Garoby