## Slide 1: LONGITUDINAL DYNAMICS
Frank Tecker
based on the course by
Joël Le Duff
Many Thanks!
CAS on Advanced Level Accelerator Physics Course
Trondheim, 18-29 August 2013

## Slide 2: Summary of the 2 lectures:
Acceleration methods
Accelerating structures
Phase Stability + Energy-Phase oscillations (Linac)
Circular accelerators: Cyclotron / Synchrotron
Dispersion Effects in Synchrotron
Longitudinal Phase Space Motion
Stationary Bucket
Injection Matching
Adiabatic Damping
Two more related lectures:
  Linear Accelerators I + II – Maurizio Vretanar
  RF Cavity Design - Erk Jensen

## Slide 3: Main Characteristics of an Accelerator
ACCELERATION is the main job of an accelerator.
It provides kinetic energy to charged particles, hence increasing their momentum.
In order to do so, it is necessary to have an electric field preferably along the direction of the initial momentum (z).
BENDING is generated by a magnetic field perpendicular to the plane of the particle trajectory. The bending radius  obeys to the relation :
FOCUSING is a second way of using a magnetic field, in which the bending effect is used to bring the particles trajectory closer to the axis, hence to increase the beam density.
Newton-Lorentz Force on a charged particle:
2nd term always perpendicular to motion => no acceleration
in practical units:

## Slide 4: Electrostatic Acceleration
Electrostatic Field:
Energy gain: W = e ΔV
Limitation: isolation problems
maximum high voltage (~ 10 MV)
used for first stage of acceleration: particle sources, electron guns
x-ray tubes
750 kV Cockroft-Walton generator at Fermilab (Proton source)
E
DV
vacuum envelope
source

## Slide 5: Methods of Acceleration: Induction
coil
beam
vacuum pipe
iron yoke
Bf
B
Bf
E
R
beam
From Maxwell’s Equations:
The electric field is derived from a scalar potential φ and a vector potential A
The time variation of the magnetic field H generates an electric field E
Example: Betatron
The varying magnetic field is used to guide particles on a circular trajectory as well as for acceleration.
Limited by saturation in iron

## Slide 6: Radio-Frequency (RF) Acceleration
Cylindrical electrodes (drift tubes) separated by gaps and fed by a RF generator, as shown above, lead to an alternating electric field polarity
Synchronism condition L = v T/2
v = particle velocity T = RF period
D.Schulte
Similar for standing wave cavity as shown (with v≈c)
Electrostatic acceleration limited by isolation possibilities => use RF fields
Wideröe-type
structure

## Slide 7: Resonant RF Cavities
Considering RF acceleration, it is obvious that when particles get high velocities the drift spaces get longer and one loses on the efficiency. => The solution consists of using a higher operating frequency.
The power lost by radiation, due to circulating currents on the electrodes, is proportional to the RF frequency. => The solution consists of enclosing the system in a cavity which resonant frequency matches the RF generator frequency.
The electromagnetic power is now constrained in the resonant volume
Each such cavity can be independently powered from the RF generator
Note however that joule losses will occur in the cavity walls (unless made of superconducting materials)

## Slide 8: Some RF Cavity Examples
L = vT/2 (π mode) L = vT (2π mode)
Single Gap Multi-Gap

## Slide 9
Synchronism condition
g
L1
L2
L3
L4
L5
RF generator
Used for protons, ions (50 – 200 MeV, f ~ 200 MHz)
RF acceleration: Alvarez Structure
LINAC 1 (CERN)

## Slide 10: Transit time factor
In the general case, the transit time factor is:
Transit time factor defined as:
0 < Ta < 1
Ta  1 for g  0, smaller ωRF
Important for low velocities (ions)
for
Simple model uniform field:
follows:
The accelerating field varies during the passage of the particle
=> particle does not always see maximum field => effective acceleration smaller

## Slide 11: Disc loaded traveling wave structures
-When particles gets ultra-relativistic (v~c) the drift tubes become very long unless the operating frequency is increased. Late 40’s the development of radar led to high power transmitters (klystrons) at very high frequencies (3 GHz).
-Next came the idea of suppressing the drift tubes using traveling waves. However to get a continuous acceleration the phase velocity of the wave needs to be adjusted to the particle velocity.
solution: slow wave guide with irises ==> iris loaded structure
CLIC Accelerating Structures (30 & 11 GHz)

## Slide 12: The Traveling Wave Case
The particle travels along with the wave, and k represents the wave propagation factor.
wave number
vφ = phase velocity v = particle velocity
If synchronism satisfied:
where Φ0 is the RF phase seen by the particle.
v = vφ and

## Slide 13: Energy Gain
In relativistic dynamics, total energy E and momentum p are linked by
W kinetic energy
Hence:
The rate of energy gain per unit length of acceleration (along z) is then:
and the kinetic energy gained from the field along the z path is:
where V is just a potential.

## Slide 14
normalized velocity
total energy
rest energy
protons
electrons
electrons
protons
Velocity, Energy and Momentum
=> electrons almost reach the speed of light very quickly (few MeV range)
Momentum
normalized velocity
total energy
rest energy

## Slide 15: Summary: Relativity + Energy Gain
RF Acceleration
(neglecting transit time factor)
The field will change during the passage of the particle through the cavity => effective energy gain is lower
Newton-Lorentz Force
Relativistics Dynamics
2nd term always perpendicular to motion => no acceleration

## Slide 16: Common Phase Conventions
For circular accelerators, the origin of time is taken at the zero crossing of the RF voltage with positive slope
Time t= 0 chosen such that:
1
f1
2
f2
For linear accelerators, the origin of time is taken at the positive crest of the RF voltage
3. I will stick to convention 1 in the following to avoid confusion

## Slide 17: Principle of Phase Stability (Linac)
Let’s consider a succession of accelerating gaps, operating in the 2π mode, for which the synchronism condition is fulfilled for a phase s .
is the energy gain in one gap for the particle to reach the next gap with the same RF phase: P1 ,P2, …… are fixed points.
If an energy increase is transferred into a velocity increase => M1 & N1 will move towards P1 => stable M2 & N2 will go away from P2 => unstable (Highly relativistic particles have no significant velocity change)
For a 2π mode, the electric field is the same in all gaps at any given time.

## Slide 18
Longitudinal phase stability means :
The divergence of the field is zero according to Maxwell :
defocusing RF force
External focusing (solenoid, quadrupole) is then necessary
Transverse focusing fields at the entrance and defocusing at the exit of the cavity.
Electrostatic case: Energy gain inside the cavity leads to focusing
RF case: Field increases during passage => transverse defocusing!
A Consequence of Phase Stability

## Slide 19
- Rate of energy gain for the synchronous particle:
- Rate of change of the phase with respect to the synchronous one:
Since:
- Rate of energy gain for a non-synchronous particle, expressed in reduced variables, and :
Energy-phase Oscillations (1)

## Slide 20: Energy-phase Oscillations (2)
one gets:
Combining the two 1st order equations into a 2nd order equation gives:
with
Stable harmonic oscillations imply:
hence:
And since acceleration also means:
You finally get the result for the stable phase range:

## Slide 21
DE, Dp/p
f
Emittance: phase space area including all the particles
NB: if the emittance contour correspond to a possible orbit in phase space, its shape does not change with time (matched beam)
DE, Dp/p
f
acceleration
deceleration
move
backward
move
forward
The particle trajectory in the phase space (Dp/p, f) describes its longitudinal motion.
reference
Longitudinal phase space
The energy – phase oscillations can be drawn in phase space:

## Slide 22
Circular accelerators: Cyclotron
Cyclotron frequency
g increases with the energy  no exact synchronism
if v  c  g  1
Synchronism condition
B = constant
wRF = constant
B
RF generator, wRF
g
Ion source
Extraction electrode
Ions trajectory
Used for protons, ions

## Slide 23
Synchrocyclotron: Same as cyclotron, except a modulation of wRF
B = constant
  g wRF = constant
wRF decreases with time
The condition:
Allows to go beyond the non-relativistic energies
Cyclotron / Synchrocyclotron
TRIUMF 520 MeV cyclotron Vancouver - Canada

## Slide 24
Constant orbit during acceleration
To keep particles on the closed orbit, B should increase with time
w and wRF increase with energy
E
R
RF generator
B
RF cavity
Synchronism condition
h integer,
harmonic number:
number of RF cycles
per revolution
Circular accelerators: The Synchrotron

## Slide 25: The Synchrotron
The synchrotron is a synchronous accelerator since there is a synchronous RF phase for which the energy gain fits the increase of the magnetic field at each turn. That implies the following operating conditions:
Energy gain per turn
Synchronous particle
RF synchronism
(h - harmonic number)
Constant orbit
Variable magnetic field
If v≈c, wr hence wRF remain constant (ultra-relativistic e- )
B
injection
extraction
r
R=C/2π
E
Bending
magnet
bending radius

## Slide 26: The Synchrotron
Energy ramping is simply obtained by varying the B field (frequency follows v):
Since:
The number of stable synchronous particles is equal to the harmonic number h. They are equally spaced along the circumference.
Each synchronous particle satisfies the relation p=eB. They have the nominal energy and follow the nominal trajectory.
Stable phase φs changes during energy ramping

## Slide 27: The Synchrotron
During the energy ramping, the RF frequency increases to follow the increase of the revolution frequency :
Since the RF frequency must follow the variation of the B field with the law
Hence: ( using )
This asymptotically tends towards when B becomes large compared to which corresponds to

## Slide 28: Dispersion Effects in a Synchrotron
If a particle is slightly shifted in momentum it will have a different orbit and the length is different.
The “momentum compaction factor” is defined as:
If the particle is shifted in momentum it will have also a different velocity. As a result of both effects the revolution frequency changes:
p=particle momentum
R=synchrotron physical radius
fr=revolution frequency
E+E
E
cavity
Circumference
2R

## Slide 29: Dispersion Effects in a Synchrotron (2)
d
x
The elementary path difference from the two orbits is:
leading to the total change in the circumference:
With ρ=∞ in straight sections we get:
< >m means that the average is considered over the bending magnet only
definition of dispersion Dx

## Slide 30: Dispersion Effects in a Synchrotron (3)
=0 at the transition energy
definition of momentum compaction factor

## Slide 31: Phase Stability in a Synchrotron
From the definition of  it is clear that an increase in momentum gives - below transition (η > 0) a higher revolution frequency (increase in velocity dominates) while
- above transition (η < 0) a lower revolution frequency (v  c and longer path) where the momentum compaction (generally > 0) dominates.
Stable synchr. Particle for  < 0
above transition
 > 0

## Slide 32: Crossing Transition
At transition, the velocity change and the path length change with momentum compensate each other. So the revolution frequency there is independent from the momentum deviation.
Crossing transition during acceleration makes the previous stable synchronous phase unstable. The RF system needs to make a rapid change of the RF phase, a ‘phase jump’.

## Slide 33
f2
f2 - The particle is decelerated
- decrease in energy - decrease in revolution frequency
- The particle arrives later – tends toward f0
f1 - The particle is accelerated
- Below transition, an increase in energy means an increase in revolution frequency
- The particle arrives earlier – tends toward f0
f1
f0
Synchrotron oscillations
Simple case (no accel.): B = const., below transition
The phase of the synchronous particle must therefore be f0 = 0.

## Slide 34
f1
f0
f2
Phase space picture
Synchrotron oscillations (2)

## Slide 35
fs
f
stable region
unstable region
separatrix
The symmetry of the case B = const. is lost
Synchrotron oscillations (3)
2
1
Case with acceleration B increasing
Phase space picture

## Slide 36: Longitudinal Dynamics in Synchrotrons
It is also often called “synchrotron motion”.
The RF acceleration process clearly emphasizes two coupled variables, the energy gained by the particle and the RF phase experienced by the same particle. Since there is a well defined synchronous particle which has always the same phase s, and the nominal energy Es, it is sufficient to follow other particles with respect to that particle. So let’s introduce the following reduced variables:
revolution frequency : fr = fr – frs
particle RF phase :  =  - s
particle momentum : p = p - ps
particle energy : E = E – Es
azimuth angle :  =  - s

## Slide 37: First Energy-Phase Equation
For a given particle with respect to the reference one:
Since:
one gets:
and
particle ahead arrives earlier
=> smaller RF phase
qs
Dq
R
v

## Slide 38: Second Energy-Phase Equation
The rate of energy gained by a particle is:
The rate of relative energy gain with respect to the reference particle is then:
leads to the second energy-phase equation:
Expanding the left-hand side to first order:

## Slide 39: Equations of Longitudinal Motion
deriving and combining
This second order equation is non linear. Moreover the parameters within the bracket are in general slowly varying with time.
We will study some cases in the following…

## Slide 40: Small Amplitude Oscillations
(for small )
with
Let’s assume constant parameters Rs, ps, s and :
Consider now small phase deviations from the reference particle:
and the corresponding linearized motion reduces to a harmonic oscillation:
where s is the synchrotron angular frequency

## Slide 41
Stability is obtained when s is real and so s2 positive:
Stability condition for ϕs
VRF
cos (fs)
acceleration
deceleration
Stable in the region if
 < tr
 < tr
 > tr
 > tr

## Slide 42: Large Amplitude Oscillations
For larger phase (or energy) deviations from the reference the second order differential equation is non-linear:
(s as previously defined)
Multiplying by and integrating gives an invariant of the motion:
which for small amplitudes reduces to:
(the variable is , and s is constant)
Similar equations exist for the second variable : Ed/dt

## Slide 43: Large Amplitude Oscillations (2)
Second value m where the separatrix crosses the horizontal axis:
Equation of the separatrix:
When  reaches -s the force goes to zero and beyond it becomes non restoring. Hence -s is an extreme amplitude for a stable motion which in the
phase space( ) is shown as
closed trajectories.
Area within this separatrix is called “RF bucket”.

## Slide 44: Energy Acceptance
From the equation of motion it is seen that reaches an extreme
when , hence corresponding to .
Introducing this value into the equation of the separatrix gives:
That translates into an acceptance in energy:
This “RF acceptance” depends strongly on s and plays an important role for the capture at injection, and the stored beam lifetime.

## Slide 45: RF Acceptance versus Synchronous Phase
The areas of stable motion (closed trajectories) are called “BUCKET”.
As the synchronous phase gets closer to 90º the buckets gets smaller.
The number of circulating buckets is equal to “h”.
The phase extension of the bucket is maximum for s =180º (or 0°) which correspond to no acceleration . The RF acceptance increases with the RF voltage.

## Slide 46: Stationnary Bucket - Separatrix
This is the case sins=0 (no acceleration) which means s=0 or  . The equation of the separatrix for s=  (above transition) becomes:
Replacing the phase derivative by the (canonical) variable W:
and introducing the expression for s leads to the following equation for the separatrix:
with C=2Rs
W

0

2
Wbk

## Slide 47: Stationnary Bucket (2)
Setting = in the previous equation gives the height of the bucket:
The area of the bucket is:
Since:
one gets:
This results in the maximum energy acceptance:

## Slide 48: Effect of a Mismatch
Injected bunch: short length and large energy spread after 1/4 synchrotron period: longer bunch with a smaller energy spread.
W
W


For larger amplitudes, the angular phase space motion is slower (1/8 period shown below) => can lead to filamentation and emittance growth
stationary bucket
accelerating bucket
W.Pirkl

## Slide 49: Bunch Matching into a Stationnary Bucket
A particle trajectory inside the separatrix is described by the equation:
W

0

2
Wbk
Wb

m
2-m
s=
The points where the trajectory crosses the axis are symmetric with respect to s=

## Slide 50: Bunch Matching into a Stationnary Bucket (2)
Setting    in the previous formula allows to calculate the bunch height:
or:
This formula shows that for a given bunch energy spread the proper matching of a shorter bunch (m close to , small) will require a bigger RF acceptance, hence a higher voltage
For small oscillation amplitudes the equation of the ellipse reduces to:
Ellipse area is called longitudinal emittance

## Slide 51: Capture of a Debunched Beam with Fast Turn-On

## Slide 52: Capture of a Debunched Beam with Adiabatic Turn-On

## Slide 53: Potential Energy Function
The longitudinal motion is produced by a force that can be derived from a scalar potential:
The sum of the potential energy and kinetic energy is constant and by analogy represents the total energy of a non-dissipative system.

## Slide 54: Hamiltonian of Longitudinal Motion
Introducing a new convenient variable, W, leads to the 1st order equations:
The two variables ,W are canonical since these equations of motion can be derived from a Hamiltonian H(,W,t):

## Slide 55: Adiabatic Damping
Though there are many physical processes that can damp the longitudinal oscillation amplitudes, one is directly generated by the acceleration process itself. It will happen in the synchrotron, even ultra-relativistic, when ramping the energy but not in the ultra-relativistic electron linac which does not show any oscillation.
As a matter of fact, when Es varies with time, one needs to be more careful in combining the two first order energy-phase equations in one second order equation:
The damping coefficient is proportional to the rate of energy variation and from the definition of s one has:

## Slide 56: Adiabatic Damping (2)
So far it was assumed that parameters related to the acceleration process were constant. Let’s consider now that they vary slowly with respect to the period of longitudinal oscillation (adiabaticity).
For small amplitude oscillations the hamiltonian reduces to:
with
Under adiabatic conditions the Boltzman-Ehrenfest theorem states that the action integral remains constant:
(W,  are canonical variables)
Since:
the action integral becomes:

## Slide 57: Adiabatic Damping (3)
leads to:
Previous integral over one period:
From the quadratic form of the hamiltonian one gets the relation:
Finally under adiabatic conditions the long term evolution of the oscillation amplitudes is shown to be:

## Slide 58: Bibliography
M. Conte, W.W. Mac Kay An Introduction to the Physics of particle Accelerators
        (World Scientific, 1991)
P. J. Bryant and K. Johnsen The Principles of Circular Accelerators and Storage Rings
        (Cambridge University Press, 1993)
D. A. Edwards, M. J. Syphers An Introduction to the Physics of High Energy Accelerators
        (J. Wiley & sons, Inc, 1993)
H. Wiedemann Particle Accelerator Physics
(Springer-Verlag, Berlin, 1993)
M. Reiser Theory and Design of Charged Particles Beams
        (J. Wiley & sons, 1994)
A. Chao, M. Tigner Handbook of Accelerator Physics and Engineering
        (World Scientific 1998)
K. Wille The Physics of Particle Accelerators: An Introduction
        (Oxford University Press, 2000)
E.J.N. Wilson An introduction to Particle Accelerators
        (Oxford University Press, 2001)
And CERN Accelerator Schools (CAS) Proceedings